TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

Advanced Multibus Architecture With Three Separate 16-Bit Data Memory Buses and One Program Memory Bus

40-Bit Arithmetic Logic Unit (ALU) Including a 40-Bit Barrel Shifter and Two Independent 40-Bit Accumulators

17-x 17-Bit Parallel Multiplier Coupled to a 40-Bit Dedicated Adder for Non-Pipelined Single-Cycle Multiply/Accumulate (MAC) Operation

Compare, Select, and Store Unit (CSSU) for the Add/Compare Selection of the Viterbi Operator

Exponent Encoder to Compute an Exponent Value of a 40-Bit Accumulator Value in a Single Cycle

Two Address Generators With Eight Auxiliary Registers and Two Auxiliary Register Arithmetic Units (ARAUs)

Data Bus With a Bus Holder Feature

Address Bus With a Bus Holder Feature ('548 and '549 Only)

Extended Addressing Mode for 8M x 16-Bit Maximum Addressable External Program Space ('548 and '549 Only)

192K x 16-Bit Maximum Addressable Memory Space (64K Words Program, 64K Words Data, and 64K Words I/O)

On-Chip ROM with Some Configurable to Program/Data Memory

Dual-Access On-Chip RAM Single-Access On-Chip RAM ('548/'549)

Single-Instruction Repeat and Block-Repeat Operations for Program Code

Block-Memory-Move Instructions for Better Program and Data Management

Instructions With a 32-Bit Long Word Operand

Instructions With Two- or Three-Operand Reads

Arithmetic Instructions With Parallel Store and Parallel Load

Conditional Store Instructions

Fast Return From Interrupt

On-Chip Peripherals

- Software-Programmable Wait-State
Generator and Programmable Bank
Switching

- On-Chip Phase-Locked Loop (PLL) Clock
Generator With Internal Oscillator or
External Clock Source

- Full-Duplex Serial Port to Support 8- or
16-Bit Transfers ('541, 'LC545, and
'LC546 Only)

- Time-Division Multiplexed (TDM) Serial
Port ('542, '543, '548, and '549 Only)

- Buffered Serial Port (BSP) ('542, '543,
'LC545, 'LC546, '548, and '549 Only)

- 8-Bit Parallel Host-Port Interface (HPI)
('542, 'LC545, '548, and '549)

- One 16-Bit Timer

- External-Input/Output (XIO) Off Control
to Disable the External Data Bus,
Address Bus and Control Signals

Power Consumption Control With IDLE1, IDLE2, and IDLE3 Instructions With Power-Down Modes

CLKOUT Off Control to Disable CLKOUT

On-Chip Scan-Based Emulation Logic, IEEE Std 1149.1t (JTAG) Boundary Scan Logic

25-ns Single-Cycle Fixed-Point Instruction Execution Time [40 MIPS] for5-V Power Supply ('C541 and 'C542 Only)

20-ns and 25-ns Single-Cycle Fixed-Point Instruction Execution Time (50 MIPS and 40 MIPS) for 3.3-V Power Supply ('LC54x)

15-ns Single-Cycle Fixed-Point Instruction Execution Time (66 MIPS) for 3.3-V Power Supply ('LC54xA, '548, 'LC549)

12.5-ns Single-Cycle Fixed-Point Instruction Execution Time (80 MIPS) for 3.3-V Power Supply ('LC548, 'LC549)

10-ns and 8.3-ns Single-Cycle Fixed-Point Instruction Execution Time (100 and 120 MIPS) for 3.3-V Power Supply (2.5-V Core) ('VC549)

Please be aware that an important notice concerning availability, standard warranty, and use in critical applications of Texas Instruments semiconductor products and disclaimers thereto appears at the end of this data sheet.

t IEEE Standard 1149.1-1990 Standard-Test-Access Port and Boundary Scan Architecture.

^ Texas Instruments

>f pul

Products conform to specifications per the terms of Texas Instruments standard warranty. Production processing does not necessarily include testing of all parameters.

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

Copyright © 1999, Texas Instruments Incorporated

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

description

The TMS320C54x, TMS320LC54x, and TMS320VC54x fixed-point, digital signal processor (DSP) families (hereafter referred to as the '54x unless otherwise specified) are based on an advanced modified Harvard architecture that has one program memory bus and three data memory buses. These processors also provide an arithmetic logic unit (ALU) that has a high degree of parallelism, application-specific hardware logic, on-chip memory, and additional on-chip peripherals. These DSP families also provide a highly specialized instruction set, which is the basis of the operational flexibility and speed of these DSPs.

Separate program and data spaces allow simultaneous access to program instructions and data, providing the high degree of parallelism. Two reads and one write operation can be performed in a single cycle. Instructions with parallel store and application-specific instructions can fully utilize this architecture. In addition, data can be transferred between data and program spaces. Such parallelism supports a powerful set of arithmetic, logic, and bit-manipulation operations that can all be performed in a single machine cycle. In addition, the 'C54x, 'LC54x, and VC54x versions include the control mechanisms to manage interrupts, repeated operations, and function calls.

Table 1 provides an overview of the '54x generation of DSPs. The table shows significant features of each device including the capacity of on-chip RAM and ROM memories, the peripherals, the execution time of one machine cycle, and the type of package with its total pin count.

Table 1. Characteristics of the '54x Processors

| DSP TYPE | NOMINAL VOLTAGE (V) | ON-CHIP MEMORY | PERIPHERALS | CYCLE TIME (ns) | PACKAGE TYPE |
| --- | --- | --- | --- | --- | --- |
|  |  | RAMT (Word) | ROM (Word) | SERIAL PORT | TIMER | HPI |  |  |
| TMS320C541 | 5.0 | 5K | 28 Kt | 2§ | 1 | No | 25 | 100-pin TQFP |
| TMS320LC541 | 3.3 | 5K | 28 Kt | 2§ | 1 | No | 20/25 | 100-pin TQFP |
| TMS320LC541Bn | 3.3 | 5K | 28 Kt | 2§ | 1 | No | 20/25 | 100-pin TQFP |
| TMS320C542 | 5.0 | 10K | 2K | 2U | 1 | Yes | 25 | 144-pin TQFP |
| TMS320LC542 | 3.3 | 10K | 2K | 2H | 1 | Yes | 20/25 | 128-pin TQFP/144-pin TQFP |
| TMS320LC543 | 3.3 | 10K | 2K | 2H | 1 | No | 20/25 | 100-pin TQFP |
| TMS320LC545 | 3.3 | 6K | 48 K# | 2ll | 1 | Yes | 20/25 | 128-pin TQFP |
| TMS320LC545AQ | 3.3 | 6K | 48 K# | 2ll | 1 | Yes | 15/20/25 | 128-pin TQFP |
| TMS320LC545BQ | 3.3 | 6K | 48 K# | 2ll | 1 | Yes | 15/20/25 | 128-pin TQFP |
| TMS320LC546 | 3.3 | 6K | 48 K# | 2ll | 1 | No | 20/25 | 100-pin TQFP |
| TMS320LC546AQ | 3.3 | 6K | 48 K# | 2ll | 1 | No | 15/20/25 | 100-pin TQFP |
| TMS320LC546BQ | 3.3 | 6K | 48 K# | 2ll | 1 | No | 15/20/25 | 100-pin TQFP |
| TMS320LC548Q | 3.3 | 32K | 2K | 3A | 1 | Yes | 12.5/15/20 | 144-pin TQFP/144-pin BGA |
| TMS320LC549Q | 3.3 | 32K | 16K | 3A | 1 | Yes | 12.5/15 | 144-pin TQFP/144-pin BGA |
| TMS320VC549Q | 3.3 (2.5 core) | 32K | 16K | 3A | 1 | Yes | 8.3/10/12.5 | 144-pin TQFP/144-pin BGA |

Legend:

TQFP = Thin Quad Flatpack

BGA = MicroStar BGA™ (Ball Grid Array)

t The dual-access RAM (single access RAM on '548 and '549 devices) can be configured as data memory or program/data memory.

t For 'C541 /'LC541, 8K words of ROM can be configured as program memory or program/data memory.

§ Two standard (general-purpose) serial ports

11 One TDM and one BSP

# For 'LC545/'LC546, 16K words of ROM can be configured as program memory or program/data memory.

|| One standard and one BSP

AOne TDM and two BSPs

□ Refer to separate data sheet for electrical specifications.

MicroStar BGA is a trademark of Texas Instruments Incorporated.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

TMS320C541, TMS320LC541

PZ PACKAGEt

(TOP VIEW)

vss C

A10

A11

A12

A13

A14

A15

CVDD

VSS

VSS C

CVDD  C

READY

PS

DS

IS

R/W

MSTRB

IOSTRB MSC XF  C

HOLDA

Faq

HOLD

bTo c

MP/MC

c

C C

nn

CO   CM

Q (j) (j) Q io "3-  co cm O >  > O    QQQQ

CO

nnnnnnnnnnnnnnnnnnnnnnn

CO

roOT-CNco^rmcD cNcococococOcoco

D5

D4

D3

D2

D1

D0

RS

X2/CLKIN

X1

CLKOUT

VSS

CVDD

VSS

TMS

TCK

TRST

TDI

TDO

EMU1/OFF

EMU0

TOUT

CNT

CLKMD3

CLKMD2

CLKMD1

|O It- |CN   |CO    Q  W Z   Z   Z    Z    Q  ™

oo	        oo    u	"	°

t DVqq is the power supply for the I/O pins while CVqq is the power supply for the core CPU, and Vss is the ground for both the I/O pins and the core CPU.

The '54x signal descriptions table lists each terminal name, function, and operating mode(s) for the TMS320C541PZ/TMS320LC541PZ (100-pin TQFP packages).

Forthe 'C541/'LC541 (100-pin packages), no letter in front of CLKRn, FSRn, DRn, CLKXn, FSXn, and DXn pin names denotes standard serial port (where n = 0 or 1 port).

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

Q ^ Z O <

TMS320C542/TMS320LC542

PGE PACKAGEtt

(TOP VIEW)

Q CM

Q <G

Q Q

NC [

vSs[

DVDD[ A10 [ HD7 [ A11 [ A12 [ A13 [ A14 [ A15 [

CVDD[ HAS [

vSs[ vSs[

CVDD[

HCS_[

HR/W[

READY [

PS[

DS [

IS_[

R/W[

MSTRB[

IOSTRB [

MSC [

XF[

HOLDA [

IAQ [

HOLD [

BIO [

MP/MC[

DVDD[

vSs[

NC [

1 O

2

3

4

5

6

7

8

9

10

11

12

13

14

15

16

17

18

19

20

21

22

23

24

25

26

27

28

29

30

31

32

33

34

35

36

108 107 106 105 104 103 102 101 100 99 98 97 96 95 94 93 92 91 90 89 88 87 86 85 84 83 82 81 80 79 78 77 76 75 74 73

vss

NC

vss ] dvdd

] D5

D4

D3 ] D2

D1 ] D0

RS

] X2/CLKIN ] X1 ] HD3 ] CLKOUT

VSS ] HPIENA

CVDD

VSS ] TMS ] TCK ] TRST ] TDI ] TDO

] EMU1/OFF ] EMU0 ] TOUT

HD2 ] CNT ] CLKMD3 ] CLKMD2 ] CLKMD1

VSS

dvdd

] NC VSS

ipЈP

100

co z

O

I

a:

o

i

>-	Q COO X X

Q	QloDQQ

a:	> > i in h

■I	Q

X

co

o m

P  Dj  CO O CO

DSBZffl

t NC = No connection

t DVopisthe powersupply for the I/O pins while CVopisthe powersupply for the core CPU, and Vss is the ground for both the I/O pins and the

core CPU.

The '54x signal descriptions table lists each terminal name, function, and operating mode(s) for the TMS320C542PGE/'LC542PGE (144-pin TQFP packages).

For the 'C542/'LC542 (144-pin TQFP packages), the letter B in front of CLKR, FSR, DR, CLKX, FSX, and DX pin names denotes buffered serial port (BSP). The letter T in front of CLKR, FSR, DR, CLKX, FSX, and DX pin names denotes time-division multiplexed (TDM) serial port.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

TMS320LC542

PBK PACKAGEt

(TOP VIEW)

Q  Q

t- o >

< < Q

Q Q

O

s

Q

I

>   if) Q>

I >

DVpp A10 HD7 A11 A12 A13 A14 A15

CVpp HAS

CVppC

HCS_C

HR/Wc

READY C

PS C

DS C

IS_C

R/WC

MSTRB C

IOSTRB cz

MSC[

XF[

HOLDA [ IAQ [

HOLD[

BJO [

MP/MC[

DVpp [

I>OIQQQIQQQQQQQ

nn nnn nnnnnnnnnnnnnnnnnnnnnnnnn

| /128127126125124123122121120119 118117116115114113112 111110109108107106105104103102101100 99 98 | 97 " |
| --- | --- |
| 1 | 96 |
| : o | 95 94 |
| 4 | 93 |
| 5 | 92 |
| 6 | 91 |
| 7 | 90 |
| 8 | 89 |
| 9 | 88 |
| 10 | 87 |
| 11 | 86 |
| 12 | 85 |
| 13 | 84 |
| 14 | 83 |
| 15 | 82 |
| 16 | 81 |
| 17 | 80 |
| 18 | 79 |
| 19 | 78 |
| 20 | 77 |
| 21 | 76 |
| 22 | 75 |
| 23 | 74 |
| 24 | 73 |
| 25 | 72 |
| 26 | 71 |
| 27 | 70 |
| 28 | 69 |
| 29 | 68 |
| 30 | 67 |
| 31 | 66 |
| 32 | 65 |
| 33 34 35 36 37 38 39 40 41 42 43 44 45 46 47 48 49 50 51 52 53 54 55 56 57 58 59 60 61 62 63 | 64 |

o

uuuuuuuuuuuuuuuuuuuuuuuuuuuuuuuu

m a

~ o

Q V) O

;- f)

IACK HBI

X X

- a a I m H

t

If)

^   O O O    [Q h-

] DVpp

D5

] D4

] D3

D2

D1

] D0

I RS

X2/CLKIN

X1

I HD3

I CLKOUT

1VSS I HPIENA iCVpp

I VSS

TMS

TCK

TRST

TDI

TDO

I EMU1/OFF

I EMU0

I TOUT

I HD2

CNT

I CLKMD3

I CLKMD2

I CLKMD1

I VSS I DVpp

t DVqq is the power supply forthe I/O pins while CVqd is the power supply forthe core CPU, and Vss is the ground for both the I/O pins and the core CPU.

The '54x signal descriptions table lists each terminal name, function, and operating mode(s) for the TMS320LC542PBK (128-pin TQFP package).

Forthe 'LC542 (128-pin TQFP package), the letter B in front of CLKR, FSR, DR, CLKX, FSX, and DX pin names denotes buffered serial port (BSP). The letter T in front of CLKR, FSR, DR, CLKX, FSX, and DX pin names denotes time-division multiplexed (TDM) serial port.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

TMS320LC543

PZ PACKAGEt

(TOP VIEW)

<C<C<C<C<C<C<C<C<C<CO>>O   QQQQ   QQQQQQQ

nnnnnnnnnnnnnnnnnnnnnnnnn

D5

D4

D3

D2

D1

D0

RS

X2/CLKIN

X1

CLKOUT

VSS

CVDD

VSS

TMS

TCK

TRST

TDI

TDO

EMU1/OFF

EMU0

TOUT

CNT

CLKMD3

CLKMD2

CLKMD1

LJUULJUULJUULJUULJ

U U L

Q  « Q   (0

> >

Q

| vss | c | 1 |
| --- | --- | --- |
| A10 | c | 2 |
| A11 | c | 3 |
| A12 | c | 4 |
| A13 | c | 5 |
| A14 | c | 6 |
| A15 | c | 7 |
| cvDD | c | 8 |
| vss | c | 9 |
| vss | c | 10 |
| cvDD | c | 11 |
| READY | c | 12 |
| PS | c | 13 |
| DS | c | 14 |
| r§ | c | 15 |
| R/W | c | 16 |
| MSTRB | c | 17 |
| IOSTRB | c | 18 |
| MSC | C | 19 |
| XF | c | 20 |
| HOLDA | c | 21 |
| Iaq | c | 22 |
| HOLD | c | 23 |
| HO | c | 24 |
| MP/MC | r | 25 |

LJ LJ cn co  q w

—ju_u_ opmi-

t DVopisthe powersupply for the I/O pins while CVopisthe powersupply for the core CPU, and Vss is the ground for both the I/O pins and the

core CPU.

The '54x signal descriptions table lists each terminal name, function, and operating mode(s) for the TMS320LC543PZ (100-pin TQFP package).

For the 'LC543 (100-pin TQFP package), the letter B in front of CLKR, FSR, DR, CLKX, FSX, and DX denotes buffered serial port (BSP). The letter T in front of CLKR, FSR, DR, CLKX, FSX, and DX denotes time-division multiplexed (TDM) serial port.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

TMS320LC545

PBK PACKAGEt

(TOP VIEW)

Q Q

O

Q  Q

t- o >

< < Q

co co I >

Q

cm ■■- o	Q co

Q

I

t-t-t-ocor^(D> co QQQQQQQQ>

I Q Q Q I

nn nnn nnnnnnnnnnnnnnnnnnnnnnnnn

128127126125124123122121120119 118117116 115114113112 111110109108107106105104103102101100 99 98 97

DVpp A10 HD7 A11 A12 A13 A14 A15

CVpp HAS

CVppC

HCS_C

HR/Wc

READY C

PS C

DS C

IS_C

R/WC

MSTRB C

IOSTRB cz

MSC[

XF[

HOLDA [ IAQ [

HOLD[

BJO [

MP/MC[

DVpp [

o

| 96 | HI Vss |
| --- | --- |
| 95 | IH DVpp |
| 94 | ZUD5 |
| 93 | zu D4 |
| 92 | zu D3 |
| 91 | ZUD2 |
| 90 | —I D1 |
| 89 | ZU D0 |
| 88 | zu rs |
| 87 | IZIX2/CLKIN |
| 86 | i X1 |
| 85 | ZU HD3 |
| 84 | HI CLKOUT |
| 83 | =IVSS |
| 82 | HI HPIENA |
| 81 | =lCVpp |
| 80 | =ivss |
| 79 | ZIlTMS |
| 78 | ZIlTCK |
| 77 | ZIlTRST |
| 76 | HlTDI |
| 75 | ZIlTDO |
| 74 | ZU EMU1/OFF |
| 73 | ZU EMU0 |
| 72 | ZUTOUT |
| 71 | ZU HD2 |
| 70 | ZUCNT |
| 69 | ZU CLKMD3 |
| 68 | ZU CLKMD2 |
| 67 | ZU CLKMD1 |
| 66 | ^vss |
| 65 | =lDVpp |

33 34 35 36 37 38 39 40 41 42 43 44 45 46 47 48 49 50 51 52 53 54 55 56 57 58 59 60 61 62 63 64

uuuuuuuuuuuuuuuuuuuuuuuuuuuuuuuu

CO O

co Q

Q X	X	>-	Q

Q CO	CO	Q	Q   -.

> u-	u-	a:	> >

o to	x	q

| IACK HBIL | IIAIN | INTO | INT1 | INT2 |
| --- | --- | --- | --- | --- |

Ј9

t DVqq is the power supply forthe I/O pins while CVqd is the power supply forthe core CPU, and Vss is the ground for both the I/O pins and the core CPU.

The '54x signal descriptions table lists each terminal name, function, and operating mode(s) forthe forthe TMS320LC545PBK (128-pin TQFP package).

Forthe 'LC545 (128-pin TQFP package), the letter B in front of CLKR, FSR, DR, CLKX, FSX, and DX pin names denotes buffered serial port (BSP). No letter in front of CLKR, FSR, DR, CLKX, FSX, and DX pin names denotes standard serial port.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

|  |  |  |  |  |  |  |  | TMS320LC546 |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | PZ PACKAGEt |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  | (TOP VIEW) |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  | Q |  |  | Q |  |  |  |
|  |  |  |  |  |  |  |  |  |  | o | Q co !> |  |  |  |
|  |  |  | < | < | < | < | <<<<<< | >>>O QQQQ | Q | QQQQ | Q Q |  |  |  |
|  |  |  | n | n | n | n | n n n n n n | nnnnnnnn | ~¦ | i n n n | n n |  |  |  |
| vss | c | 1 | 100 |  |  | & | S 8 S 8 g 5 | gggfeSSSS | s |  | [^ f2 | 75 | 3 | D5 |
| A10 | n | 2 |  |  |  |  |  |  |  |  |  | 74 | 3 | D4 |
| A11 | c | 3 |  |  |  |  |  |  |  |  |  | 73 | 3 | D3 |
| A12 | c | 4 |  |  |  |  |  |  |  |  |  | 72 | 3 | D2 |
| A13 | c | 5 |  |  |  |  |  |  |  |  |  | 71 | 3 | D1 |
| A14 | c | 6 |  |  |  |  |  |  |  |  |  | 70 | 3 | D0 |
| A15 | c | 7 |  |  |  |  |  |  |  |  |  | 69 | 3 | RS |
| cvDD | c | 8 |  |  |  |  |  |  |  |  |  | 68 | 3 | X2/CLKIN |
| vss | c | 9 |  |  |  |  |  |  |  |  |  | 67 | 3 | X1 |
| vss | c | 10 |  |  |  |  |  |  |  |  |  | 66 | 3 | CLKOUT |
| cvDD | c | 11 |  |  |  |  |  |  |  |  |  | 65 | 3 | vss |
| READY | c | 12 |  |  |  |  |  |  |  |  |  | 64 | 3 | cvDD |
| PS | c | 13 |  |  |  |  |  |  |  |  |  | 63 | 3 | vss |
| DS | n | 14 |  |  |  |  |  |  |  |  |  | 62 | J | TMS |
| r§ | c | 15 |  |  |  |  |  |  |  |  |  | 61 | 3 | TCK |
| R/W | L" | 16 |  |  |  |  |  |  |  |  |  | 60 | 3 | TRST |
| MSTRB | c | 17 |  |  |  |  |  |  |  |  |  | 59 | 3 | TDI |
| OSTRB |  | 18 |  |  |  |  |  |  |  |  |  | 58 | 3 | TDO |
| MSC | C | 19 |  |  |  |  |  |  |  |  |  | 57 | 3 | EMU1/OFF |
| XF | c | 20 |  |  |  |  |  |  |  |  |  | 56 | 3 | EMU0 |
| HOLDA | c | 21 |  |  |  |  |  |  |  |  |  | 55 | 3 | TOUT |
| Iaq | c | 22 |  |  |  |  |  |  |  |  |  | 54 | 3 | CNT |
| HOLD | c | 23 |  |  |  |  |  |  |  |  |  | 53 | 3 | CLKMD3 |
| HO | c | 24 |  |  |  |  |  |  |  |  |  | 52 | 3 | CLKMD2 |
| MP/MC | n | 25 |  |  |  |  |  |  |  |  |  | 51 | 3 | CLKMD1 |
|  |  |  |  | Si |  |  |  |  |  | "?^" | § S | / |  |  |
|  |  |  | u | u | u | u | u u u u u u | LJUULJUULJU | J | _l U U U | u u |  |  |  |
|  |  |  |  | a: | a: | a: | ce ce ce X X co | Q X X Q co X X |  | — | O |  | CM | CO | Q CO |  |  |  |
|  |  |  |  | _i |  | CL | CO Q Q *. X- CO CL CQ —' —' > | Q CO CO Q CO Q Q > LL LL > > CQ | O < | z | 1— ~Z. | 1 | 1— |  | >> |  |  |  |
|  |  |  |  | o | o | CQ | o o | O CQ Q |  |  |  |  |  |  |  |  |  |  |

t DVpDisthe powersupply forthe I/O pins while CVopisthe powersupply forthe core CPU, and Vss is the ground for both the I/O pins and the

core CPU.

The '54x signal descriptions table lists each terminal name, function, and operating mode(s) forthe forthe TMS320LC546PZ (100-pin TQFP package).

Forthe 'LC546 (100-pin TQFP package), the letter B in front of CLKR, FSR, DR, FSX, and DX denotes buffered serial port (BSP). No letter in front of CLKR, FSR, DR, FSX, and DX denotes standard serial port.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

TMS320LC548, TMS320LC549, and TMS320VC549

PGE PACKAGEtt

(TOP VIEW)

Q

O >

<Q

] A18 ] A17

VSS ] A16 ] D5 ] D4 ] D3 ] D2 ] D1 ] D0 ] RS

] X2/CLKIN ] X1 ] HD3 ] CLKOUT

VSS

] HPIENA  CVDD

VSS ] TMS ] TCK ] TRST ] TDI ] TDO

] EMU1/OFF ] EMU0 ] TOUT ] HD2 ] TEST1 ] CLKMD3 ] CLKMD2 ] CLKMD1

VSS

DVDD ] BDX1 ] BFSX1

A22 [

vSs[

DVDD[ A10 [ HD7 [ A11 [ A12 [ A13 [ A14 [ A15 [

CVDD[ HAS [

CVDD[ HCS_[ HR/W[ READY [ PS[ D_S IS_

R/W[

MSTRB[

IOSTRB [

MSC [

XF[

HOLDA [

IAQ [

HOLD [

BIO [

MP/MC[

DVDD[

vsst

BDR1 [ BFSR1 [

Q Q <n

>   05

q m

Q <n

CD >   05

Q Q >

CM f

< <

Q

I>OIQQQIQQQ

| 1 O | 108 |
| --- | --- |
| 2 | 107 |
| 3 | 106 |
| 4 | 105 |
| 5 | 104 |
| 6 | 103 |
| 7 | 102 |
| 8 | 101 |
| 9 | 100 |
| 10 | 99 |
| 11 | 98 |
| 12 | 97 |
| 13 | 96 |
| 14 | 95 |
| 15 | 94 |
| 16 | 93 |
| 17 | 92 |
| 18 | 91 |
| 19 | 90 |
| 20 | 89 |
| 21 | 88 |
| 22 | 87 |
| 23 | 86 |
| 24 | 85 |
| 25 | 84 |
| 26 | 83 |
| 27 | 82 |
| 28 | 81 |
| 29 | 80 |
| 30 | 79 |
| 31 | 78 |
| 32 | 77 |
| 33 | 76 |
| 34 | 75 |
| 35 | 74 |
| 36 | 73 |

<n *- g

*- a: p x c/3

O     Oh-

X

| IACK HBIL | IIAIN | INTO | INT1 | INT2 |
| --- | --- | --- | --- | --- |

h qQ

O

CD

t NC = No connection

t DVqq is the power supply for the I/O pins while CVqq is the power supply for the core CPU, and Vss is tne ground for both the I/O pins and the

core CPU.

The '54x signal descriptions table lists each terminal name, function, and operating mode(s) for the TMS320LC548PGE (144-pin TQFP package).

For the 'LC548, 'LC549 and 'VC549 (144-pin TQFP package), the letter B in front of CLKRn, FSRn, DRn, CLKXn, FSXn, and DXn pin names denotes buffered serial port (BSP), where n = 0 or 1 port. The letter T in front of CLKR, FSR, DR, CLKX, FSX, and DX pin names denotes time-division multiplexed (TDM) serial port.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

| TMS320LC548, TMS320LC549," | rMS320VC549 |  |
| --- | --- | --- |
|  |  |  |  | GGU | PACKAGE |  |  |  |  |  |
|  |  |  |  | (BOTTOM VIEW) |  |  |  |  |  |
| 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |  |
|  |  |  |  |  |  |  |  |  |  |  |  | \ |  |
| 0 | 0 | 0 | 0 | 0 | o | o | o | 0 | o | o | o | o | A |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | B |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | C |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | D |
| 0 | 0 | 0 | 0 |  |  |  |  |  | 0 | 0 | 0 | 0 | E |
| 0 | 0 | 0 | 0 |  |  |  |  |  | 0 | 0 | 0 | 0 | F |
| 0 | 0 | 0 | 0 |  |  |  |  |  | 0 | 0 | 0 | 0 | G |
| 0 | 0 | 0 | 0 |  |  |  |  |  | o | o | o | o | H |
| 0 | 0 | 0 | 0 |  |  |  |  |  | 0 | 0 | 0 | 0 | J |
| 0 | 0 | 0 | 0 | 0 | o | o | o | 0 | o | o | o | o | K |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | L |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | M |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | N |

The pin assignments table to follow lists each signal quadrant and BGA ball pin numberforthe TMS320LC548, TMS320LC549, and TMS320VC549 (144-pin BGA package).

The '54x signal descriptions table lists each terminal name, function, and operating mode(s) for the TMS320LC548GGU, TMS320LC549GGU, and TMS320VC549GGU.

10

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

| Pin Assignments for the TMS320LC548GGU, TMS320LC549GGU, and TMS320VC549GGU (144-Pin BGA Package)t |
| --- |
| SIGNAL QUADRANT 1 | BGA BALL # | SIGNAL QUADRANT 2 | BGA BALL # | SIGNAL QUADRANT 3 | BGA BALL # | SIGNAL QUADRANT 4 | BGA BALL # |
| vss | A1 | BFSX1 | N13 | vss | N1 | A19 | A13 |
| A22 | B1 | BDX1 | M13 | BCLKR1 | N2 | A20 | A12 |
| vss | C2 | DVDD | L12 | HCNTL0 | M3 | vss | B11 |
| DVDD | C1 | vss | L13 | vss | N3 | DVDD | A11 |
| A10 | D4 | CLKMD1 | K10 | BCLKR0 | K4 | D6 | D10 |
| HD7 | D3 | CLKMD2 | K11 | TCLKR | L4 | D7 | C10 |
| A11 | D2 | CLKMD3 | K12 | BFSR0 | M4 | D8 | B10 |
| A12 | D1 | TEST1 | K13 | TFSR/TADD | N4 | D9 | A10 |
| A13 | E4 | HD2 | J10 | BDR0 | K5 | D10 | D9 |
| A14 | E3 | TOUT | J11 | HCNTL1 | L5 | D11 | C9 |
| A15 | E2 | EMU0 | J12 | TDR | M5 | D12 | B9 |
| cvDD | E1 | EMU1/OFF | J13 | BCLKX0 | N5 | HD4 | A9 |
| HAS | F4 | TDO | H10 | TCLKX | K6 | D13 | D8 |
| vss | F3 | TDI | H11 | vss | L6 | D14 | C8 |
| vss | F2 | TRST | H12 | HINT | M6 | D15 | B8 |
| cvDD | F1 | TCK | H13 | CVDD | N6 | HD5 | A8 |
| HCS | G2 | TMS | G12 | BFSX0 | M7 | cvDD | B7 |
| HR/W | G1 | vss | G13 | TFSX/TFRM | N7 | vss | A7 |
| READY | G3 | cvDD | G11 | HRDY | L7 | HDS1 | C7 |
| PS | G4 | HPIENA | G10 | DVDD | K7 | vss | D7 |
| DS | H1 | vss | F13 | vss | N8 | HDS2 | A6 |
| IS | H2 | CLKOUT | F12 | HD0 | M8 | DVDD | B6 |
| R/W | H3 | HD3 | F11 | BDX0 | L8 | A0 | C6 |
| MSTRB | H4 | X1 | F10 | TDX | K8 | A1 | D6 |
| IOSTRB | J1 | X2/CLKIN | E13 | IACK | N9 | A2 | A5 |
| MSC | J2 | RS | E12 | HBIL | M9 | A3 | B5 |
| XF | J3 | D0 | E11 | NMI | L9 | HD6 | C5 |
| HOLDA | J4 | D1 | E10 | INT0 | K9 | A4 | D5 |
| IAQ | K1 | D2 | D13 | INT1 | N10 | A5 | A4 |
| HOLD | K2 | D3 | D12 | INT2 | M10 | A6 | B4 |
| BIO | K3 | D4 | D11 | INT3 | L10 | A7 | C4 |
| MP/MC | L1 | D5 | C13 | cvDD | N11 | A8 | A3 |
| DVDD | L2 | A16 | C12 | HD1 | M11 | A9 | B3 |
| vss | L3 | vss | C11 | vss | L11 | cvDD | C3 |
| BDR1 | M1 | A17 | B13 | BCLKX1 | N12 | A21 | A2 |
| BFSR1 | M2 | A18 | B12 | vss | M12 | vss | B2 |

t DVqq is the power supply for the I/O pins while CVqq is the power supply for the core CPU, and Vss is tne ground for both the I/O pins and the core CPU.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

11

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

'54x Signal Descriptions

|  | TERMINAL |  |
| --- | --- | --- |
| NAME TYPEt | DESCRIPTION |
|  |  | DATA SIGNALS |
| A22 | (MSB) | Parallel port address bus A22 (MSB) through A0 (LSB). The sixteen LSBs (A15-A0) are multiplexed to address |
| A21 |  | external data/program memory or I/O. A15-A0 are placed in the high-impedance state in the hold mode. A15-A0 |
| A20 |  | also go into the high-impedance state when EMU1/OFF is low. The seven MSBs (A22 to A16) are used for |
| A19 |  | extended program memory addressing ('548 and '549 only). |
| A18 |  | On the '548 and '549 devices, the address bus have a feature called bus holder that eliminates passive |
| A17 |  | components and the power dissipation associated with it. The bus holders keep the address bus at the previous |
| A16 |  | logic level when the bus goes into a high-impedance state. The bus holders on the address bus are always |
| A15 |  | enabled. |
| A14 |  |  |
| A13 |  |  |
| A12 |  |  |
| A11 | O/Z |  |
| A10 |  |  |
| A9 |  |  |
| A8 |  |  |
| A7 |  |  |
| A6 |  |  |
| A5 |  |  |
| A4 |  |  |
| A3 |  |  |
| A2 A1 |  |  |
| A0 | (LSB) |  |
| D15 | (MSB) | Parallel port data bus D15 (MSB) through D0 (LSB). D15-D0are multiplexed to transfer data between the core |
| D14 |  | CPU and external data/program memory or I/O devices. D15-D0 are placed in the high-impedance state when |
| D13 |  | not output or when RS or HOLD is asserted. D15-D0also go into the high-impedance state when EMU1/OFF |
| D12 |  | is low. |
| D11 |  | The data bus has a feature called bus holder that eliminates passive components and the power dissipation |
| D10 |  | associated with it. The bus holders keep the data bus at the previous logic level when the bus goes into a |
| D9 |  | high-impedance state. These bus holders are enabled or disabled by the BH bit in the bank switching control |
| D8 D7 | I/O/Z | register (BSCR). |
| D6 |  |  |
| D5 |  |  |
| D4 |  |  |
| D3 |  |  |
| D2 D1 |  |  |
| D0 | (LSB) |  |
|  |  | INITIALIZATION, INTERRUPT AND RESET OPERATIONS |
|  |  | Interrupt acknowledge signal. IACK indicates the receipt of an interrupt and that the program counter is fetching |
| IACK | O/Z | the interrupt vector location designated by A15-0. IACK also goes into the high-impedance state when |
|  |  | EMU1/OFF is low. |
| INT0 |  |  |
| INT1 | 1 | External user interrupt inputs. INT0-INT3are prioritized and are maskable by the interrupt mask register and the |
| INT2 | I | interrupt mode bit. INT0 -INT3 can be polled and reset by the interrupt flag register. |
| INT3 |  |  |

1I = Input, O = Output, Z = High impedance

12

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

| '54x Signal Descriptions (Continued) |
| --- |
| TERMINAL NAME TYPEt | DESCRIPTION |
| INITIALIZATION, INTERRUPT AND RESET OPERATIONS (CONTINUED) |
| nmI i | Nonmaskable interrupt. NMI is an external interrupt that cannot be masked by way ofthe INTMorthe IMR. When NMI is activated, the processor traps to the appropriate vector location. |
| RS I | Reset input. RS causes the DSP to terminate execution and forces the program counter to 0FF80h. When RS is brought to a high level, execution begins at location 0FF80h of the program memory. RS affects various registers and status bits. |
| MP/MC I | Microprocessor/microcomputer mode-select pin. If active-low at reset (microcomputer mode), MP/MC causes the internal program ROM to be mapped into the upper program memory space. In the microprocessor mode, off-chip memory and its corresponding addresses (instead of internal program ROM) are accessed by the DSP. |
| CNT I | I/O level select. For 5-V operation, all input and output voltage levels are TTL-compatible when CNT is pulled down to a low level. For 3-V operation with CMOS-compatible I/O interface levels, CNT is pulled to a high level. |
| MULTIPROCESSING SIGNALS |
| bio i | Branch control input. A branch can be conditionally executed when BIO is active. If low, the processor executes the conditional instruction. The BIO condition is sampled during the decode phase ofthe pipeline for the XC instruction, and all other instructions sample BIO during the read phase ofthe pipeline. |
| XF O/Z | External flag output (latched software-programmable signal). XF is set high by the SSBX XF instruction, set low by RSBX XF instruction or by loading the ST1 status register. XF is used for signaling other processors in multiprocessor configurations or as a general-purpose output pin. XF goes into the high-impedance state when OFF is low, and is set high at reset. |
| MEMORY CONTROL SIGNALS |
| DS PS O/Z IS | Data, program, and I/O space select signals. DS, PS, and IS are always high unless driven low for communicating to a particular external space. Active period corresponds to valid address information. Placed into a high-impedance state in hold mode. DS, PS, and IS also go into the high-impedance state when EMU1/OFF is low. |
| MSTRB O/Z | Memory strobe signal. MSTRB is always high unless low-level asserted to indicate an external bus access to data or program memory. Placed in high-impedance state in hold mode. MSTRB also goes into the high-impedance state when OFF is low. |
| READY I | Data-ready input. READY indicates that an external device is prepared for a bus transaction to be completed. If the device is not ready (READY is low), the processor waits one cycle and checks READY again. Note that the processor performs ready-detection if at least two software wait states are programmed. The READY signal is not sampled until the completion ofthe software wait states. |
| R/W O/Z | Read/write signal. R/W indicates transfer direction during communication to an external device and is normally high (in read mode), unless asserted low when the DSP performs a write operation. Placed in the high-impedance state in hold mode, R/W also goes into the high-impedance state when EMU1/OFF is low. |
| IOSTRB O/Z | I/O strobe signal. IOSTRB is always high unless low level asserted to indicate an external bus access to an I/O device. Placed in high-impedance state in hold mode. IOSTRB also goes into the high-impedance state when EMU1/OFFislow. |
| HOLD I | Hold input. HOLD is asserted to request control ofthe address, data, and control lines. When acknowledged by the '54x, these lines go into high-impedance state. |
| HOLDA O/Z | Hold acknowledge signal. HOLDA indicates to the external circuitry that the processor is in a hold state and that the address, data, and control lines are in a high-impedance state, allowing them to be available to the external circuitry. HOLDA also goes into the high-impedance state when EMU1/OFF is low. |
| MSC O/Z | Microstate complete signal. Goes low on CLKOUT falling at the start ofthe first software wait state. Remains low until one CLKOUT cycle before the last programmed software wait state. If connected to the READY line, MSC forces one external wait state after the last internal wait state has been completed. MSC also goes into the high-impedance state when EM1/OFF is low. |

1I = Input, O = Output, Z = High impedance

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

13

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

'54x Signal Descriptions (Continued)

| TERMINAL NAME TYPEt | DESCRIPTION |
| --- | --- |
| MEMORY CONTROL SIGNALS (CONTINUED) |
| Iaq o/z | Instruction acquisition signal. IAQ is asserted (active low) when there is an instruction address on the address bus and goes into the high-impedance state when EMU1/OFF is low. |
| OSCILLATOR/TIMER SIGNALS |
| CLKOUT O/Z | Master clock output signal. CLKOUT cycles at the machine-cycle rate of the CPU. The internal machine cycle is bounded by the falling edges ofthis signal. CLKOUT also goes into the high-impedance state when EMU1/OFF is low. |
| CLKMD1 CLKMD2 I CLKMD3 | Clock mode external/internal input signals. CLKMD1, CLKMD2, and CLKMD3 allow you to select and configure different clock modes, such as crystal, external clock, and various PLL factors. Refer to PLL section for a detailed functional description of these pins. |
| X2/CLKIN I | Input pin to internal oscillator from the crystal. If the internal (crystal) oscillator is not being used, a clock can become input to the device using this pin. The internal machine cycle time is determined by the clock operating-mode pins (CLKMD1, CLKMD2 and CLKMD3). |
| X1 O | Output pin from the internal oscillator for the crystal. If the internal oscillator is not used, X1 should be left unconnected. X1 does not go into the high-impedance state when EMU1/OFF is low. |
| TOUT O/Z | Timer output. TOUT signals a pulse when the on-chip timer counts down past zero. The pulse is a CLKOUT-cycle wide. TOUT also goes into the high-impedance state when EMU1/OFF is low. |
| BUFFERED SERIAL PORT 0 AND BUFFERED SERIAL PORT 1 SIGNALS |
| BCLKR0 BCLKR1 | Receive clocks. External clock signal for clocking data from the data-receive (DR) pin into the buffered serial port receive shift registers (RSRs). Must be present during buffered serial port transfers. If the buffered serial port is not being used, BCLKR0 and BCLKR1 can be sampled as an input by way of IN0 bit of the SPC register. |
| BCLKX0 BCLKX1 UUI^ | Transmit clock. Clock signal for clocking data from the serial port transmit shift register (XSR) to the data transmit (DX) pin. BCLKX can be an input if MCM in the serial port control register is cleared to 0. It also can be driven by the device at 1/(CLKDV+ 1) where CLKDV range is 0-31 CLKOUT frequency when MCM is set to 1. If the buffered serial port is not used, BCLKX can be sampled as an input by way of IN1 of the SPC register. BCLKX0 and BCLKX1 go into the high-impedance state when OFF is low. |
| BDR0 BDR1 ' | Buffered serial-data-receive input. Serial data is received in the RSR by BDR0/BDR1. |
| BDX0 BDX1 O/Z | Buffered serial-port-transmit output. Serial data is transmitted from the XSR by way of BDX. BDX0 and BDX1 are placed in the high-impedance state when not transmitting and when EMU1/OFF is low. |
| BFSR0 BFSR1 | Frame synchronization pulse for receive input. The falling edge of the BFSR pulse initiates the data-receive process, beginning the clocking of the RSR. |
| BFSX0 I/O/Z BFSX1 UUI^ | Frame synchronization pulse for transmit input/output. The falling edge of the BFSX pulse initiates the data-transmit process, beginning the clocking of the XSR. Following reset, the default operating condition of BFSX is an input. BFSX0 and BFSX1 can be selected by software to be an output when TXM in the serial control register is set to 1. This pin goes into the high-impedance state when EMU1/OFF is low. |
| SERIAL PORT 0 AND SERIAL PORT 1 SIGNALS |
| CLKR0 CLKR1 | Receive clocks. External clock signal for clocking data from the data receive (DR) pin into the serial port receive shift register (RSR). Must be present during serial port transfers. If the serial port is not being used, CLKR0 and CLKR1 can be sampled as an input via IN0 bit of the SPC register. |
| CLKX0 I/O/Z CLKX1 "u/^ | Transmit clock. Clock signal for clocking data from the serial port transmit shift register (XSR) to the data transmit (DX) pin. CLKX can be an input if MCM in the serial port control register is cleared to 0. It also can be driven by the device at 1/4 CLKOUT frequency when MCM is set to 1. If the serial port is not used, CLKX can be sampled as an input via IN1 of the SPC register. CLKX0 and CLKX1 go into the high-impedance state when EMU1/OFF is low. |
| DR0 DR1 | Serial-data-receive input. Serial data is received in the RSR by DR. |

1I = Input, O = Output, Z = High impedance

14

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

'54x Signal Descriptions (Continued)

| TERMINAL NAME TYPEt | DESCRIPTION |
| --- | --- |
|  |  | SERIAL PORT 0 AND SERIAL PORT 1 SIGNALS (CONTINUED) |
| DX0 DX1 | O/Z | Serial port transmit output. Serial data is transmitted from the XSR via DX. DX0 and DX1 are placed in the high-impedance state when not transmitting and when EMU1/OFF is low. |
| FSR0 FSR1 | I | Frame synchronization pulse for receive input. The falling edge of the FSR pulse initiates the data-receive process, beginning the clocking of the RSR. |
| FSX0 FSX1 | I/O/Z | Frame synchronization pulse fortransmit input/output. The falling edge of the FSX pulse initiates the data transmit process, beginning the clocking of the XSR. Following reset, the default operating condition of FSX is an input. FSX0 and FSX1 can be selected by software to be an output when TXM in the serial control register is set to 1. This pin goes into the high-impedance state when EMU1/OFF is low. |
|  |  | TDM SERIAL PORT SIGNALS |
| TCLKR | I | TDM receive clock input |
| TDR | I | TDM serial data-receive input |
| TFSR/TADD | I/O | TDM receive frame synchronization or TDM address |
| TCLKX | I/O/Z | TDM transmit clock |
| TDX | O/Z | TDM serial data-transmit output |
| TFSX/TFRM | I/O/Z | TDM transmit frame synchronization |
|  |  | HOST-PORT INTERFACE SIGNALS |
| HD0-HD7 | I/O/Z | Parallel bidirectional data bus. HD0-HD7 are placed in the high-impedance state when not outputting data. The signals go into the high-impedance state when EMU1/OFF is low. These pins each have bus holders similar to those on the address/data bus, but which are always enabled. |
| HCNTL0 HCNTL1 | I | Control inputs |
| HBIL | I | Byte-identification input |
| HCS | I | Chip-select input |
| HDS1 HDS2 | I | Data strobe inputs |
| HAS | I | Address strobe input |
| HR/W | I | Read/write input |
| HRDY | O/Z | Ready output. This signal goes into the high-impedance state when EMU1/OFF is low. |
| HINT | O/Z | Interrupt output. When the DSP is in reset, this signal is driven high. The signal goes into the high-impedance state when EMU1/OFF is low. |
| HPIENA | I | HPI module select input. This signal must be tied to a logic 1 state to have HPI selected. If this input is left open or connected to ground, the HPI module will not be selected, internal pullup for the HPI input pins are enabled, and the HPI data bus has keepers set. This input is provided with an internal pull-down resistor which is active only when RS is low. HPIENA is sampled when RS goes high and ignored until RS goes low again. Refer to the Electrical Characteristics section for the input current requirements for this pin. |
|  |  | SUPPLY PINS |
| cvDD | Supply | +Vdq. CVqq is the dedicated power supply for the core CPU. |
| DVDD | Supply | +Vdq. DVqq is the dedicated power supply for I/O pins. |
| vSs | Supply | Ground. Vss is the dedicated power ground for the device. |

1I = Input, O = Output, Z = High impedance

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

15

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

'54x Signal Descriptions (Continued)

| TERMINAL NAME TYPEt | DESCRIPTION |
| --- | --- |
| IEEE1149.1 TEST PINS |
| TCK I | IEEE standard 1149.1 test clock. Pin with internal pullup device. This is normally a free-running clock signal with a 50% duty cycle. The changes on the test-access port (TAP) of input signals TMS and TDI are clocked into the TAP controller, instruction register, or selected test data register on the rising edge of TCK. Changes at the TAP output signal (TDO) occur on the falling edge of TCK. |
| TDI I | IEEE standard 1149.1 test data input. Pin with internal pullup device. TDI is clocked into the selected register (instruction or data) on a rising edge of TCK. |
| TDO O/Z | IEEE standard 1149.1 test data output. The contents of the selected register (instruction or data) is shifted out of TDO on the falling edge of TCK. TDO is in the high-impedance state except when the scanning of data is in progress. TDO also goes into the high-impedance state when EMU1/OFF is low. |
| TMS I | IEEE standard 1149.1 test mode select. Pin with internal pullup device. This serial control input is clocked into the TAP controller on the rising edge of TCK. |
| TRST I | IEEE standard 1149.1 test reset. TRST, when high, gives the IEEE standard 1149.1 scan system control of the operations of the device. If TRST is not connected or driven low, the device operates in its functional mode, and the IEEE standard 1149.1 signals are ignored. Pin with internal pulldown device. |
| EMU0 I/O/Z | Emulator interrupt 0 pin. When TRST is driven low, EMU0 must be high for the activation of the EMU1/OFF condition. When TRST is driven high, EMU0 is used as an interrupt to or from the emulator system and is defined as input/output by way of IEEE standard 1149.1 scan system. |
| EMU1/OFF I/O/Z | Emulator interrupt 1 pin/disable all outputs. When TRST is driven high, EMU1/OFF is used as an interrupt to or from the emulator system and is defined as input/output byway of IEEE standard 1149.1 scan system. When TRST is driven low, EMU1/OFF is configured as OFF. The EMU1/OFF signal, when active low, puts all output drivers into the high-impedance state. Note that OFF is used exclusively for testing and emulation purposes (not for multiprocessing applications). Therefore, for the OFF condition, the following conditions apply: TRST = low, EMU0 = high EMU1/OFF = low |
| DEVICE TEST PIN |
| TEST1 I | Test1 - Reserved for internal use only ('LC548, 'LC549, and 'VC549 only). This pin must not be connected (NC). |

1I = Input, O = Output, Z = High impedance

architecture

The '54x DSPs use an advanced, modified Harvard architecture that maximizes processing power by maintaining three separate bus structures for data memory and one for program memory. Separate program and data spaces allow simultaneous access to program instructions and data, providing a high degree of parallelism. For example, two read and one write operations can be performed in a single cycle. Instructions with parallel store and application-specific instructions fully utilize this architecture. In addition, data can be transferred between data and program spaces. Such parallelism supports a powerful set of arithmetic, logic, and bit-manipulation operations that can all be performed in a single machine cycle. In addition, the '54x include the control mechanisms to manage interrupts, repeated operations, and function calls.

The functional block diagram includes the principal blocks and bus structure in the '54x devices.

16

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

functional block diagram of the '54x internal hardware

System Control Interface

Program Address Generation Logic (PAGEN)

Data Address Generation Logic (DAGEN)

o

PC, IPTR, RC, BRC, RSA, REA

ARAU0,ARAU1,

AR0-AR7 ARP, BK, DP, SP

PAB

pb r

CAB f

CB|_ DAB f

Memory

And External Interface

DBF

eabF

Peripherals

(Serial Ports,

HPI, etc.)

EB

EXP Encoder

MUX

/

T Register

\ Sign Ctr /   \ Sign Ctr /

A(40)	B(40)	\Sign Ctr/   \Sign Ctr/

\Sign Ctr/

Multiplier(17x17)

Fractional

\ MUX /

V1	■/

\       Adder(40)      /

ZERO

SAT

ROUND

V

ALU(40)

| Legend: |
| --- |
| A | Accumulator A |
| B | Accumulator B |
| C | CB Data Bus |
| D | DB Data Bus |
| E | EB Data Bus |
| M | MAC Unit |
| P | PB Program Bus |
| S | Barrel Shifter |
| T | T Register |
| U | ALU |

\

MUX

COMP

TRN

TC

Barrel Shifter

MSW/LSW Select

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

17

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

central processing unit (CPU)

The CPU of the '54x devices contains:

A 40-bit arithmetic logic unit (ALU)

Two 40-bit accumulators

A barrel shifter

A 17 x 17-bit multiplier/adder

A compare, select and store unit (CSSU)

arithmetic logic unit (ALU)

The '54x devices perform 2s-complement arithmetic using: a 40-bit arithmetic logic unit (ALU) and two 40-bit accumulators (ACCA and ACCB). The ALU also can perform Boolean operations.

The ALU can function as two 16-bit ALUs and perform two 16-bit operations simultaneously when the C16 bit in status register 1 (ST1) is set.

accumulators

The accumulators, ACCA and ACCB, store the output from the ALU or the multiplier/adder block; the accumulators can also provide a second input to the ALU orthe multiplier/ adder. The accumulators are divided into three parts:

- Guard bits (bits 32-39)

- A high-order word (bits 16-31)

- A low-order word (bits 0-15)

Instructions are provided for storing the guard bits, the high- and the low-order accumulator words in data memory, and for manipulating 32-bit accumulatorwords in or out of data memory. Also, any of the accumulators can be used as temporary storage for the other.

barrel shifter

The '54x's barrel shifter has a 40-bit input connected to the accumulator, or data memory (CB, DB) and a 40-bit output connected to the ALU, or data memory (EB). The barrel shifter produces a left shift of 0 to 31 bits and a right shift of 0 to 16 bits on the input data. The shift requirements are defined in the shift-count field (ASM) of ST1 or defined in the temporary register (TREG), which is designated as a shift-count register. This shifter and the exponent detector normalize the values in an accumulator in a single cycle. The least significant bits (LSBs) of the output are filled with 0s and the most significant bits (MSBs) can be eitherzero-filled or sign-extended, depending on the state of the sign-extended mode bit (SXM) of ST1. Additional shift capabilities enable the processorto perform numerical scaling, bit extraction, extended arithmetic, and overflow prevention operations.

multiplier/adder

The multiplier/adder performs 17 x 17-bit 2s-complement multiplication with a 40-bit accumulation in a single instruction cycle. The multiplier/adder block consists of several elements: a multiplier, adder, signed/unsigned input control, fractional control, a zero detector, a rounder (2s-complement), overflow/saturation logic, and TREG. The multiplier has two inputs: one input is selected from the TREG, a data-memory operand, or an accumulator; the other is selected from the program memory, the data memory, an accumulator, or an immediate value. The fast on-chip multiplier allows the '54x to perform operations such as convolution, correlation, and filtering efficiently.

In addition, the multiplier and ALU together execute multiply/accumulate (MAC) computations and ALU operations in parallel in a single instruction cycle. This function is used in determining the Euclid distance, and in implementing symmetrical and least mean square (LMS) filters, which are required for complex DSP algorithms.

Texas Instruments

1 8	POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

compare, select and store unit (CSSU)

The compare, select and store unit (CSSU) performs maximum comparisons between the accumulator's high and low word, allows the test/control (TC) flag bit of status register 0 (ST0) and the transition (TRN) register to keep their transition histories, and selects the larger word in the accumulator to be stored in data memory. The CSSU also accelerates Viterbi-type butterfly computation with optimized on-chip hardware.

program control

Program control is provided by several hardware and software mechanisms:

- The program controller decodes instructions, manages the pipeline, stores the status of operations, and
decodes conditional operations. Some of the hardware elements included in the program controller are the
program counter, the status and control register, the stack, and the address-generation logic.

- Some of the software mechanisms used for program control include branches, calls, conditional
instructions, a repeat instruction, reset, and interrupts.

power-down modes

There are three power-down modes, activated by the IDLE1, IDLE2, and IDLE3 instructions. In these modes, the '54x devices enter a dormant state and dissipate considerably less power than in normal operation. The IDLE1 instruction is used to shutdown the CPU. The IDLE2 instruction is used to shutdown the CPU and on-chip peripherals. The IDLE3 instruction is used to shut down the '54x processor completely. This instruction stops the PLL circuitry as well as the CPU and peripherals.

bus structure

The '54x device architecture is built around eight major 16-bit buses:

- One program-read bus (PB), which carries the instruction code and immediate operands from program
memory

- Two data-read buses (CB, DB) and one data-write bus (EB), which interconnect to various elements, such
as the CPU, data-address generation logic, program-address generation logic, on-chip peripherals, and
data memory

- The CB and DB carry the operands read from data memory.

- The EB carries the data to be written to memory.

•	Four address buses (PAB, CAB, DAB, and EAB), which carry the addresses needed for instruction
execution

The '54x devices have the capability to generate up to two data-memory addresses per cycle, which are stored into two auxiliary register arithmetic units (ARAU0 and ARAU1).

The PB can carry data operands stored in program space (for instance, a coefficient table) to the multiplier for multiply/accumulate operations or to a destination in data space for the data move instruction. This capability allows implementation of single-cycle three-operand instructions such as FIRS.

The '54x devices also have an on-chip bidirectional bus for accessing on-chip peripherals; this bus is connected to DB and EB through the bus exchanger in the CPU interface. Accesses using this bus can require more than two cycles for reads and writes depending on the peripheral's structure.

The '54x devices can have bus keepers connected to the data bus. Bus keepers ensure that the data bus does not float. When bus keepers are enabled, the data bus maintains its previous level. Setting bit 1 of the bank switching control register (BSCR) enables bus keepers and clearing bit 1 disables the bus keepers. A reset automatically disables the bus keepers.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443	1 9

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

bus structure (continued)

The '548 and '549 devices also have equivalent bus keepers connected to the address bus. The bus keepers ensure the address bus does not float when in high-impedance. For the '548 and '549 devices, the bus keepers are always enabled.

Table 2 summarizes the buses used by various types of accesses.

|  |  | Table 2. | Bus Usage for | Accesses |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| ACCESS TYPE | ADDRESS BUS | PROGRAM BUS | DATA BUS |
|  | PAB | CAB | DAB | EAB | PB | CB | DB | EB |
| Program read | V |  |  |  | V |  |  |  |
| Program write | V |  |  |  |  |  |  | V |
| Data single read |  |  | V |  |  |  | V |  |
| Data dual read |  | V | V |  |  | V | V |  |
| Data long (32-bit) read |  | V(hw) | V(lw) |  |  | V(hw) | V(lw) |  |
| Data single write |  |  |  | V |  |  |  | V |
| Data read/data write |  |  | V | V |  |  | V | V |
| Dual read/coefficient read | V | V | V |  | V | V | V |  |
| Peripheral read |  |  | V |  |  |  | V |  |
| Peripheral write |  |  |  | V |  |  |  | V |

Legend:

hw = high 16-bit word lw = low 16-bit word

memory

The total memory address range for the host of'54x devices is 192K 16-bit words. The '548 and '549 devices have 8M-word program memory. The memory space is divided into three specific memory segments: 64K-word program, 64K-word data, and 64K-word I/O. The program memory space contains the instructions to be executed as well as tables used in execution. The data memory space stores data used by the instructions. The I/O memory space interfaces to external memory-mapped peripherals and can also serve as extra data storage space.

The parallel nature of the architecture of these DSPs allows them to perform four concurrent memory operations in any given machine cycle: fetching an instruction, reading two operands, and writing an operand. The four parallel buses are the program-read bus (PB), the data-write bus (EB) and the two data-read buses (CB and DB). Each bus accesses different memory spaces fordifferent aspects of the DSP's operation. Additionally, this architecture allows dual-operand reads, 32-bit-long word accesses, and a single read with a parallel store.

The '54x DSPs include on-chip memory to aid in system performance and integration. on-chip ROM

The'C541 and'LC541 feature a 28K-wordx 16-bit on-chip maskable ROM. 8K words of the'C541 and'LC541 ROM can be mapped into program and data memory space if the data ROM (DROM) bit in the processor mode status (PMST) register is set. This allows an instruction to use data stored in the ROM as an operand.

The 'LC545/'LC546 all feature a 48K-word x 16-bit on-chip maskable ROM. 16K words of the ROM on these devices can be mapped into program and data memory space if the DROM bit in the PMST register is set.

The 'C542/'LC542/'LC543/'LC548 all feature 2K-word x 16-bit on-chip ROM. The 'LC549 and 'VC549 feature 16K-word x 16-bit on-chip ROM.

20

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

on-chip ROM (continued)

Customers can arrange to have the ROM of the '54x programmed with contents unique to any particular application.

on-chip dual-access RAM (DARAM)

The '541 devices have a 5K-word x 16-bit on-chip DARAM (5 blocks of 1K-word each). The '542 and '543 devices have a 10K-word x 16-bit on-chip DARAM (5 blocks of 2K-word each). The '545 and '546 devices have a 6K-word x 16-bit on-chip DARAM (3 blocks of 2K-word each). The '548 and '549 devices have a 8K-word x 16-bit on-chip DARAM (4 blocks of 2K-word each).

Each of these RAM blocks can be accessed twice per machine cycle. This memory is intended primarily to store data values; however, it can be used to store program as well. At reset, the DARAM is mapped into data memory space. DARAM can be mapped into program/data memory space by setting the OVLY bit in the PMST register.

on-chip single-access RAM (SARAM)

The '548 and '549 devices have a 24Kword x 16 bit on-chip SARAM (three blocks of 8K words each).

Each of these SARAM blocks is a single-access memory. This memory is intended primarily to store data values; however, it can be used to store program as well. At reset, the SARAM is mapped into data memory space (2000h-7FFFh). SARAM can be mapped into program/data memory space by setting the OVLY bit in the PMST register.

on-chip memory security

The '54x devices have a maskable option to protect the contents of on-chip memories. When the related bit is set, no externally originating instruction can access the on-chip memory spaces.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443	21

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

memory (continued)

| Hex | Program |
| --- | --- |
| 0000 007F 0080 13FF 1400 FF7F | Reserved (OVLY= 1) or External (OVLY=0) |
|  | On-Chip DARAM (OVLY=1) or External (OVLY=0) |
|  | External |
| FF80 FFFF | Interrupts and Reserved (External) |

MP/MC= 1 (Microprocessor Mode)

| Hex | Proqram |
| --- | --- |
| 0000 007F 0080 13FF 1400 8FFF | Reserved (OVLY=1) or External (OVLY=0) |
|  | On-Chip DARAM (OVLY=1) or External (OVLY=0) |
|  | External |
| 9000 FF7F | On-Chip ROM (28K Words) |
| FF80 FFFF | Interrupts and Reserved (On-Chip) |

MP/MC= 0 (Microcomputer Mode)

Figure 1. Memory Map ('541 only)

| Hex | Data |
| --- | --- |
| 0000 005F 0060 007F 0080 13FF | Memory-Mapped Registers |
|  | Scratch-Pad RAM |
|  | On-Chip DARAM (5K Words) |
| 1400 DFFF E000 FEFF FF00 FFFF | External |
|  | On-Chip ROM (DROM=1) or External (DROM = 0) |
|  | Reserved (DROM=1) or External (DROM= 0) |

Hex 0000

007F 0080

27FF 2800

FF7F FF80

FFFF

Program

Reserved (OVLY=1)

or External (OVLY=0)

On-Chip DARAM (OVLY=1)

or External (OVLY=0)

External

Interrupts and Reserved (External)

MP/MC=1 (Microprocessor Mode)

| Hex | Program |
| --- | --- |
| 0000 007F | Reserved (OVLY=1) or External (OVLY=0) |
| 0080 27FF | On-Chip DARAM (OVLY=1) or External (OVLY=0) |
| 2800 EFFF | External |
| F000 F7FF | Reserved |
| F800 FF7F | On-Chip ROM (2K Words) |
| FF80 FFFF | Interrupts and Reserved (On-Chip) |

MP/MC= 0 (Microcomputer Mode)

| Hex | Data |
| --- | --- |
| 0000 005F 0060 007F 0080 | Memory-Mapped Registers |
|  | Scratch-Pad RAM |
|  | On-Chip DARAM (10K Words) |
| 27FF |  |
| 2800 |  |
|  | External |
| FFFF |  |

Figure 2. Memory Map ('542 and '543 only)

22

^? Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

memory (continued)

MP/MC= 0 (Microcomputer Mode)

Figure 3. Memory Map ('545 and '546 only)

Hex	Program

0000

Reserved (OVLY=1)

or External (OVLY=0)

007F 0080

On-Chip DARAM (OVLY= 1)

or External (OVLY=0)

17FF 1800

External

FF7F FF80

FFFF

Interrupts and Reserved (External)

MP/MC= 1 (Microprocessor Mode)

| Hex | Program |
| --- | --- |
| 0000 007F 0080 17FF 1800 3FFF | Reserved (OVLY= 1) or External (OVLY=0) |
|  | On-Chip DARAM (OVLY= 1) or External (OVLY=0) |
|  | External |
| 4000 FF7F | On-Chip ROM (48 K Words) |
| FF80 FFFF | Interrupts and Reserved (On-Chip) |

Hex

Data

| 0000 005F 0060 007F 0080 17FF | Memory-Mapped Registers |
| --- | --- |
|  | Scratch-Pad RAM |
|  | On-Chip DARAM (6K Words) |
| 1800 BFFF | External |
| C000 FEFF | On-Chip ROM (DROM= 1) or External (DROM = 0) |
| FF00 FFFF | Reserved (DROM=1) or External (DROM= 0) |

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

23

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

memory (continued)

| Hex | Program |
| --- | --- |
| 0000 007F | Reserved (OVLY=1) or External (OVLY=0) |
| 0080 1FFF | On-Chip DARAM (OVLY=1) or External (OVLY=0) |
| 2000 7FFF | On-Chip SARAM (OVLY=1) or External (OVLY=0) |
| 8000 FF7F | External |
| FF80 FFFF | Interrupts and Reserved (External) |

| Hex | Program |
| --- | --- |
| 0000 007F 0080 1FFF | Reserved (OVLY=1) or External (OVLY=0) |
|  | On-Chip DARAM (OVLY=1) or External (OVLY=0) |
| 2000 7FFF | On-Chip SARAM (OVLY= 1) or External (OVLY=0) |
| 8000 EFFF | External |
| F000 F7FF | Reserved |
| F800 FF7F | On-Chip ROM (2K Words) |
| FF80 FFFF | Interrupts and Reserved (On-Chip) |

| Hex | Data |
| --- | --- |
| 0000 005F | Memory-Mapped Registers |
| 0060 007F | Scratch-Pad RAM |
| 0080 |  |
|  | On-Chip DARAM (8K Words) |
| 1FFF |  |
| 2000 |  |
|  | On-Chip SARAM (24K Words) |
| 7FFF |  |
| 8000 |  |
|  | External |
| FFFF |  |

MP/MC=1 (Microprocessor Mode)

MP/MC= 0 (Microcomputer Mode)

Figure 4. Memory Map ('548 only) (In the case of a 64K Program Word Address Reach)

24

^? Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

memory (continued)

| Hex | Program |
| --- | --- |
| 0000 007F | Reserved (OVLY=1) or External (OVLY=0) |
| 0080 1FFF | On-Chip DARAM (OVLY=1) or External (OVLY=0) |
| 2000 7FFF | On-Chip SARAM (OVLY=1) or External (OVLY=0) |
| 8000 FF7F | External |
| FF80 FFFF | Interrupts and Reserved (External) |

| Hex | Program |
| --- | --- |
| 0000 007F | Reserved (OVLY= 1) or External (OVLY=0) |
| 0080 1FFF | On-Chip DARAM (OVLY= 1) or External (OVLY=0) |
| 2000 7FFF | On-Chip SARAM (OVLY=1) or External (OVLY=0) |
| 8000 BFFF C000 FEFF FF00 FFFF | External |
|  | On-Chip ROM (16K Words) |
|  | Interrupts and Reserved (On-Chip) |

| Hex | Data |
| --- | --- |
| 0000 005F | Memory-Mapped Registers |
| 0060 007F | Scratch-Pad RAM |
| 0080 1FFF | On-Chip DARAM (8K Words) |
| 2000 7FFF | On-Chip SARAM (24K Words) |
| 8000 BFFF | External |
| C000 FEFF | On-Chip ROM (DROM=1) or External (DROM = 0) |
| FF00 FFFF | Reserved (DROM= 1) or External (DROM= 0) |

MP/MC= 1 (Microprocessor Mode)

MP/MC= 0 (Microcomputer Mode)

Figure 5. Memory Map ('549 only)

| xx 0000 |  | 010000 | r -i | 02 0000 | r -i | 7F 0000 | r -i |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | PageO |  | Page 1 |  | Page 2 |  | Page 127 |
|  | 32K Wordst |  | 32K Wordst |  | 32K Wordst | • • • | 32K Wordst |
| xx7FFF |  | 01 FFFF | _ | 02 FFFF | i_ J | 7FFFFF | J |
| 00 8000 |  | 018000 |  | 02 8000 |  | 7F 8000 |  |
|  | PageO |  | Page 1 |  | Page 2 |  | Page 127 |
|  | 32K Words |  | 32K Words |  | 32K Words | • • • | 32K Words |
| 00 FFFF |  | 01 FFFF |  | 02 FFFF |  | 7FFFFF |  |
|  | XPC = 0 |  | XPC= 1 |  | XPC = 2 |  | XPC = 127 |

t See Figure 4 and Figure 5 for more information about this on-chip memory region.

t These pages available when OVLY = 0when on-chip RAM is not mapped in program space or data space. When OVLY = 1 the first 32K words

are all on page 0 when on-chip RAM is mapped in program space or data space.

NOTE A: When the on-chip RAM is enabled in program space, all accesses to the region xx 0000 - xx 7FFF, regardless of page number, are mapped to the on-chip RAM at 00 0000 - 00 7FFF.

Figure 6. Extended Program Memory ('548 and '549 only)

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

25

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

program memory

The external program memory space on the '54x devices addresses up to 64K 16-bit words. Software can configure their memory cells to reside inside or outside of the program address map. When the cells are mapped into program space, the device automatically accesses them when their addresses are within bounds. When the program-address generation (PAGEN) logic generates an address outside its bounds, the device automatically generates an external access. The advantages of operating from on-chip memory are as follows:

- Higher performance because no wait states are required

- Lower cost than external memory

- Lower power than external memory

The advantage of operating from off-chip memory is the ability to access a larger address space. program memory address map

The reset, interrupt, and trap vectors are addressed in program space. These vectors are soft — meaning that the processor, when taking the trap, loads the program counter (PC) with the trap address and executes the code at the vector location. Fourwords are reserved at each vector location to accommodate a delayed branch instruction, and either two 1-word instructions or one 2-word instruction, which allows branching to the appropriate interrupt service routine without the overhead.

At device reset, the reset, interrupt, and trap vectors are mapped to address FF80h in program space. However, these vectors can be remapped to the beginning of any 128-word page in program space after device reset. This is done by loading the interrupt vector pointer (IPTR) bits in the PMST register with the appropriate 128-word page boundary address. After loading IPTR, any user interrupt or trap vector is mapped to the new 128-word page. For example:

STM   #05800h,PMST     ;Remapped vectors to start at 5800h.

This example moves the interrupt vectors to program space at address 05800h. Any subsequent interrupt (except for a device reset) fetches its interrupt vector from that new location. For example, if, after loading the IPTR, an INT2 occurs, the interrupt service routine vector is fetched from location 5848h in program space as opposed to location FFC8h. This feature facilitates moving the desired vectors out of the boot ROM and then removing the ROM from the memory map. Once the system code is booted into the system from the boot-loader code resident in ROM, the application reloads the IPTR with a value pointing to the new vectors. In the previous example, the STM instruction is used to modify the PMST. Note that the STM instruction modifies not only the IPTR but other status/control bits in the PMST register.

NOTE: The hardware reset (RS) vector cannot be remapped, because the hardware reset loads the IPTR with 1s. Therefore, the reset vector is always fetched at location FF80h in program space. In addition, for the '54x, 128 words are reserved in the on-chip ROM for device-testing purposes. Application code written to be implemented in on-chip ROM must reserve these 128 words at addresses FF00h-FF7Fh in program space.

extended program memory ('548 and '549 only)

The '548 and '549 devices use a paged extended memory scheme in program space to allow access of up to 8M of program memory. This extended program memory is organized into 128 pages (0-127), each 64K in length. To implement the extended program memory scheme, the '548 and '549 device includes the following additional features:

- Seven additional address lines (for a total of 23)

- An extra memory-mapped register [program counter extension register (XPC)]

Texas Instruments

26	POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

extended program memory ('548 and '549 only) (continued)

•	Six new instructions for addressing extended program memory space:

- FB[D] — Far branch

- FBACC[D] — Far branch to the location specified by the value in accumulator A or accumulator B

- FCALA[D] — Far call to the location specified by the value in accumulator A or accumulator B

- FCALL[D] — Far call

- FRET[D] — Far return

- FRETE[D] — Far return with interrupts enabled

•	Two '54x instructions are extended to use the 23 bits in the '548 and '549 devices:

- READA — Read program memory addressed by accumulator A and store in data memory

- WRITA — Write data to program memory addressed by accumulator A

For more information on these six new instructions and the two extended instructions, refer to the instruction set summary table in this data sheet and to the TMS320C54x DSP Reference Set, Volume 2, Mnemonic Instruction Set, literature number SPRU172. And for more information on extended program memory, refer to the TMS320C54x DSP Reference Set, Volume 1, CPU and Peripherals, literature number SPRU131.

data memory

The data memory space on the '54x device addresses contains up to 64K of 16-bit words. The 'devices automatically access the on-chip RAM when addressing within its bounds. When an address is generated outside the RAM bounds, the device automatically generates an external access.

The advantages of operating from on-chip memory are as follows:

- Higher performance because no wait states are required

- Higher performance because of better flow within the pipeline of the CALU

- Lower cost than external memory

- Lower power than external memory

The advantage of operating from off-chip memory is the ability to access a larger address space. bootloader

A bootloader is available in the standard '54x on-chip ROM. This bootloader can be used to transfer user code from an external source to anywhere in the program memory at power up automatically. If MP/MC of the device is sampled low during a hardware reset, execution begins at location FF80h of the on-chip ROM. This location contains a branch instruction to the start of the bootloader program. The standard '54x devices provide different ways to download the code to accommodate various system requirements:

- Parallel from 8-bit or 16-bit-wide EPROM

- Parallel from I/O space 8-bit or 16-bit mode

- Serial boot from serial ports 8-bit or 16-bit mode

- Host-port interface boot ('542, '545, '548, and '549 devices only)

- Warm boot

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443	27

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

bootloader (continued)

The bootloader provided in the on-chip ROM of the '548 and '549 devices implements several enhanced features. These include the addition of BSP and TDM boot modes. To accommodate these new boot modes, the encoding of the boot-mode selection word has been modified.

Fora detailed description of bootloader functionality, refer to the TMS320C54x DSP Reference Set, Volume 4: Applications Guide (literature number SPRU173). For a detailed description of the enhanced bootloader functionality, refer to the TMS320x548/'549 Bootloader Technical Reference.

on-chip peripherals

All the '54x devices have the same CPU structure; however, they have different on-chip peripherals connected to their CPUs. The on-chip peripheral options provided are:

Software-programmable wait-state generator

Programmable bank switching

Parallel I/O ports

Serial ports (standard, TDM, and BSP)

A hardware timer

A clock generator [with a multiple phase-locked loop (PLL) on '549 devices]

software-programmable wait-state generators

Software-programmable wait-state generators can be used to extend external bus cycles up to seven machine cycles to interface with slower off-chip memory and I/O devices. The software wait-state generators are incorporated without any external hardware. For off-chip memory access, a number of wait states can be specified for every 32K-word block of program and data memory space, and for one 64K-word block of I/O space within the software wait-state (SVWVSR) register.

programmable bank-switching

Programmable bank-switching can be used to insert one cycle automatically when crossing memory-bank boundaries inside program memory or data memory space. One cycle can also be inserted when crossing from program-memory space to data-memory space ('54x) or one program memory page to another program memory page ('548 and '549 only). This extra cycle allows memory devices to release the bus before other devices start driving the bus; thereby avoiding bus contention. The size of memory bank forthe bank-switching is defined by the bank-switching control register (BSCR).

parallel I/O ports

Each '54x device has a total of 64K I/O ports. These ports can be addressed by the PORTR instruction or the PORTW instruction. The IS signal indicates a read/write operation through an I/O port. The devices can interface easily with external devices through the I/O ports while requiring minimal off-chip address-decoding circuits.

host-port interface ('542, '545, '548, and '549 only)

The host-port interface (HPI) is an 8-bit parallel port used to interface a host processor to the DSP device. Information is exchanged between the DSP device and the host processor through on-chip memory that is accessible by both the host and the DSP device. The DSP devices have access to the HPI control (HPIC) register and the host can address the HPI memory through the HPI address register (HPIA). HPI memory is a 2K-word DARAM block that resides at 1000h to 17FFh in data memory and can also be used as general-purpose on-chip data or program DARAM.

Texas Instruments

28	POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

host-port interface ('542, '545, '548, and '549 only) (continued)

Data transfers of 16-bit words occur as two consecutive bytes with a dedicated pin (HBIL) indicating whether the high or low byte is being transmitted. Two control pins, HCNTL1 and HCNTL0, control host access to the HPIA, HPI data (with an optional automatic address increment), or the HPIC. The host can interrupt the DSP device by writing to HPIC. The DSP device can interrupt the host with a dedicated HINT pin that the host can acknowledge and clear.

The HPI has two modes of operation, shared-access mode (SAM) and host-only mode (HOM). In SAM, the normal mode of operation, both the DSP device and the host can access HPI memory. In this mode, asynchronous host accesses are resynchronized internally and, in case of conflict, the host has access priority and the DSP device waits one cycle. The HOM capability allows the host to access HPI memory while the DSP device is in IDLE2 (all internal clocks stopped) or in reset mode. The host can therefore access the HPI RAM while the DSP device is in its optimal configuration in terms of power consumption.

The HPI control register has two data strobes, HDS1 and HDS2, a read/write strobe HR/W, and an address strobe HAS, to enable a glueless interface to a variety of industry-standard host devices. The HPI is interfaced easily to hosts with multiplexed address/data bus, separate address and data buses, one data strobe and a read/write strobe, or two separate strobes for read and write.

The HPI supports high-speed back-to-back accesses.

- In the SAM, the HPI can handle one byte every five DSP device periods—that is, 64 MBps with a 40-MIPS
DSP, or 160 MBps with a 100-MIPS DSP. The HPI is designed so that the host can take advantage of this
high bandwidth and run at frequencies up to (f x n) ^5, where n is the number of host cycles for an external
access and f is the DSP device frequency.

- In HOM, the HPI supports high-speed back-to-back host accesses at 1 byte every 50 ns—that is, 160 MBps
with a -40 or faster DSP.

serial ports

The '54x devices provide high-speed full-duplex serial ports that allow direct interface to other '54x devices, codecs, and other devices in a system. There is a standard serial port, a time-division-multiplexed (TDM) serial port, and a buffered serial port (BSP). The '549 devices provides a misalignment detection feature to that allows the device to detect when a word or words are lost in the serial data line.

The general-purpose serial port utilizes two memory-mapped registers for data transfer: the data-transmit register (DXR) and the data-receive register (DRR). Both of these registers can be accessed in the same manner as any other memory location. The transmit and receive sections of the serial port each have associated clocks, frame-synchronization pulses, and serial-shift registers; and serial data can be transferred either in bytes or in 16-bit words. Serial port receive and transmit operations can generate their own maskable transmit and receive interrupts (XINTand RINT), allowing serial-port transfers to be managed through software. The '54x serial ports are double-buffered and fully static.

The TDM port allows the device to communicate through time-division multiplexing with up to seven other '54x devices with TDM ports. Time-division multiplexing is the division of time intervals into a number of subintervals with each subinterval representing a prespecified communications channel. The TDM port serially transmits 16-bit words on a single data line (TDAT) and destination addresses on a single address line (TADD). Each device can transmit data on a single channel and receive data from one or more of the eight channels, providing a simple and efficient interface for multiprocessing applications. A frame synchronization pulse occurs once every 128 clock cycles, corresponding to the transmission of one 16-bit word on each of the eight channels. Like the general-purpose serial port, the TDM port is double-buffered on both input and output data.

The buffered serial port (BSP) consists of a full-duplex double-buffered serial-port interface and an auto-buffering unit (ABU). The serial port block of the BSP is an enhanced version of the standard serial port. The ABU allows the serial port to read/write directly to the '54x internal memory using a dedicated bus independent of the CPU. This results in minimal overhead for serial port transactions and faster data rates.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443	29

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

serial ports (continued)

When auto-buffering capability is disabled (standard mode), serial port transfers are performed undersoftware control through interrupts. In this mode, the ABU is transparent and the word-based interrupts (WXINT and WRINT) provided by the serial port are sent to the CPU as transmit interrupt (XINT) and receive interrupt (RINT). When auto buffering is enabled, word transfers are done directly between the serial port and the '54x internal memory using ABU-embedded address generators.

The ABU has its own set of circular-addressing registers with corresponding address-generation units. Memory forthe buffers resides in 2K words of the '54x internal memory. The length and starting addresses of the buffers are user-programmable. A buffer-empty/buffer-full interrupt can be posted to the CPU. Buffering is easily halted by an auto-disabling capability. Auto-buffering capability can be enabled separately for transmit and receive sections. When auto buffering is disabled, operation is similarto that of the general-purpose serial port.

The BSP allows transfer of 8-, 10-, 12-, or 16-bit data packets. In burst mode, data packets are directed by a frame synchronization pulse for every packet. In continuous mode, the frame synchronization pulse occurs when the data transmission is initiated and no further pulses occur. The frame and clock strobes are frequency-and polarity-programmable. The BSP is fully static and operates at arbitrarily low clock frequencies. The maximum operating frequency for '54x devices up to 50 MIPs is CLKOUT. For higher-speed '54x devices, the maximum operating frequency is 50 MBps at 20 ns.

buffer misalignment (BMINT) interrupt ('549 only)

The BMINT interrupt is generated when a frame sync occurs and the ABU transmit or receive buffer pointer is not at the top of the buffer address. This is useful for detecting several potential error conditions on the serial interface, including extraneous and missed clocks and frame sync pulses. A BMINT interrupt, therefore, indicates that one or more words may have been lost on the serial interface.

BMINT is useful for detecting buffer misalignment only when the buffer pointers) are initially loaded with the top of buffer address, and a frame of data contains the same number of words as the buffer length. These are the only conditions underwhich a frame sync occurring at a buffer address, otherthan the top of buffer, constitute an error condition. In cases where these conditions are met, a frame sync always occurs when the buffer pointer is at the top of buffer address, if the interface is functioning properly.

If BMINT is enabled under conditions other than those stated above, interrupts may be generated under circumstances otherthan actual buffer misalignment. In these cases, BMINT should generally be masked in the IMR register so that the processor will ignore this interrupt.

BMINT is available when operating auto-buffering mode with continuous transfers, the FIG bit cleared to 0, and external serial clocks or frames.

The BSP0 and BSP1 BMINT bits in the IMR and IFR registers are bits 12 and 13, respectively, (bit 15 is the MSB), and their interrupt vector locations are 070h and 074h, respectively.

Texas Instruments

30	POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

serial ports (continued)

Table 3 provides a comparison of the serial ports available in the '54x devices.

Table 3. Serial Port Configurations for the '54x

| DEVICE | NO.OF STANDARD SERIAL PORTS | NO. OF BSPs (BSP ADDRESS RANGES) | NO. OF TDM SERIAL PORTS |
| --- | --- | --- | --- |
| TMS320C541 TMS320LC541 | 2 | - | - |
| TMS320C542 TMS320LC542 | - | 1 (0800h-0FFFh) | 1 |
| TMS320LC543 | - | 1 (0800h-0FFFh) | 1 |
| TMS320LC545 TMS320LC545A | 1 | 1 (0800h-0FFFh) | - |
| TMS320LC546 TMS320LC546A | 1 | 1 (0800h-0FFFh) | - |
| TMS320LC548 | - | 2(0800h-0FFFh and1800h-1FFFh) | 1 |
| TMS320LC549 TMS320VC549 | - | 2(0800h-0FFFh and1800h-1FFFh) | 1 |

hardware timer

The '54x devices feature a 16-bit timing circuit with a four-bit prescaler. The timer counter is decremented by one at every CLKOUT cycle. Each time the counter decrements to zero, a timer interrupt is generated. The timer can be stopped, restarted, reset, or disabled by specific status bits.

clock generator

The clock generator provides clocks to the '54xdevice, and consists of an internal oscillator and a phase-locked loop (PLL) circuit. The clock generator requires a reference clock input, which can be provided by using a crystal resonator with the internal oscillator, or from an external clock source. The reference clock input is then either divided by two (or by four on the '545A, '546A, '548, and '549) to generate clocks for the '54x device, or the PLL circuit can be used to generate the device clock by multiplying the reference clock frequency by a scale factor, allowing use of a clock source with a lower frequency than that of the CPU.

The PLL is an adaptive circuit that, once synchronized, locks onto and tracks an input clock signal. When the PLL is initially started, it enters a transitional mode during which the PLL acquires lock with the input signal. Once the PLL is locked, it continues to track and maintain synchronization with the input signal. Then, other internal clock circuitry allows the synthesis of new clock frequencies for use as master clock for the '54x device.

Two types of PLL are available: a hardware-programmable PLL and a software-programmable PLL. All '54x devices have the hardware-programmable PLL except the '545A, '546A, '548, and '549, which have the software-programmable PLL. On the hardware-programmable PLL, an external delay must be provided before the device is released from reset in order for the PLL to achieve lock. With the software-programmable PLL, a lock timer is provided to implement this delay automatically. Note that both the hardware- and the software-programmable PLLs require the device to be reset after power up to begin functioning properly.

hardware-programmable PLL

The '54x can use either the internal oscillator or an external frequency source for an input clock. The clock generation mode is determined by the CLKMD1, CLKMD2 and CLKMD3 clock mode pins except on the '545A, the '546A, the '548, and the '549 (see software-programmable PLL description below). Table 4 outlines the selection of the clock mode by these pins. Note that both the hardware- and the software-programmable PLLs require the device to be reset after power up to begin functioning properly.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

31

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

| hardware-programmable PLL (continued) Table 4. Clock Mode Configurations |
| --- |
| MODE-SELECT PINS | CLOCK MODE |
| CLKMD1 | CLKMD2 | CLKMD3 | OPTION it | OPTION 2t |
| 0 | 0 | 0 | PLL x 3 with external source | PLL x 5 with external source |
| 1 | 1 | 0 | PLL x 2 with external source | PLL x 4 with external source |
| 1 | 0 | 0 | PLL x3, internal oscillator enabled | PLL x 5, internal oscillator enabled |
| 0 | 1 | 0 | PLL x 1.5 with external source | PLL x 4.5 with external source |
| 0 | 0 | 1 | Divide-by-two with external source | Divide-by-two with external source |
| 0 | 1 | 1 | Stop modet | Stop modet |
| 1 | 0 | 1 | PLL x 1 with external source | PLL x 1 with external source |
| 1 | 1 | 1 | Divide-by-two, internal oscillator enabled | Divide-by-two, internal oscillator enabled |

t Option: Option 1 or option 2 is selected when ordering the device. t Stop mode: The function of the stop mode is equivalent to that of the power-down mode of IDLE3; however, the IDLE3 instruction is recommended rather than stop mode to realize full power saving, since IDLE3 stops clocks synchronously and can be exited with an interrupt.

software-programmable PLL ('545A, '546A, '548, and '549)

The software-programmable PLL features a high level of flexibility, and includes a clock sealer that provides various clock multiplier ratios, capability to directly enable and disable the PLL, and a PLL lock timer that can be used to delay switching to PLL clocking mode of the device until lock is achieved.

Devices that have a built-in software-programmable PLL can be configured in one of two clock modes:

- PLL mode. The input clock (X2/CLKIN) is multiplied by 1 of 31 possible ratios. These ratios are achieved
using the PLL circuitry.

- DIV (divider) mode. The input clock is divided by 2 or 4. Note that when DIVmode is used, the PLL can be
completely disabled in order to minimize power dissipation.

The software-programmable PLL is controlled using the 16-bit memory-mapped (address 0058h) clock mode register (CLKMD). The CLKMD register is used to define the clock configuration of the PLL clock module. The CLKMD register fields are shown in Figure 7 and described below. Note that upon reset, the CLKMD register is initialized with a predetermined value dependent only upon the state of the CLKMD1 - CLKMD3 pins (see Table 6).

R/WT R = read, W= write twhen in DIV mode (PLLSTATUS is low), PLLMUL, PLLDIV, PLLCOUNT, and PLLON/OFF are don't cares, and their contents are

R/WT

R/WT

R/WT

R/W

R

indeterminate.

Bit #

| 15-12 | 11 | 10-3 | 2 | 1 | 0 |
| --- | --- | --- | --- | --- | --- |
| PLLMUL | PLLDIV | PLLCOUNT | PLLON/OFF | PLLNDIV | PLLSTATUS |

Figure 7. Clock Mode Control Register (CLKMD)

32

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

software-programmable PLL ('545A, '546A, '548, and '549) (continued)

Bits 15-12  PLLMUL. PLL multiplier. Defines the frequency multiplier in conjunction with PLLDIV and PLLNDIV, as shown in Table 5.

Bit 11

Bits 10-3

Bit 2

PLLDIV. PLL divider. Defines the frequency multiplier in conjunction with PLLMUL and PLLNDIV, as shown in Table 5.

- = an integer multiply factor is used.

- = a non-integer multiply factor is used.

PLLCOUNT. PLL counter value. Specifies the number of input clock cycles (in increments of 16 cycles) for the PLL lock timer to count before the PLL begins clocking the processor after the PLL is started. The PLL counter is a down-counter, which is driven by the input clock divided by 16; therefore, for every 16 input clocks, the PLL counter decrements by one.

The PLL counter can be used to ensure that the processor is not clocked until the PLL is locked, so that only valid clock signals are sent to the device.

PLLON/OFF. PLL on/off. Enables or disables the PLL part of the clock generator in conjunction with the PLLNDIV bit. Note that PLLON/OFF and PLLNDIV can both force the PLL to run; when PLLON/OFF is high, the PLL runs independently of the state of PLLNDIV.

| PLLON/OFF | PLLNDIV | PLL STATE |
| --- | --- | --- |
| 0 | 0 | Off |
| 1 | 0 | On |
| 0 | 1 | On |
| 1 | 1 | On |

Bit 1

BitO

PLLNDIV. PLL clock generator select. Determines whether the clock generator works in PLL mode or in divider (DIV) mode, thereby defining the frequency multiplier in conjunction with PLLMUL and PLLDIV.

- = Divider mode is used

- = PLL mode is used

PLLSTATUS. PLL status. Indicates the mode in which the clock generator is operating.

- = DIV mode

- = PLL mode

Table 5. PLL Multiplier Ratio as a Function of PLLNDIV, PLLDIV, and PLLMUL

| PLLNDIV | PLLDIV | PLLMUL | MULTIPLIERt |
| --- | --- | --- | --- |
| 0 | x | 0-14 | 0.5 |
| 0 | x | 15 | 0.25 |
| 1 | 0 | 0-14 | PLLMUL+ 1 |
| 1 | 0 | 15 | Reserved |
| 1 | 1 | 0 or even | (PLLMUL+ 1) 4- 2 |
| 1 | 1 | odd | PLLMUL -h 4 |

t CLKOUT = CLKIN x multiplier

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

33

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

software-programmable PLL ('545A, '546A, '548, and '549) (continued)

Immediately following reset, the clock mode is determined by the values of the three external pins: CLKMD1, CLKMD2, and CLKMD3. The modes corresponding to the CLKMD pins are shown in Table 6.

|  |  | Table 6. | Clock Mode Settings at | Reset |
| --- | --- | --- | --- | --- |
| CLKMD1 | CLKMD2 | CLKMD3 |  | CLKMD REGISTER RESET VALUE |  | CLOCK MODE |
| 0 | 0 | 0 |  | 0000h |  | Divide-by-two, with external source |
| 0 | 0 | 1 |  | 1000h |  | Divide-by-two, with external source |
| 0 | 1 | 0 |  | 2000h |  | Divide-by-two, with external source |
| 1 | 0 | 0 |  | 4000h |  | Divide-by-two, internal oscillator enabled |
| 1 | 1 | 0 |  | 6000h |  | Divide-by-two, with external source |
| 1 | 1 | 1 |  | 7000h |  | Divide-by-two, internal oscillator enabledt |
| 1 | 0 | 1 |  | 0007h |  | PLL x 1 with external source |
| 0 | 1 | 1 |  | — |  | Stop mode |

t Reserved mode ('549 only). Do not use in normal operation.

Following reset, the software-programmable PLL can be programmed to any configuration desired, as described above. Note that when the PLL x 1 with external source option (CLKMD[1-3]=101) is selected during reset, the internal PLL lock-count timer is not active; therefore, the system must delay releasing reset in order to allow for the PLL lock-time delay. Also, note that both the hardware- and the software-programmable PLLs require the device to be reset after power up to begin functioning properly.

programming considerations when using the software-programmable PLL

The software-programmable PLL offers many different options in startup configurations, operating modes, and power-saving features. Programming considerations and several software examples are presented here to illustrate the proper use of the software-programmable PLL at start-up, when switching between different clocking modes, and before and after IDLE1/IDLE2/IDLE3 instruction execution.

use of the PLLCOUNT programmable lock timer

During the lockup period, the PLL should not be used to clock the '54x. The PLLCOUNT programmable lock timer provides a convenient method of automatically delaying clocking of the device by the PLL until lock is achieved.

The PLL lock timer is a counter, loaded from the PLLCOUNT field in the CLKMD register, that decrements from its preset value to 0. The timer can be preset to any value from 0 to 255, and its input clock is CLKIN divided by 16. The resulting lockup delay can therefore be set from 0 to 255 x 16 CLKIN cycles.

The lock timer is activated when the clock generator operating mode is switched from DIV to PLL (see the section describing switching from DIV mode to PLL mode). During the lockup period, the clock generator continues to operate in DIV mode; after the PLL lock timer has decremented to zero, the PLL begins clocking the '54x.

Accordingly, the value loaded into PLLCOUNT is chosen based on the following relationship:

PLLCOUNT > Lockup Time/(16 xtCLKIN)

where tcLKlN 's tne inPut reference clock period and lockup time is the required PLL lockup time as shown in Figure 8.

34

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

use of the PLLCOUNT programmable lock timer (continued)

0)

F

Q.

3

60 55 50 45 40 35 30 25 20 15 10 5 0

|  |  |  |  |  |  | /59 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | / |  |  |  |
|  |  |  |  | 44 | / |  |  |  |
|  |  |  |  | / |  |  |  |  |
|  |  |  |  | / |  |  |  | 35 |
|  |  |  |  |  |  | '54Ј | Only |  |
| 23 |  |  | / |  |  |  |  | 29 |
| + |  | 22, | / | -* |  | 24 |  |  |
|  | 17 |  | ——— | 19 |  |  |  |  |
|  | * |  |  |  |  |  |  |  |

2.5  10   20   30   40   50   60   70   80   100

CLKOUT Frequency (MHz) Figure 8. PLL Lockup Time Versus CLKOUT Frequency

switching from DIV mode to PLL mode

Several circumstances may require switching from DIV mode to PLL mode; however, note that if the PLL is not locked when switching from DIV mode to PLL mode, the PLL lockup time delay must be observed before the mode switch occurs to ensure that only proper clock signals are sent to the device. It is, therefore, important to know whether or not the PLL is locked when switching operating modes.

The PLL is unlocked on power-up, after changing the PLLMUL or PLLDIV values, after turning off the PLL (PLLON/OFF = 0), or after loss of input reference clock. Once locked, the PLL remains locked even in DIV mode as long as the PLL had been previously locked and has not been turned off (PLLON/OFF stays 1), and the PLLMUL and PLLDIV values have not been changed since the PLL was locked.

Switching from DIV mode to PLL mode (setting PLLNDIVto 1) activates the PLLCOUNT programmable lock timer (when PLLCOUNT is preloaded with a non-zero value), and this can be used to provide a convenient method for implementing the lockup time delay. The PLLCOUNT lock timer feature should be used in the situations described above, where the PLL is unlocked unless a reset delay is used to implement the lockup delay, or the PLL is not used.

Switching from DIV mode to PLL mode is accomplished by loading the CLKMD register. The following procedure describes switching from DIV mode to PLL mode when the PLL is not locked. When performing this mode switch with the PLL already locked, the effect is the same as when switching from PLL to DIV mode, but in the reverse order. In this case, the delays of when the new clock mode takes effect are the same.

When switching from DIV to PLL mode with the PLL unlocked, orwhenthe mode change will result in unlocked operation, the PLLMUL[3-0], PLLDIV, and PLLNDIV bits are set to select the desired frequency multiplier as described in Table 5, and the PLLCOUNT[7-0] bits are set to select the required lockup time delay. Note that PLLMUL, PLLDIV, PLLCOUNT, and PLLON/OFF can only be modified when in DIV mode.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

35

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

switching from DIV mode to PLL mode (continued)

Once the PLLNDIVbit is set, the PLLCOUNT timer begins being decremented from its preset value. When the PLLCOUNT timer reaches zero, the switch to PLL mode takes effect after six CLKIN cycles plus 3.5 PLL cycles (CLKOUT frequency). When the switch to PLL mode is completed, the PLLSTATUS bit in the CLKMD register is read as 1. Note that during the PLL lockup period, the '54x continues operating in DIV mode.

The following software example shows an instruction that can be used to switch from DIV mode to PLL x 3, with a CLKIN frequency of 13 MHz and PLLCOUNT = 41 (decimal).

STM

#0010000101001111b, CLKMD

switching clock mode from PLL to DIV

When switching from PLL mode to DIV mode, the PLLCOUNT delay does not occur, and the switch between the two modes takes place after a short transition delay.

The switch from PLL mode to DIV mode is also accomplished by loading the CLKMD register. The PLLNDIV bit is set to 0, selecting DIV mode, and the PLLMUL bits are set to select the desired frequency multiplier as shown in Table 5.

The switch to DIV mode takes effect in 6 CLKIN cycles plus 3.5 PLL cycles (CLKOUT frequency) for all PLLMUL values except 1111b. With a PLLMUL value of 1111b, the switch to DIV mode takes effect in 12 CLKIN cycles plus 3.5 PLL cycles (CLKOUT frequency). When the switch to DIV mode is completed, the PLLSTATUS bit in the CLKMD register is read as 0.

The following software example shows a code sequence that can be used to switch from PLL x 3 to divide-by-two mode. Note that the PLLSTATUS bit is polled to determine when the switch to DIV mode has taken effect, and then the STM instruction is used to turn off the PLL at this point.

| STM | #0b, CLKMD |
| --- | --- |
| LDM | CLKMD, A |
| AND | #01 b, A |
| BC | TstStatu, ANEQ |
| STM | #0b, CLKMD |

TstStatu:

;switch to DIV mode ;poll STATUS bit

;reset PLLONJDFF when STATUS ;is DIV mode

switching mode from one PLL multiplier to another

When switching from one PLL multiplier ratio to another is required, the clock generator must be switched from PLL mode to DIV mode before selecting the new multiplier ratio; switching directly from one PLL multiplier ratio to another is not supported.

In order to switch from one PLL multiplier ratio to another, the following steps must be followed:

- Set the PLLNDIV bit to 0, selecting DIV mode.

- Poll the PLLSTATUS bit until a 0 is obtained, indicating that DIV mode is enabled and that PLLMUL, PLLDIV,
and PLLCOUNT can be updated.

- Modify the CLKMD register to set the PLLMUL[3-0], PLLDIV, and PLLNDIV bits to the desired frequency
multiplier as defined in Table 5, and the PLLCOUNT[7-0] bits to the required lock-up time.

When the PLLNDIV bit is set to one in step three, the PLLCOUNT timer begins decrementing from its preset value. Once the PLLCOUNT timer reaches zero, the new PLL mode takes effect after six CLKIN cycles plus 3.5 PLL cycles (CLKOUT frequency).

36

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

switching mode from one PLL multiplier to another (continued)

Also, note that a direct switch between divide-by-two mode and divide-by-four mode is not possible. To switch between these two modes, the clock generator must first be set to PLL mode with an integer-only (non-fractional) multiplier ratio, and then set back to DIV mode in the desired divider configuration (see previous sections for details on switching between DIV and PLL modes).

The following software example shows a code sequence that can be used to switch clock mode from PLL x X

to PLL x 1. ~

STM	#0b, CLKMD	;switch to DIV mode

TstStatu:      LDM	CLKMD, A

AND	#01 b, A	;poll STATUS bit

BC	TstStatu, ANEQ

STM	#0000001111101111b, CLKMD         ;switch to PLL x 1 mode

programmable clock generator operation immediately following reset

Immediately following reset, the operating mode of the clock generator is determined only on the basis of the CLKMD1/2/3 pin state as described in Table 6. All but two of these operating modes are 'divide-by-two with external source'. Switching from divide-by-two to a PLL mode can easily be accomplished by changing the CLKMD register contents. Note that if use of the internal oscillator is desired, either the 100 or the 111 state of the CLKMD1-CLKMD3 pins must be selected at reset (as shown in Table 6) since the internal oscillator cannot be programmed through software.

The following software example shows an instruction that can be used to switch from divide-by-two mode to the PLL x 3 mode.

STM       #0010000101001111b, CLKMD considerations when using IDLE1/IDLE2/IDLE3

When using one of the IDLE instructions to reduce power requirements, proper management of the PLL is important. The clock generator consumes the least power when operating in DIV mode with the PLL disabled. Therefore, if power dissipation is a significant consideration, it is desirable to switch from PLL to DIV mode, and disable the PLL, before executing the IDLE1/IDLE2/IDLE3 instructions. This is accomplished as explained above in the section describing switching clock mode from PLL to DIV. After waking up from IDLE1/IDLE2/IDLE3, the clock generator can be reprogrammed to PLL mode as explained above in the section describing switching clock mode from DIV to PLL.

Note that when the PLL is stopped during an IDLE state, and the '54xdevice is restarted and the clock generator is switched back to PLL mode, the PLL lockup delay occurs in the same manner as in a normal device startup. Therefore, in this case, the lockup delay must also be accounted for, either externally or by using the PLL lockup counter timer.

The following software example illustrates a code sequence that switches the clock generator from PLL x 3 mode to divide-by-two mode, turns off the PLL, and enters IDLE3. After waking up from IDLE3, the clock generator is switched back from DIV mode to PLL x 3 mode using a single STM instruction, with a PLLCOUNT of 64 (decimal) used for the lock timer value.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443	37

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

considerations when using IDLE1/IDLE2/IDLE3 (continued)

|  | STM | #0b, CLKMD |
| --- | --- | --- |
| TstStatu: | LDM | CLKMD,A |
|  | AND | #01 b, A |
|  | BC | TstStatu, ANEQ |
|  | STM | #0b, CLKMD |

;switch to DIV mode

;poll STATUS bit

;reset PLLONJDFF when STATUS ;is DIV mode IDLE3

(After IDLE3 wake-up - switch the PLL from DIV mode to PLL x 3 mode)

STM       #0010001000000111b, CLKMD        ;PLLCOUNT = 64 (decimal) PLL considerations when using the bootloader

The ROM on the '545A and '546A contains a bootloader program that can be used to load programs into RAM for execution following reset. When using this bootloader with the software-programmable PLL, several considerations are important for proper system operation.

On the '545A and '546A, for compatibility, the bootloader configures the PLL to the same mode as would have resulted if the same CLKMD1-3 input bits had been provided to the option-1 or option-2 hardware-programmable PLL (see Table 4), according to whether the '545A or'546A is an option-1 or option-2 device. Once the bootloader program has finished executing, and control is transferred to the user's program, the PLL can be reprogrammed to any desired configuration.

Texas Instruments

38	POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

memory-mapped registers

Most '54xdevices have 26 (except '548 and '549 have 27) memory-mapped CPU registers, which are mapped into data memory located at addresses 0h to 1Fh. Each of these devices also has a set of memory-mapped registers associated with peripherals. Table 7 gives a list of CPU memory-mapped registers (MMR) common to all '54xdevices. Table 8 shows additional peripheral MMRs associated with the '541 devices, Table 9 shows those associated with the '545/'546 devices, Table 10 shows those associated with the '542/'543 devices, and Table 11 shows those associated with the '548/'549 devices.

| Table | 7. Core Processor Memory-Mapped Registers |
| --- | --- |
| NAME |  | ADDRESS |  | DESCRIPTION |
|  |  | DEC | HEX |  |  |
| IMR |  | 0 | 0 |  | Interrupt mask register |
| IFR |  | 1 | 1 |  | Interrupt flag register |
| - |  | 2-5 | 2-5 |  | Reserved for testing |
| ST0 |  | 6 | 6 |  | Status register 0 |
| ST1 |  | 7 | 7 |  | Status register 1 |
| AL |  | 8 | 8 |  | Accumulator A low word (15-0) |
| AH |  | 9 | 9 |  | Accumulator A high word (31-16) |
| AG |  | 10 | A |  | Accumulator A guard bits (39-32) |
| BL |  | 11 | B |  | Accumulator B low word (15-0) |
| BH |  | 12 | C |  | Accumulator B high word (31-16) |
| BG |  | 13 | D |  | Accumulator B guard bits (39-32) |
| TREG |  | 14 | E |  | Temporary register |
| TRN |  | 15 | F |  | Transition register |
| AR0 |  | 16 | 10 |  | Auxiliary register 0 |
| AR1 |  | 17 | 11 |  | Auxiliary register 1 |
| AR2 |  | 18 | 12 |  | Auxiliary register 2 |
| AR3 |  | 19 | 13 |  | Auxiliary register 3 |
| AR4 |  | 20 | 14 |  | Auxiliary register 4 |
| AR5 |  | 21 | 15 |  | Auxiliary register 5 |
| AR6 |  | 22 | 16 |  | Auxiliary register 6 |
| AR7 |  | 23 | 17 |  | Auxiliary register 7 |
| SP |  | 24 | 18 |  | Stack pointer register |
| BK |  | 25 | 19 |  | Circular buffer size register |
| BRC |  | 26 | 1A |  | Block-repeat counter |
| RSA |  | 27 | 1B |  | Block-repeat start address |
| REA |  | 28 | 1C |  | Block-repeat end address |
| PMST |  | 29 | 1D |  | Processor mode status (PMST) register |
| XPC |  | 30 | 1E |  | Extended program counter ('548 and '549 only) |
| - |  | 31 | 1F |  | Reserved |

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

39

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

memory-mapped registers (continued)

Table 8. Peripheral Memory-Mapped Registers ('541 Only)

| NAME | ADDRESS | DESCRIPTION |
| --- | --- | --- |
|  | DEC | HEX |  |
| DRR0 | 32 | 20 | Serial port 0 data-receive register |
| DXR0 | 33 | 21 | Serial port 0 data-transmit register |
| SPC0 | 34 | 22 | Serial port 0 control register |
| — | 35 | 23 | Reserved |
| TIM | 36 | 24 | Timer register |
| PRD | 37 | 25 | Timer period register |
| TCR | 38 | 26 | Timer control register |
| — | 39 | 27 | Reserved |
| SWWSR | 40 | 28 | S/W wait-state register |
| BSCR | 41 | 29 | Bank-switching control register |
| — | 42-47 | 2A-2F | Reserved |
| DRR1 | 48 | 30 | Serial port 1 data-receive register |
| DXR1 | 49 | 31 | Serial port 1 data-transmit register |
| SPC1 | 50 | 32 | Serial port 1 control register |
| — | 51 | 33 | Reserved |
| — | 52-95 | 34-5 F | Reserved |

40

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

memory-mapped registers (continued)

| Table | J. Peripheral | Memory-Mapped Registers ('545 and '546 Only)t |
| --- | --- | --- |
| NAME | ADDRESS | DESCRIPTION |
|  | DEC | HEX |  |
| BDRR | 32 | 20 | BSP data-receive register |
| BDXR | 33 | 21 | BSP data-transmit register |
| BSPC | 34 | 22 | BSP serial-port control register |
| BSPCE | 35 | 23 | BSP control extension register |
| TIM | 36 | 24 | Timer register |
| PRD | 37 | 25 | Timer period counter |
| TCR | 38 | 26 | Timer control register |
| — | 39 | 27 | Reserved |
| SWWSR | 40 | 28 | External bus S/W wait-state register |
| BSCR | 41 | 29 | External bus bank-switching control register |
| — | 42-43 | 2A-2B | Reserved |
| HPIC | 44 | 2C | HPI control register! |
| — | 45-47 | 2D-2F | Reserved |
| DRR | 48 | 30 | Data-receive register |
| DXR | 49 | 31 | Data-transmit register |
| SPC | 50 | 32 | Serial-port control register |
| — | 51 -55 | 33-37 | Reserved |
| AXR | 56 | 38 | BSP ABU transmit-address register |
| BKX | 57 | 39 | BSP ABU transmit-buffer-size register |
| ARR | 58 | 3A | BSP ABU receive-address register |
| BKR | 59 | 3B | BSP ABU receive-buffer-size register |

t BSP = Buffered serial port ABU = Auto-buffering unit t Host-port interface (HPI) on 'LC545 only

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

41

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

memory-mapped registers (continued)

| Table 10. | Peripheral Memory-Mapped Registers ('542 and '543 Only)t |
| --- | --- |
| NAME | ADDRESS | DESCRIPTION |
|  | DEC | HEX |  |
| BDRR | 32 | 20 | BSP data-receive register |
| BDXR | 33 | 21 | BSP data-transmit register |
| BSPC | 34 | 22 | BSP serial-port control register |
| BSPCE | 35 | 23 | BSP control extension register |
| TIM | 36 | 24 | Timer register |
| PRD | 37 | 25 | Timer period counter |
| TCR | 38 | 26 | Timer control register |
| — | 39 | 27 | Reserved |
| SWWSR | 40 | 28 | External bus S/W wait-state register |
| BSCR | 41 | 29 | External bus bank-switching control register |
| — | 42-43 | 2A-2B | Reserved |
| HPIC | 44 | 2C | HPI control register! |
| — | 45-47 | 2D-2F | Reserved |
| TRCV | 48 | 30 | TDM data-receive register |
| TDXR | 49 | 31 | TDM data-transmit register |
| TSPC | 50 | 32 | TDM serial-port control register |
| TCSR | 51 | 33 | TDM channel-select register |
| TRTA | 52 | 34 | TDM receive/transmit register |
| TRAD | 53 | 35 | TDM receive address register |
| — | 54-55 | 36-37 | Reserved |
| AXR | 56 | 38 | BSP ABU transmit-address register |
| BKX | 57 | 39 | BSP ABU transmit-buffer-size register |
| ARR | 58 | 3A | BSP ABU receive-address register |
| BKR | 59 | 3B | BSP ABU receive-buffer-size register |

t BSP = Buffered serial port TDM = Time-division multiplexed ABU = Auto-buffering unit

t Host-port interface (HPI) on '542 only

42

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

memory-mapped registers (continued)

Table 11. Peripheral Memory-Mapped Registers ('548 and '549 Only)t

| NAME | ADDRESS | DESCRIPTION |
| --- | --- | --- |
|  | DEC | HEX |  |
| BDRR0 | 32 | 20 | BSP 0 data-receive register |
| BDXR0 | 33 | 21 | BSP 0 data-transmit register |
| BSPC0 | 34 | 22 | BSP 0 control register |
| BSPCE0 | 35 | 23 | BSP 0 control extension register |
| TIM | 36 | 24 | Timer count register |
| PRD | 37 | 25 | Timer period register |
| TCR | 38 | 26 | Timer control register |
| — | 39 | 27 | Reserved |
| SWWSR | 40 | 28 | External interface software wait-state register |
| BSCR | 41 | 29 | External interface bank-switching control register |
| — | 42 | 2A | Reserved |
| — | 43 | 2B | Reserved |
| HPIC | 44 | 2C | HPI control register |
| — | 45-47 | 2D-2F | Reserved |
| TRCV | 48 | 30 | TDM port data-receive register |
| TDXR | 49 | 31 | TDM port data-transmit register |
| TSPC | 50 | 32 | TDM serial port control register |
| TCSR | 51 | 33 | TDM channel-select register |
| TRTA | 52 | 34 | TDM receive/transmit register |
| TRAD | 53 | 35 | TDM receive /address register |
| — | 54-55 | 36-37 | Reserved |
| AXR0 | 56 | 38 | ABU 0 transmit-address register |
| BKX0 | 57 | 39 | ABU 0 transmit-buffer-size register |
| ARR0 | 58 | 3A | ABU 0 receive-address register |
| BKR0 | 59 | 3B | ABU 0 receive-buffer-size register |
| AXR1 | 60 | 3C | ABU 1 transmit-address register |
| BKX1 | 61 | 3D | ABU 1 transmit-buffer-size register |
| ARR1 | 62 | 3E | ABU 1 receive-address register |
| BKR1 | 63 | 3F | ABU 1 receive-buffer-size register |
| BDRR1 | 64 | 40 | BSP 1 data-receive register |
| BDXR1 | 65 | 41 | BSP 1 data-transmit register |
| BSPC1 | 66 | 42 | BSP 1 control register |
| BSPCE1 | 67 | 43 | BSP 1 control extension register |
| — | 68-87 | 44-57 | Reserved |
| CLKMD | 88 | 58 | Clock mode register |
| — | 89-95 | 59-5F | Reserved |

t BSP = Buffered serial port ABU = Auto-buffering unit HPI = Host-port interface

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

43

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

status registers (ST0, ST1)

The status registers, ST0 and ST1, contain the status of the various conditions and modes forthe '54x devices. ST0 contains the flags (OV, C, and TC) produced by arithmetic operations and bit manipulations in addition to the data page pointer (DP) and the auxiliary register pointer (ARP) fields. ST1 contains the various modes and instructions that the processor operates on and executes.

accumulators (AL, AH, AG, and BL, BH, BG)

The '54x devices have two 40-bit accumulators: accumulator A and accumulator B. Each accumulator is memory-mapped and partitioned into accumulator low-word (AL, BL), accumulator high-word (AH, BH), and accumulator guard bits (AG, BG).

39	32 31	16 15	0

| AG (BG) | AH (BH) | AL (BL) |
| --- | --- | --- |

auxiliary registers (AR0-AR7)

The eight 16-bit auxiliary registers (AR0-AR7) can be accessed by the CALU and modified by the auxiliary register arithmetic units (ARAUs). The primary function of the auxiliary registers is generating 16-bit addresses for data space. However, these registers also can act as general-purpose registers or counters.

temporary register (TREG)

The TREG is used to hold one of the multiplicands for multiply and multiply/accumulate instructions. It can hold a dynamic (execution-time programmable) shift count for instructions with shift operation such as ADD, LD, and SUB instructions. It also can hold a dynamic bit address forthe BITT instruction. The EXP instruction stores the exponent value computed into the TREG, while the NORM instruction uses the TREG value to normalize the number. For ACS operation of Viterbi decoding, TREG holds branch metrics used by the DADST and DSADT instructions.

transition register (TRN)

The TRN is a 16-bit register that is used to hold the transition decision forthe path to new metrics to perform the Viterbi algorithm. The CMPS (compare, select, max, and store) instruction updates the contents of the TRN based on the comparison between the accumulator high word and the accumulator low word.

stack-pointer register (SP)

The SP is a 16-bit register that contains the address at the top of the system. The SP always points to the last element pushed onto the stack. The stack is manipulated by interrupts, traps, calls, returns, and the PUSHD, PSHM, POPD, and POPM instructions. Pushes and pops of the stack predecrement and postincrement, respectively, all 16 bits of the SP.

circular-buffer-size register (BK)

The 16-bit BK is used by the ARAUs in circular addressing to specify the data block size. block repeat registers (BRC, RSA, REA)

The block-repeat counter (BRC) is a 16-bit register used to specify the number of times a block of code is to be repeated when performing a block repeat. The block-repeat start address (RSA) is a 16-bit register containing the starting address of the block of program memory to be repeated when operating in the repeat mode. The 16-bit block repeat-end address (REA) contains the ending address if the block of program memory is to be repeated when operating in the repeat mode.

interrupt registers (IMR, IFR)

The interrupt-mask register (IMR) is used to mask off specific interrupts individually at required times. The interrupt-flag register (IFR) indicates the current status of the interrupts.

Texas Instruments

44	POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

processor-mode status register (PMST)

The processor-mode status register (PMST) controls memory configurations of the '54x devices.

interrupts

Vector-relative locations and priorities for all internal and external interrupts are shown in Table 12.

|  | Table 12 | '54x Interrupt Locations and Priorities |
| --- | --- | --- |
| NAME | LOCATION | PRIORITY | FUNCTION |
|  | DECIMAL | HEX |  |  |
| RS, SINTR | 0 | 00 | 1 | Reset (Hardware and software reset) |
| NMI, SINT16 | 4 | 04 | 2 | Nonmaskable interrupt |
| SINT17 | 8 | 08 | - | Software interrupt #17 |
| SINT18 | 12 | 0C | - | Software interrupt #18 |
| SINT19 | 16 | 10 | - | Software interrupt #19 |
| SINT20 | 20 | 14 | - | Software interrupt #20 |
| SINT21 | 24 | 18 | - | Software interrupt #21 |
| SINT22 | 28 | 1C | - | Software interrupt #22 |
| SINT23 | 32 | 20 | - | Software interrupt #23 |
| SINT24 | 36 | 24 | - | Software interrupt #24 |
| SINT25 | 40 | 28 | - | Software interrupt #25 |
| SINT26 | 44 | 2C | - | Software interrupt #26 |
| SINT27 | 48 | 30 | - | Software interrupt #27 |
| SINT28 | 52 | 34 | - | Software interrupt #28 |
| SINT29 | 56 | 38 | - | Software interrupt #29 |
| SINT30 | 60 | 3C | - | Software interrupt #30 |
| INTO, SINT0 | 64 | 40 | 3 | External user interrupt #0 |
| INT1, SINT1 | 68 | 44 | 4 | External user interrupt #1 |
| INT2, SINT2 | 72 | 48 | 5 | External user interrupt #2 |
| TINT, SINT3 | 76 | 4C | 6 | External timer interrupt |
| BRINT0, SINT4 | 80 | 50 | 7 | BSP #0 receive interruptt |
| BXINT0, SINT5 | 84 | 54 | 8 | BSP #0 transmit interruptt |
| TRINT, SINT6 | 88 | 58 | 9 | TDM receive interruptt |
| TRINT, SINT7 | 92 | 5C | 10 | TDM transmit interruptt |
| INT3, SINT8 | 96 | 60 | 11 | External user interrupt #3 |
| HINT, SINT9 | 100 | 64§ | 12 | HPI interrupt ('542, '545, '548, '549 only) |
| BRINT1.SINT10 | 104 | 68§ | 13 | BSP #1 receive interrupt ('548, '549 only) |
| BXINT1, SINT11 | 108 | 6C§ | 14 | BSP #1 transmit interrupt ('548, '549 only) |
| BMINT0, SINT12 | 112 | 70§ | 15 | BSP #0 misalignment detection interrupt ('549 only) |
| BMINT1.SINT13 | 116 | 74§ | 16 | BSP #1 misalignment detection interrupt ('549 only) |
| — | 120-127 | 78-7F§ | - | Reserved |

t On '541 devices, these interrupt locations are serial port 0 interrupts (RINT0/XINT0). t On '541, '545, and '546 devices, these interrupt locations are serial port 1 interrupts (RINT1/XINT1).

§ On'541, '543, and'546 devices, interrupt locations 64h-7Fh are reserved. On '542 and'545 devices, interrupt locations 68h-7Fh are reserved. On '548 devices, interrupt locations 70h - 7Fh are reserved.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

45

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

interrupts (continued)

The IFR and IMR registers are laid out as shown in Figure 9.

15-14	13	12	11	10	9	8	7	6

|  RESERVED   | BMINT1   | BMINT0  | BXINT1   | BRINT1   |    HINT     |    INT3     |   TXNT    |   TRNT    | BXINT0   | TRINT0   |    TINT     |    INT2     |    INT1     |    INT0

Figure 9. IFR and IMR Registers

instruction set summary

This section summarizes the syntax used by the mnemonic assembler and the associated instruction set opcodes for the '54x DSP devices (see Table 13). For detailed information on instruction operation, see the TMS320C54xDSP Reference Set, Volume 2: Mnemonic Instruction Set (literature number SPRU172); and for detailed information on the algebraic assembler, see the TMS320C54x DSP Reference Set, Volume 3: Algebraic Instruction Set (literature number SPRU179).

Texas Instruments

46	POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

instruction set summary (continued)

Table 13. '54x Instruction Set Opcodes

| MNEMONIC SYNTAX | DESCRIPTION | WORDS/ CYCLESt | MSB | OPCODE | LSB |
| --- | --- | --- | --- | --- | --- |
|  | ARITHMETIC INSTRUCTIONS |  |  |  |  |  |
| ABDST Xmem, Ymem | Absolute distance | 1/1 | 1110 | 0011 | XXXX | YYYY |
| ABS src[, dst] | Absolute value of ACC | 1/1 | 1111 | 01SD | 1000 | 0101 |
| ADD Smem, src | Add operand to ACC | 1/1 | 0000 | 000S | IAAA | AAAA |
| ADD Smem, TS, src | Add (shifted by TREG[5:0]) operand to ACC | 1/1 | 0000 | 01 0S | IAAA | AAAA |
| ADD Smem, 16, src[, dst] | Add (shifted by 16 bits) operand to ACC | 1/1 | 0011 | 11SD | IAAA | AAAA |
| ADD Smem [, SHIFT], src [, dst] | Add shifted operand to ACC (2-word opcode) | 2/2 | 0110 0000 | 1111 11SD | IAAA 000S | AAAA HIFT |
| ADD Xmem, SHFT, src | Add shifted operand to ACC | 1/1 | 1001 | 000S | XXXX | SHFT |
| ADD Xmem, Ymem, dst | Add dual operands, shift result by 16 | 1/1 | 1010 | 000 D | XXXX | YYYY |
| ADD #lk[, SHFT], src [, dst] | Add shifted long-immediate value to ACC | 2/2 | 1111 | 00SD | 0000 | SHFT |
| ADD #lk, 16, src[, dst] | Add (shifted by 16 bits) long-immediate to ACC | 2/2 | 1111 | 00SD | 0110 | 0000 |
| ADD src [, SHIFT], [, dst] | Add ACC(s) (A/B), then shift result | 1/1 | 1111 | 01SD | 000S | HIFT |
| ADD src, ASM [, cfef] | Add ACC(s) (A/B), then shift result by ASM value | 1/1 | 1111 | 01SD | 1000 | 0000 |
| ADDC Smem, src | Add to accumulator with carry | 1/1 | 0000 | 011S | IAAA | AAAA |
| ADDM #//c, Smem | Add long-immediate value to memory | 2/2 | 0110 | 1011 | IAAA | AAAA |
| ADDS Smem, src | Add to ACC with sign-extension suppressed | 1/1 | 0000 | 001S | IAAA | AAAA |
| DADD Lmem, src[, dst] | Double/dual add to accumulator | 1/1 | 0101 | 00SD | IAAA | AAAA |
| DADST Lmem, dst | Double/dual add/subtract of T, long operand | 1/1 | 0101 | 101D | IAAA | AAAA |
| DELAY Smem | Memory delay | 1/1 | 0100 | 1101 | IAAA | AAAA |
| DRSUB Lmem, src | Double/dual 16-bit subtract from long word | 1/1 | 0101 | 100S | IAAA | AAAA |
| DSADT Lmem, dst | Double/dual, subtract/add of T, long operand | 1/1 | 0101 | 111D | IAAA | AAAA |
| DSUB Lmem, src | Double-precision/dual 16-bit subtract from ACC | 1/1 | 0101 | 01 0S | IAAA | AAAA |
| DSUBT /.mem, cfef | Double/dual, subtract/subtract of T, long operand | 1/1 | 0101 | 110D | IAAA | AAAA |
| EXP src | Accumulator exponent | 1/1 | 1111 | 01 0S | 1000 | 1110 |
| FIRS Xmem, Ymem, pmad | Symmetrical finite impulse response filter | 2/3 | 1110 | 0000 | XXXX | YYYY |
| LMS Xmem, Ymem | Least mean square | 1/1 | 1110 | 0001 | XXXX | YYYY |
| MAC[R] Smem, src | Multiply by TREG, add to ACC, round if specified | 1/1 | 0010 | 10RS | IAAA | AAAA |
| MAC[R] Xmem, ymem, src[, dst] | Multiply dual, add to ACC, round if specified | 1/1 | 1011 | 0RSD | XXXX | YYYY |
| MAC #//e, src[, dst] | Multiply TREG by long-immediate, add to ACC | 2/2 | 1111 | 00SD | 0110 | 0111 |
| MAC Smem, #//e, src[, dst] | Multiply by long-immediate value, add to ACC | 2/2 | 0110 | 01SD | IAAA | AAAA |
| MACA[R] Smem [, B ] | Multiply by ACCA, add to ACCB [round] | 1/1 | 0011 | 01R1 | IAAA | AAAA |
| MACA[R] T, src[, dst] | Multiply TREG by ACCA, add to ACC [round] | 1/1 | 1111 | 01SD | 1000 | 100R |
| MACD Smem, pmad, src | Multiply by program memory, accumulate/delay | 2/3 | 0111 | 101S | IAAA | AAAA |
| MACP Smem, pmad, src | Multiply by program memory, then accumulate | 2/3 | 0111 | 100S | IAAA | AAAA |
| MACSU Xmem, Ymem, src | Multiply signed by unsigned, then accumulate | 1/1 | 1010 | 011S | XXXX | YYYY |
| MAS[R] Smem, src | Multiply by T, subtract from ACC [round] | 1/1 | 0010 | 11RS | IAAA | AAAA |

t Values for words and cycles assume the use of DARAM for data. Add one word and one cycle when using long-offset indirect addressing or

absolute addressing with a single data-memory operand. t Delayed Instruction § Condition true 11 Condition false

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

47

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

instruction set summary (continued)

Table 13. '54x Instruction Set Opcodes (Continued)

| MNEMONIC SYNTAX | DESCRIPTION | WORDS/ CYCLESt | MSB | OPCODE | LSB |
| --- | --- | --- | --- | --- | --- |
|  | ARITHMETIC INSTRUCTIONS (CONTINUED) |  |  |  |  |
| MAS[R] Xmem, Ymem, src[, dst] | Multiply dual, subtract from ACC [round] | 1/1 | 1011 | 1RSD | XXXX | YYYY |
| MASA Smem [, B ] | Multiply operand by ACCA, subtract from ACCB | 1/1 | 0011 | 0011 | IAAA | AAAA |
| MASA[R] T, src[, dst] | Multiply ACCA by T, subtract from ACC [round] | 1/1 | 1111 | 01SD | 1000 | 101R |
| MAX dst | Accumulator maximum | 1/1 | 1111 | 010D | 1000 | 0110 |
| MIN dst | Accumulator minimum | 1/1 | 1111 | 010D | 1000 | 0111 |
| MPY[R] Smem, dst | Multiply TREG by operand, round if specified | 1/1 | 0010 | 00RD | IAAA | AAAA |
| MPY Xmem, Ymem, dst | Multiply dual data-memory operands | 1/1 | 1010 | 010D | XXXX | YYYY |
| MPY Smem, #lk, dst | Multiply operand by long-immediate operand | 2/2 | 0110 | 001D | IAAA | AAAA |
| MPY #lk, dst | Multiply TREG value by long-immediate operand | 2/2 | 1111 | 000D | 0110 | 0110 |
| MPYA Smem | Multiply single data-memory operand by ACCA | 1/1 | 0011 | 0001 | IAAA | AAAA |
| MPYA dst | Multiply TREG value by ACCA | 1/1 | 1111 | 010D | 1000 | 1100 |
| MPYU Smem, dst | Multiply unsigned | 1/1 | 0010 | 010D | IAAA | AAAA |
| NEG src[, dst] | Negate accumulator | 1/1 | 1111 | 01 SD | 1000 | 0100 |
| NORM src[,dst] | Normalize | 1/1 | 1111 | 01 SD | 1000 | 1111 |
| POLY Smem | Evaluate polynomial | 1/1 | 0011 | 0110 | IAAA | AAAA |
| RND src[, dst] | Round accumulator | 1/1 | 1111 | 01 SD | 1001 | 1111 |
| SAT src | Saturate accumulator | 1/1 | 1111 | 01 0S | 1000 | 0011 |
| SQDST Xmem, Ymem | Square distance | 1/1 | 1110 | 0010 | XXXX | YYYY |
| SQUR Smem, cfef | Square single data-memory operand | 1/1 | 0010 | 011D | IAAA | AAAA |
| SQUR A, dst | Square ACCA high | 1/1 | 1111 | 010D | 1000 | 1101 |
| SQURA Smem, src | Square and accumulate | 1/1 | 0011 | 100S | IAAA | AAAA |
| SQURS Smem, src | Square and subtract | 1/1 | 0011 | 101S | IAAA | AAAA |
| SUB Smem, src | Subtract operand from accumulator | 1/1 | 0000 | 100S | IAAA | AAAA |
| SUB Smem, TS, src | Shift by TREG[5:0], then subtract from ACC | 1/1 | 0000 | 110S | IAAA | AAAA |
| SUB Smem, 16, src [, c/sf ] | Shift operand 16 bits, then subtract from ACC | 1/1 | 0100 | 00SD | IAAA | AAAA |
| SUB Smem [, SHIFT], src [, cfef ] | Shift operand, then subtract from ACC (2-word opcode) | 2/2 | 0110 0000 | 1111 11SD | IAAA 001S | AAAA HIFT |
| SUB Xmem, SHFT, src | Shift operand, then subtract from ACC | 1/1 | 1001 | 001S | XXXX | SHFT |
| SUB Xmem, Ymem, dst | Shift dual operands by 16, then subtract | 1/1 | 1010 | 001D | XXXX | YYYY |
| SUB #//f[, SHFT], src[, dst] | Shift long-immediate, then subtract from ACC | 2/2 | 1111 | 00SD | 0001 | SHFT |
| SUB #//e, 16, src [, dst] | Shift long-immediate 16 bits, subtract from ACC | 2/2 | 1111 | 00SD | 0110 | 0001 |
| SUB src[, SHIFT], [, dst] | Subtract shifted ACC from ACC | 1/1 | 1111 | 01 SD | 001S | HIFT |
| SUB src, ASM [, c/sf] | Subtract ACC shifted by ASM from ACC | 1/1 | 1111 | 01 SD | 1000 | 0001 |
| SUBB Smem, src | Subtract from accumulator with borrow | 1/1 | 0000 | 111 D | IAAA | AAAA |
| SUBC Smem, src | Subtract conditionally | 1/1 | 0001 | 111S | IAAA | AAAA |
| SUBS Smem, src | Subtract from ACC, sign-extension suppressed | 1/1 | 0000 | 101S | IAAA | AAAA |

t Values for words and cycles assume the use of DARAM for data. Add one word and one cycle when using long-offset indirect addressing or

absolute addressing with a single data-memory operand. t Delayed Instruction § Condition true 11 Condition false

48

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

instruction set summary (continued)

Table 13. '54x Instruction Set Opcodes (Continued)

| MNEMONIC SYNTAX | DESCRIPTION | WORDS/ CYCLESt | MSB | OPCODE | LSB |
| --- | --- | --- | --- | --- | --- |
|  | CONTROL INSTRUCTIONS |  |  |  |  |
| B[D] pmad | Branch unconditionally with optional delay | 2/4,2* | 1111 | 00Z0 0111 | 0011 |
| BACC[D] src | Branch to address in ACC, optional delay | 1 /6,4* | 1111 | 01ZS 1110 | 0010 |
| BANZ[D] pmad, Sind | Branch on AR(ARP) not zero, optional delay | 2/4§,2fl,2* | 0110 | 11Z0 IAAA | AAAA |
| BC[D] pmad, cond[, cond[, cond ]] | Branch conditionally, optional delay | 2/5§,3fl,3* | 1111 | 10Z0 CCCC | CCCC |
| CALA[D] src | Call subroutine at address in ACC, optional delay | 1/6,4* | 1111 | 01ZS 1110 | 0011 |
| CALL[D] pmad | Call unconditionally, optional delay | 2/4,211 | 1111 | 00Z0 0111 | 0100 |
| CC[D] pmad, cond[, cond[, cond]] | Call conditionally, optional delay | 2/5§,3fl,3* | 1111 | 10Z1 CCCC | CCCC |
| FB[D] extpmad | Far branch unconditionally (optional delay) | 2/4,2* | 1111 | 10Z0 1KKK | KKKK |
| FBACC[D] src | Far branch to address in ACC, optional delay | 1 /6,4* | 1111 | 01ZS 1110 | 0110 |
| FCALA[D] src | Far call to address in ACC, optional delay | 1 /6,4* | 1111 | 01ZS 1110 | 0111 |
| FCALL[D] extpmad | Far call unconditionally, optional delay | 2/4,2* | 1111 | 10Z1 1KKK | KKKK |
| FRAME K | Stack pointer immediate offset | 1/1 | 1110 | 1110 KKKK | KKKK |
| FRET[D] | Far return (FRETD is for delayed return) | 1 /6,4* | 1111 | 01Z0 1110 | 0100 |
| FRETE[D] | Far return, enable interrupts, optional delay | 1 /6,4* | 1111 | 01Z0 1110 | 0101 |
| IDLE K | Idle until interrupt | 1/4 | 1111 | 01NN 1110 | 0001 |
| INTR K | Software interrupt | 1/3 | 1111 | 0111 110K | KKKK |
| MAR Smem | Modify auxiliary register | 1/1 | 0110 | 1101 IAAA | AAAA |
| NOP | No operation | 1/1 | 1111 | 0100 1001 | 0101 |
| POPD Smem | Pop top of stack to data memory | 1/1 | 1000 | 1011 IAAA | AAAA |
| POPM MMR | Pop top of stack to memory-mapped register | 1/1 | 1000 | 1010 IAAA | AAAA |
| PSHD Smem | Push data-memory value onto stack | 1/1 | 0100 | 1011 IAAA | AAAA |
| PSHM MMR | Push memory-mapped register onto stack | 1/1 | 0100 | 1010 IAAA | AAAA |
| RC[D] cond[, cond[, cond]] | Return conditionally, optional delay | 1/5§,3iT.3t | 1111 | 11Z0 CCCC | CCCC |
| RESET | Software reset | 1/3 | 1111 | 0111 1110 | 0000 |
| RET[D] | Return, optional delay | 1/5,3* | 1111 | 11Z0 0000 | 0000 |
| RETE[D] | Return and enable interrupts, optional delay | 1/5,3* | 1111 | 01Z0 1110 | 1011 |
| RETF[D] | Return fast and enable interrupts, optional delay | 1/3,1* | 1111 | 01Z0 1001 | 1011 |
| RPT Smem | Repeat next instruction, count is in operand | 1/1 | 0100 | 0111 IAAA | AAAA |
| RPT #K | Repeat next instruction, count is short immediate | 1/1 | 1110 | 1100 KKKK | KKKK |
| RPT #lk | Repeat next instruction, count is long immediate | 2/2 | 1111 | 0000 0111 | 0000 |
| RPTB[D] pmad | Block repeat, optional delay | 2/4,2* | 1111 | 00Z0 0111 | 0010 |
| RPTZ dst,#lk | Repeat next instruction and clear accumulator | 2/2 | 1111 | 000D 0111 | 0001 |
| RSBX N, SBIT | Reset status-register bit | 1/1 | 1111 | 01N0 1011 | SBIT |
| SSBX N, SBIT | Set status-register bit | 1/1 | 1111 | 01N1 1011 | SBIT |
| TRAP K | Software interrupt | 1/3 | 1111 | 0100 110K | KKKK |
| XC n, cond[, cond [, cond] ] | Execute conditionally | 1/1 | 1111 | 11N1 CCCC | CCCC |

t Values for words and cycles assume the use of DARAM for data. Add one word and one cycle when using long-offset indirect addressing or

absolute addressing with a single data-memory operand. * Delayed Instruction § Condition true 11 Condition false

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

49

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

instruction set summary (continued)

Table 13. '54x Instruction Set Opcodes (Continued)

| MNEMONIC SYNTAX | DESCRIPTION | WORDS/ CYCLESt | MSB | OPCODE | LSB |
| --- | --- | --- | --- | --- | --- |
|  | I/O INSTRUCTIONS |  |  |  |  |  |
| PORTR PA, Smem | Read data from port | 2/2 | 0111 | 0100 | IAAA | AAAA |
| PORTW Smem, PA | Write data to port | 2/2 | 0111 | 0101 | IAAA | AAAA |
|  | LOAD/STORE INSTRUCTIONS |  |  |  |  |  |
| CMPS src, Smem | Compare, select and store maximum | 1/1 | 1000 | 111S | IAAA | AAAA |
| DLD Lmem, dst | Long-word load to accumulator | 1/1 | 0101 | 011 D | IAAA | AAAA |
| DST src, Lmem | Store accumulator in long word | 1/2 | 0100 | 111S | IAAA | AAAA |
| LD Smem, dst | Load accumulator with operand | 1/1 | 0001 | 000D | IAAA | AAAA |
| LD Smem, TS, dst | Shift operand by TREG[5:0], then load into ACC | 1/1 | 0001 | 010D | IAAA | AAAA |
| LD Smem, 16, dst | Shift operand by 16 bits, then load into ACC | 1/1 | 0100 | 010D | IAAA | AAAA |
| LD Smem I, SHIFT], dst | Shift operand, then load into ACC (2-word opcode) | 2/2 | 0110 0000 | 1111 110D | IAAA 01 0S | AAAA HIFT |
| LD Xmem, SHFT, dst | Shift operand, then load into ACC | 1/1 | 1001 | 010D | XXXX | SHFT |
| LD #K, dst | Load ACC with short-immediate operand | 1/1 | 1110 | 100D | KKKK | KKKK |
| LD #lk[, SHFT], dst | Shift long-immediate, then load into ACC | 2/2 | 1111 | 000D | 0010 | SHFT |
| LD #lk, 16, dst | Shift long-immediate 16 bits, load into ACC | 2/2 | 1111 | 000D | 0110 | 0010 |
| LD src, ASM [, dst] | Shift ACC by value in ASM register | 1/1 | 1111 | 01SD | 1000 | 0010 |
| LD src[, SHIFT] [, dsf] | Shift accumulator | 1/1 | 1111 | 01SD | 01 0S | HIFT |
| LD Smem, T | Load TREG with single data-memory operand | 1/1 | 0011 | 0000 | IAAA | AAAA |
| LD Smem, DP | Load DP with single data-memory operand | 1/3 | 0100 | 0110 | IAAA | AAAA |
| LD #/c9, DP | Load DP with 9-bit operand | 1/1 | 1110 | 101K | KKKK | KKKK |
| LD #/c5, ASM | Load ACC shift-mode register with 5-bit operand | 1/1 | 1110 | 1101 | 000K | KKKK |
| LD #k3, ARP | Load ARP with 3-bit operand | 1/1 | 1111 | 0100 | 1010 | 0KKK |
| LD Smem, ASM | Load operand bits 4-0 into ASM register | 1/1 | 0011 | 0010 | IAAA | AAAA |
| LD Xmem, dst ¦¦MAC[R] Vmem[, dsf_ ] | Parallel load, multiply/accumulate [round] | 1/1 | 1010 | 10RD | XXXX | YYYY |
| LD Xmem, dst ¦¦MAS[R] Ymeml, dst_] | Parallel load, multiply/subtract [round] | 1/1 | 1010 | 11RD | XXXX | YYYY |
| LDM MM/?, cfef | Load memory-mapped register to ACC | 1/1 | 0100 | 100D | IAAA | AAAA |
| LDR Smem, dst | Load memory value in ACC high with rounding | 1/1 | 0001 | 011D | IAAA | AAAA |
| LDU Smem, dst | Load unsigned memory value | 1/1 | 0001 | 001D | IAAA | AAAA |
| LTD Smem | Load TREG and insert delay | 1/1 | 0100 | 1100 | IAAA | AAAA |
| SACCD src, Xmem, cond | Store accumulator conditionally | 1/1 | 1001 | 111S | XXXX | COND |
| SRCCD Xmem, cond | Store block-repeat counter conditionally | 1/1 | 1001 | 1101 | XXXX | COND |
| ST T, Smem | Store TREG | 1/1 | 1000 | 1100 | IAAA | AAAA |
| ST TRN, Smem | Store TRN | 1/1 | 1000 | 1101 | IAAA | AAAA |
| ST #//e, Smem | Store long-immediate operand | 2/2 | 0111 | 0110 | IAAA | AAAA |
| STH src, Smem | Store accumulator high to data memory | 1/1 | 1000 | 001S | IAAA | AAAA |

t Values for words and cycles assume the use of DARAM for data. Add one word and one cycle when using long-offset indirect addressing or

absolute addressing with a single data-memory operand. t Delayed Instruction § Condition true 11 Condition false

50

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

instruction set summary (continued)

Table 13. '54x Instruction Set Opcodes (Continued)

| MNEMONIC SYNTAX | DESCRIPTION | WORDS/ CYCLESt | OPCODE MSB LSB |
| --- | --- | --- | --- |
| LOAD/STORE INSTRUCTIONS (CONTINUED) |
| STH src, ASM, Smem | Shift ACC high by ASM, store to data memory | 1/1 | 1000 011S IAAA AAAA |
| STH src, SHFT, Xmem | Shift ACC high, then store to data memory | 1/1 | 1001 101S XXXX SHFT |
| STH src [, SHIFT], Smem | Shift ACC high, then store to data memory (2-word opcode) | 2/2 | 0110 1111 IAAA AAAA 0000 11 0S 011S HIFT |
| ST src, Ymem ¦¦ ADD Xmem, dst | Store ACC with parallel add | 1/1 | 1100 00SD XXXX YYYY |
| ST src, Ymem ¦¦ LD Xmem, dst | Store ACC with parallel load into accumulator | 1/1 | 1100 10SD XXXX YYYY |
| ST src, Ymem ¦¦ LD Xmem, T | Store ACC with parallel load into TREG | 1/1 | 1110 01 S0 XXXX YYYY |
| ST src, Ymem ¦¦ MAC[R] Xmem, dst | Parallel store and multiply ACC [round] | 1/1 | 1101 0RSD XXXX YYYY |
| ST src, Ymem ¦¦ MAS[R] Xmem, dst | Parallel store, multiply, and subtract | 1/1 | 1101 1RSD XXXX YYYY |
| ST src, Ymem ¦¦ MPY Xmem, dst | Parallel store and multiply | 1/1 | 1100 11SD XXXX YYYY |
| ST src, Ymem ¦¦ SUB Xmem, cfef | Parallel store and subtract | 1/1 | 1100 01SD XXXX YYYY |
| STL src, Smem | Store ACC low to data memory | 1/1 | 1000 000S IAAA AAAA |
| STL src, ASM, Smem | Shift ACC low by ASM, store to data memory | 1/1 | 1000 01 0S IAAA AAAA |
| STL src, SHF7; Xmem | Shift ACC low, then store to data memory | 1/1 | 1001 100S XXXX SHFT |
| STL src [, SHIFT], Smem | Shift ACC low, then store to data memory (2-word opcode) | 2/2 | 0110 1111 IAAA AAAA 0000 11 0S 100S HIFT |
| STLM src, MMR | Store ACC low to MMR | 1/1 | 1000 100S IAAA AAAA |
| STM #//c, MMR | Store long-immediate to MMR | 2/2 | 0111 0111 IAAA AAAA |
| STRCD Xmem, cond | Store TREG conditionally | 1/1 | 1001 1100 XXXX COND |
| LOGICAL INSTRUCTIONS |
| AND Smem, src | AND single data-memory operand with ACC | 1/1 | 0001 100S IAAA AAAA |
| AND #lk[, SHFT], src[, dst] | Shift long-immediate operand, AND with ACC | 2/2 | 1111 00SD 0011 SHFT |
| AND #lk, 16, src [, dst] | Shift long-immediate 16 bits, AND with ACC | 2/2 | 1111 00SD 0110 0011 |
| AND src[, SHIFT], [, cfef] | AND accumulator(s), then shift result | 1/1 | 1111 00SD 100S HIFT |
| ANDM #//e, Smem | AND memory with long-immediate operand | 2/2 | 0110 1000 IAAA AAAA |
| BIT Xmem, 6/TC | Test bit | 1/1 | 1001 0110 XXXX BITC |
| BITF Smem,#lk | Test bit field specified by immediate value | 2/2 | 0110 0001 IAAA AAAA |
| BITT Smem | Test bit specified by TREG | 1/1 | 0011 0100 IAAA AAAA |
| CMPL src[, dst] | Complement accumulator | 1/1 | 1111 01SD 1001 0011 |
| CMPM Smem,#lk | Compare memory with long-immediate operand | 2/2 | 0110 0000 IAAA AAAA |
| CMPR CC,ARx | Compare auxiliary register with AR0 | 1/1 | 1111 01CC 1010 1ARX |
| OR Smem, src | OR single data-memory operand with ACC | 1/1 | 0001 101S IAAA AAAA |

t Values for words and cycles assume the use of DARAM for data. Add one word and one cycle when using long-offset indirect addressing or

absolute addressing with a single data-memory operand. t Delayed Instruction § Condition true 11 Condition false

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

51

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

instruction set summary (continued)

Table 13. '54x Instruction Set Opcodes (Continued)

| MNEMONIC SYNTAX | DESCRIPTION |  | WORDS/ CYCLESt | MSB | OPCODE | LSB |
| --- | --- | --- | --- | --- | --- | --- |
|  | LOGICAL INSTRUCTIONS (CONTINUED) |  |  |  |  |  |
| OR #lk[, SHFT], src[, dst] | Shift long-immediate operand, then OR with ACC |  | 2/2 | 1111 | 00SD | 0100 | SHFT |
| OR #lk, 16, src[, dst] | Shift long-immediate 16 bits, then OR with ACC |  | 2/2 | 1111 | 00SD | 0110 | 0100 |
| OR src[, SHIFT], [, dst] | OR accumulator(s), then shift result |  | 1/1 | 1111 | 00SD | 101S | HIFT |
| ORM #lk, Smem | OR memory with constant |  | 2/2 | 0110 | 1001 | IAAA | AAAA |
| ROL src | Rotate accumulator left |  | 1/1 | 1111 | 01 0S | 1001 | 0001 |
| ROLTC src | Rotate accumulator left using TC |  | 1/1 | 1111 | 01 0S | 1001 | 0010 |
| ROR src | Rotate accumulator right |  | 1/1 | 1111 | 01 0S | 1001 | 0000 |
| SFTA src, SHIFT[, dst] | Shift accumulator arithmetically |  | 1/1 | 1111 | 01SD | 011S | HIFT |
| SFTC src | Shift accumulator conditionally |  | 1/1 | 1111 | 01 0S | 1001 | 0100 |
| SFTL src, SHIFT[, dst] | Shift accumulator logically |  | 1/1 | 1111 | 00SD | 111S | HIFT |
| XOR Smem, src | XOR operand with ACC |  | 1/1 | 0001 | 110S | IAAA | AAAA |
| XOR #lk[, SHFT], src[, dst] | Shift long-immediate, then XOR with ACC |  | 2/2 | 1111 | 00SD | 0101 | SHFT |
| XOR #lk, 16, src[, dst] | Shift long-immediate 16 bits, then XOR with ACC |  | 2/2 | 1111 | 00SD | 0110 | 0101 |
| XOR src[, SHIFT] [, dst] | XOR accumulator(s), then shift result |  | 1/1 | 1111 | 00SD | 110S | HIFT |
| XORM #lk, Smem | XOR memory with constant |  | 2/2 | 0110 | 1010 | IAAA | AAAA |
|  | MOVE INSTRUCTIONS |  |  |  |  |  |
| MVDD Xmem, Ymem | Move within data memory, X/Y addressing |  | 1/1 | 1110 | 0101 | XXXX | YYYY |
| MVDK Smem, dmad | Move data, destination addressing |  | 2/2 | 0111 | 0001 | IAAA | AAAA |
| MVDM dmad,MMR | Move data to memory-mapped register |  | 2/2 | 0111 | 0010 | IAAA | AAAA |
| MVDP Smem, pmad | Move data to program memory |  | 2/4 | 0111 | 1101 | IAAA | AAAA |
| MVKD dmad, Smem | Move data with source addressing |  | 2/2 | 0111 | 0000 | IAAA | AAAA |
| MVMD MM/?, dmad | Move memory-mapped register to data |  | 2/2 | 0111 | 0011 | IAAA | AAAA |
| MVMM MMRx, MMRy | Move between memory-mapped registers |  | 1/1 | 1110 | 0111 | MMRX | MMRY |
| MVPD pmad, Smem | Move program memory to data memory |  | 2/3 | 0111 | 1100 | IAAA | AAAA |
| READA Smem | Read data memory addressed by ACCA |  | 1/5 | 0111 | 1110 | IAAA | AAAA |
| WRITA Smem | Write data memory addressed by ACCA |  | 1/5 | 0111 | 1111 | IAAA | AAAA |

t Values for words and cycles assume the use of DARAM for data. Add one word and one cycle when using long-offset indirect addressing or

absolute addressing with a single data-memory operand. t Delayed Instruction § Condition true 11 Condition false

52

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

development support

Texas Instruments offers an extensive line of development tools forthe '54x generation of DSPs, including tools to evaluate the performance of the processors, generate code, develop algorithm implementations, and fully integrate and debug software and hardware modules.

The following products support development of '54x-based applications:

Software Development Tools:

Assembler/Linker

Simulator

Optimizing ANSI C compiler

Application algorithms

C/Assembly debugger and code profiler

Hardware Development Tools:

Extended development system (XDS™) emulator (supports '54x multiprocessor system debug) '54x EVM (Evaluation Module) '54x DSK (DSP Starter Kit)

The TMS320 Family Development Support Reference Guide (SPRU011) contains information about development support products for all TMS320 family member devices, including documentation. Refer to this document for further information about TMS320 documentation or any other TMS320 support products from Texas Instruments. There is an additional document, the TMS320 Third Party Support Reference Guide (SPRU052), which contains information about TMS320-related products from other companies in the industry. To receive copies of TMS320 literature, contact the Literature Response Center at 800/477-8924.

See Table 14 for complete listings of development support tools for the '54x. For information on pricing and availability, contact the nearest TI field sales office or authorized distributor.

| Table 14. | Development Support Tools |  |
| --- | --- | --- |
| DEVELOPMENT TOOL |  | PLATFORM |  | PART NUMBER |
|  | Software |  |
| Assembler/Linker |  | PC-DOS™, OS/2™ |  | TMDS324L850-02 |
| Compiler/Assembler/Linker |  | PC-DOS, OS/2 |  | TMDS324L855-02 |
| Compiler/Assembler/Linker |  | SPARC™ |  | TMDS324L555-09 |
| Simulator |  | PC-DOS, WIN™ |  | TMDS324L851-02 |
| Simulator |  | SPARC, WIN |  | TMDS324L551-09 |
| Digital Filter Design Package for PC |  | PC-DOS |  | DFDP |
| XDS510™ Debugger/Emulation Software |  | PC-DOS, OS/2, WIN |  | TMDS32401L0 |
| XDS510WS™ Debugger/Emulation Software |  | SPARC, WIN |  | TMDS32406L0 |
|  | Hardware |  |
| XDS510 Emulator! |  | PC-DOS, OS/2 |  | TMDS00510 |
| XDS510WS Emulator* |  | SPARC, WIN |  | TMDS00510WS |
| 3 V/5 V PC/SPARC JTAG Emulation Cable |  | N/A |  | TMDS3080002 |
| EVM Evaluation Module |  | PC-DOS, WIN |  | TMDX3260051 |
| DSK DSP Starter Kit |  | PC-DOS |  | TMDX32400L0 |

t Includes XDS510 board and JTAG emulation cable; TMDS32401 L0 C-source debugger conversion software not included t Includes XDS510WS box, SCSI cable, power supply, and JTAG emulation cable; TMDS32406L0 C-source debugger conversion software not included

PC-DOS and OS/2 are trademarks of International Business Machines Corp.

SPARC is a trademark of SPARC International, Inc.

WIN is a trademark of Microstate Corporation.

XDS, XDS510, and XDS510WS are trademarks of Texas Instruments Incorporated.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

53

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

device and development support tool nomenclature

To designate the stages in the product development cycle, TI assigns prefixes to the part numbers of all TMS320 devices and support tools. Each TMS320 member has one of three prefixes: TMX, TMP, or TMS. Texas Instruments recommends two of three possible prefixdesignators for its support tools: TMDX and TMDS. These prefixes represent evolutionary stages of product development from engineering prototypes (TMX/TMDX) through fully qualified production devices/tools (TMS/TMDS). This development flow is defined below.

Device development evolutionary flow:

TMX	Experimental device that is not necessarily representative of the final device's electrical

specifications

TMP	Final silicon die that conforms to the device's electrical specifications but has not completed

quality and reliability verification

TMS	Fully-qualified production device

Support tool development evolutionary flow:

TMDX        Development support product that has not yet completed Texas Instruments internal qualification testing.

TMDS        Fully qualified development support product

TMX and TMP devices and TMDX development support tools are shipped against the following disclaimer:

"Developmental product is intended for internal evaluation purposes."

TMS devices and TMDS development support tools have been characterized fully, and the quality and reliability of the device has been demonstrated fully. TI's standard warranty applies.

Predictions show that prototype devices (TMX or TMP) have a greater failure rate than the standard production devices. Texas Instruments recommends that these devices not be used in any production system because their expected end-use failure rate still is undefined. Only qualified production devices are to be used.

TI device nomenclature also includes a suffix with the device family name. This suffix indicates the package type (for example, PZ, PGE, PBK, or GGU) and temperature range (for example, L). Figure 10 provides a legend for reading the complete device name for any TMS320 family member.

Texas Instruments

54	POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

device and development support tool nomenclature (continued)

TMS 320 (B)  C 542 PGE  (L)

PREFIX

TMX = TMP = TMS = SMJ = SM =

experimental device prototype device qualified device MIL-STD-883C High Rel (non-883C)

DEVICE FAMILY

320 =  TMS320 Family

BOOT-LOADER OPTION

TECHNOLOGY

C = E = F = LC = VC =

CMOS

CMOS EPROM

CMOS Flash EEPROM

Low-Voltage CMOS (3.3 V)

Low Voltage CMOS [3 V (2.5 V core)]

t DIP = Dual-In-Line Package PGA = Pin Grid Array CC = Chip Carrier QFP = Quad Flat Package TQFP = Thin Quad Flat Package

TEMPERATURE RANGE

('54x DEFAULT: -40C TO 100C)

| H | = 0°C to 50°C |
| --- | --- |
| L | = 0°C to 70°C |
| S | = -55°Cto100°C |
| M | = -55°Cto125°C |
| A | = -40°Cto85°C |
| PACKAGE TYPEt |
| N | = plastic DIP |
| J | = ceramic DIP |
| JD | = ceramic DIP side-brazed |
| GB | = ceramic PGA |
| FZ | = ceramic CC |
| FN | = plastic leaded CC |
| FD | = ceramic leadless CC |
| PJ | = 100-pin plastic EIAJ QFP |
| PQ | = 132-pin plastic bumpered QFP |
| PZ | = 100-pin plastic TQFP |
| PBK = 128-pin plastic TQFP |
| PGE = 144-pin plastic TQFP |
| GGU= 144-pin BGA |
| DEVICE |
| '1x | DSP: |
|  | 10 16 |
|  | 14 17 |
|  | 15 |
| '2x | DSP: |
|  | 25 |
|  | 26 |
| '2xx D |
|  | 203 206 240 |
|  | 204 209 |
| '3x | DSP: |
|  | 30 |
|  | 31 |
|  | 32 |
| '4x | DSP: |
|  | 40 |
|  | 44 |
| '5x | DSP: |
|  | 50 53 |
|  | 51 56 |
|  | 52 57 |
| '54x C |
|  | 541 545 |
|  | 542 546 |
|  | 543 548 |
|  | 549 |
| '6x | DSP: |
|  | 6201 |
|  | 6701 |

Figure 10. TMS320 DSP Device Nomenclature

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

55

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

documentation support

Extensive documentation supports all TMS320 family generations of devices from product announcement through applications development. The types of documentation available include: data sheets, such as this document, with design specifications; complete user's guides for all devices; development support tools; and hardware and software applications.

The four-volume TMS320C54x DSP Reference Set (literature number SPRU210) consists of:

- Volume 1: CPU and Peripherals (literature number SPRU131)

- Volume 2: Mnemonic Instruction Set (literature number SPRU172)

- Volume 3: Algebraic Instruction Set (literature number SPRU179)

- Volume 4: Applications Guide (literature number SPRU173)

The reference set describes in detail the '54x TMS320 products currently available and the hardware and software applications, including algorithms, for fixed-point TMS320 devices.

For general background information on DSPs and TI devices, see the three-volume publication Digital Signal Processing Applications with the TMS320 Family (literature numbers SPRA012, SPRA016, and SPRA017).

A series of DSP textbooks is published by Prentice-Hall and John Wiley & Sons to support digital signal processing research and education. The TMS320 newsletter, Details on Signal Processing, is published quarterly and distributed to update TMS320 customers on product information. The TMS320 DSP bulletin board service (BBS) provides access to information pertaining to the TMS320 family, including documentation, source code and object code for many DSP algorithms and utilities. The BBS can be reached at 281/274-2323.

Information regarding TI DSP products is also available on the Worldwide Web at http://www.ti.com uniform resource locator (URL).

Texas Instruments

56	POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

electrical characteristics and operating conditions — 'C541, 'C542

absolute maximum ratings over specified temperature range (unless otherwise noted)t

Supply voltage range, Vrjrjt 	 -0.3 V to 7 V

Input voltage range 	 -0.3 V to 7 V

Output voltage range 	 -0.3 V to 7 V

Operating case temperature range, TC 	-40°C to 100°C

Storage temperature range, Tstg	-55°C to 150°C

t Stresses beyond those listed under "absolute maximum ratings" may cause permanent damage to the device. These are stress ratings only, and functional operation of the device at these or any other conditions beyond those indicated under "recommended operating conditions" is not implied. Exposure to absolute-maximum-rated conditions for extended periods may affect device reliability.

t All voltage values are with respect to

recommended operating conditions

|  |  |  | MIN | NOM | MAX | UNIT |
| --- | --- | --- | --- | --- | --- | --- |
| VDD | Supply voltage |  | 4.75 | 5 | 5.25 | V |
| vss | Supply voltage |  |  | 0 |  | V |
| V¦H | High-level input voltage | RS, INTn, NMI.CNT.CLKMDn X2/CLKIN | 3 |  | VDD + 0.3 | V |
|  |  | All other inputs | 2 |  | Vdd + 0.3 |  |
| V¦L | Low-level input voltage |  | -0.3 |  | 0.8 | V |
| lOH | High-level output current |  |  |  | -300 | MA |
| lOL | Low-level output current |  |  |  | 2 | mA |
| Tc | Operating case temperature |  | -40 |  | 100 | °C |

Refer to Figure 11 for 5-V device test load circuit values.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

57

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

electrical characteristics and operating conditions — 'C541, 'C542 (continued)

electrical characteristics over recommended operating case temperature range (unless otherwise noted)

|  | PARAMETER | TEST CONDITIONS | MIN | TYPt | MAX | UNIT |
| --- | --- | --- | --- | --- | --- | --- |
| VOH | High-level output voltaget |  | Iqh = -300 nA | 2.4 |  |  | V |
| VOL | Low-level output voltaget |  | lOL = 2 mA |  |  | 0.6 | V |
| hz | Input current in high impedance | VDD = MAX, V¦ = VSS to VDD | -20 |  | 20 | MA |
|  |  | TRST | With internal pulldown | -10 |  | 800 | ma |
| l¦ | Input current (Vi ~ Vqq to Vnni | HPIENA | With internal pulldown, RS = 0 | -10 |  | 400 |  |
|  |  | TMS, TCK, TDI, HPlll | With internal pullups | -500 |  | 10 |  |
|  |  | D[15:0], HD[7:0] | Bus holders enabled, Vqd = MAX* | -150 |  | 250 | HA |
|  |  | All other input-only pins |  | -10 |  | 10 |  |
| !dDC | Supply current, core CPU |  | Vqd = 5 V, fx = 40 MHz,§ Tq = 25°C |  | 47H |  | mA |
| 'ddp | Supply current, pins |  | VDD = 5 V, fx = 40 MHz,§ Tc = 25°C |  | 18# |  | mA |
| Idd | Supply current, standby | IDLE2 | PLLximode, 40 MHz input |  | 4 |  | mA |
|  |  | IDLE3 | Divide-by-two mode, CLKIN stopped |  | 5 |  | MA |
| Ci | Input capacitance |  |  |  | 10 |  | PF |
| Co | Output capacitance |  |  |  | 10 |  | PF |

t All typical values are at Vqd = 5 V, Tq = 25°C.

t All input and output voltage levels except RS, INT0-INT3, NMI, CNT, X2/CLKIN, CLKMD0-CLKMD3 are TTL-compatible.

§ Clock mode: PLL x 1 with external source

11 This value was obtained with 50% usage of MAC and 50% usage of NOP instructions. Actual operating current varies with program being

executed. * This value was obtained with single-cycle external writes, CLKOFF = Oand load = 15 pF. For more details on how this calculation is performed,

refer to the Calculation of TMS320C54x Power Dissipation application report (literature number SPRA164). || HPI input signals except for HPIENA.

^ vl ^ V||_(MAX) °r V|H(MIN) ^ vl ^ V|H(MAX)

58

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

PARAMETER MEASUREMENT INFORMATION

timing parameter symbology

Timing parameter symbols used are created in accordance with JEDEC Standard 100-A. To shorten the symbols, some of the pin names and other related terminology have been abbreviated as follows:

| Lowercase | subscripts and their meanings: | Letters and symbols and their meanings |
| --- | --- | --- |
| a | access time | H | High |
| c | cycle time (period) | L | Low |
| d | delay time | V | Valid |
| dis | disable time | Z | High impedance |
| en | enable time |  |  |
| f | fall time |  |  |
| h | hold time |  |  |
| r | rise time |  |  |
| su | setup time |  |  |
| t | transition time |  |  |
| v | valid time |  |  |
| w | pulse duration (width) |  |  |
| X | Unknown, changing, or don't care level |  |  |

signal transition reference points

All timing references are made at a voltage of 1.5 volts, except rise and fall times which are referenced at the 10% and 90% points of the specified low and high logic levels, respectively.

Output o Under Test

Tester Pin Electronics

vLoad

Where: Iql	= 2 mA (all outputs)

Ioh	= 300 MA (all outputs)

VLoad	=1-5V

Cj	= 40 pF typical load circuit capacitance.

Figure 11. 5-V Test Load Circuit

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

59

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

electrical characteristics and operating conditions — 'LC54x, 'VC54x

See Table 1, Characteristics of the '54x Processors, for specific device applicability.

absolute maximum ratings over specified temperature range (unless otherwise noted)t

Supply voltage range, Voot 	-0.3 V to 4.6 V

Input voltage range 	-0.3 V to 4.6 V

Output voltage range 	-0.3 V to 4.6 V

Operating case temperature range, TC	-40°C to 100°C

Storage temperature range, Tstg	-55°C to 150°C

t Stresses beyond those listed under "absolute maximum ratings" may cause permanent damage to the device. These are stress ratings only, and functional operation of the device at these or any other conditions beyond those indicated under "recommended operating conditions" is not implied. Exposure to absolute-maximum-rated conditions for extended periods may affect device reliability.

t All voltage values are with respect to

recommended operating conditions

|  |  |  | MIN | NOM | MAX | UNIT |
| --- | --- | --- | --- | --- | --- | --- |
| VDD | Device supply voltage |  | 3 | 3.3 | 3.6 | V |
| vss | Supply voltage, GND |  |  | 0 |  | V |
| V¦H | High-level input voltage | RS,INTn,NMI,CNT, X2/CLKIN, CLKMDn, Vdd = 3.3±0.3V | 2.5 |  | VDD + 0.3 | V |
|  |  | All other inputs | 2 |  | VDD + 0.3 |  |
| V¦L | Low-level input voltage |  | -0.3 |  | 0.8 | V |
| 'OH | High-level output current |  |  |  | -300 | HA |
| lOL | Low-level output current |  |  |  | 1.5 | mA |
| TC | Operating case temperature |  | -40 |  | 100 | °C |

Refer to Figure 12 for 3.3-V device test load circuit values.

60

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

electrical characteristics and operating conditions — 'LC54x, 'VC54x (continued)

See Table 1, Characteristics of the '54x Processors, for specific device applicability.

electrical characteristics over recommended operating case temperature range (unless otherwise noted)

|  | PARAMETER | TEST CONDITIONS | MIN | TYPt | MAX | UNIT |
| --- | --- | --- | --- | --- | --- | --- |
| VOH | High-level output voltaget | VDD = 3.3 ± 0.3 V, IOH = MAX | 2.4 |  |  | V |
| VOL | Low-level output voltaget | lOL = MAX |  |  | 0.4 | V |
| hz | Input current in high | impedance | VDD = MAX,V¦ = VSStoVDD | -10 |  | 10 | MA |
|  |  |  | TRST | With internal pulldown | -10 |  | 800 | ma |
|  |  |  | HPIENA | With internal pulldown, RS = 0 | -10 |  | 400 |  |
| l¦ | Input current (V = Vcc to Vnn) |  | TMS, TCK, TDI, HPlll | With internal pullups | -400 |  | 10 |  |
|  |  |  | D[15:0], HD[7:0] | Bus holders enabled, Vqd = MAXA | -150 |  | 250 |  |
|  |  |  | All other input-only pins |  | -10 |  | 10 |  |
| Iddc | Supply current, core | CPU | VDD = 3.3 V, fx = 40 MHz,§ TC = 25°C |  | 30H |  | mA |
| !DDP | Supply current, pins |  | VDD = 3.3 V, fx = 40 MHz,§ Tc = 25°C |  | 12# |  | mA |
|  | Supply current, |  | IDLE2 | PLL x 1 mode, 40 MHz input |  | 2 |  | mA |
| Idd | standby |  | IDLE3 | Divide-by-two mode, CLKIN stopped |  | 5 |  | MA |
| Ci | Input capacitance |  |  |  | 10 |  | PF |
| Co | Output capacitance |  |  |  | 10 |  | PF |

t All values are typical unless otherwise specified.

t All input and output voltage levels except RS, INT0-INT3, NMI, CNT, X2/CLKIN, CLKMD0-CLKMD3 are LVTTL-compatible.

§ Clock mode: PLL x 1 with external source

11 This value was obtained with 50% usage of MAC and 50% usage of NOP instructions. Actual operating current varies with program being

executed. * This value was obtained with single-cycle external writes, CLKOFF = 0 and load = 15 pF. For more details on how this calculation is performed,

refer to the Calculation of TMS320C54x Power Dissipation application report (literature number SPRA164). || HPI input signals except for HPIENA.

^ V| < V|L(MAX) °r V|H(MIN) ^ vl ^ V|H(MAX)

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

61

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

PARAMETER MEASUREMENT INFORMATION

Output o Under Test

Tester Pin Electronics

V|_oad

Where: Iql	= 1 -5 mA (all outputs)

Ioh	= 300 MA (all outputs)

VLoad	=1-5V

Cj	= 40 pF typical load circuit capacitance.

Figure 12. 3.3-V Test Load Circuit

62

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

internal oscillator with external crystal

The internal oscillator is enabled by selecting the appropriate clock mode at reset (this is device dependent -see PLL section) and connecting a crystal or ceramic resonator across X1 and X2/CLKIN. The CPU clock frequency is one-half the crystal's oscillation frequency following reset. After reset, the clock mode of the devices with the software PLL can also be changed to divide-by-four.

The crystal should be in fundamental mode operation and parallel resonant with an effective series resistance of 30ohms and power dissipation of 1 mW. The connection of the required circuit, consisting of the crystal and two load capacitors, is shown in Figure 13. The load capacitors, C1 and C2, should be chosen such that the equation below is satisfied. C|_ in the equation is the load specified for the crystal.

C2)

recommended operating conditions (see Figure 13)

|  |  |  | 'C54x-40 LC54x-40 |  |  | LC54x-50 |  |  | '54x-66 |  | UNIT |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | MIN | NOM | MAX | MIN | NOM | MAX | MIN | NOM | MAX |  |
| fx | Input clock frequency | 10t |  | 20* | 10t |  | 20* | 10t |  | 20* | MHz |

t This device utilizes a fully static design and therefore can operate with tc(ci) approaching ~. The device is characterized at frequencies

approaching 0 Hz. t It is recommended that the PLL clocking option be used for maximum frequency operation.

X1

X2/CLKIN

C1

Crystal

D

C2

Figure 13. Internal Divide-by-Two Clock Option With External Crystal

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

63

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

divide-by-two/divide-by-four clock option - PLL disabled

The frequency of the reference clock provided attheX2/CLKIN pin can be divided by a factor of two or four to generate the internal machine cycle. The selection of the clock mode is described in the clockgeneratorsection.

When an external clock source is used, the frequency injected must conform to specifications listed in the timing requirements table.

switching characteristics over recommended operating conditions [H = 0.5tC(co)] (see Figure 13 and Figure 14, and the recommended operating conditions table)

|  | PARAMETER |  | 'C54x-40 'LC54x-40 |  |  | 'LC54x-50 |  |  | '54x-66 |  | UNIT |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | MIN | TYP | MAX | MIN | TYP | MAX | MIN | TYP | MAX |  |
| (c(CO) | Cycle time, CLKOUT | 25* | 2tc(CI) | t | 20* | 2tc(CI) | t | 15* | 2tc(CI) | t | ns |
| td(CIH-CO) | Delay time, X2/CLKIN high to CLKOUT high/low | 6 | 12 | 18 | 6 | 12 | 18 | 4 | 10 | 16 | ns |
| (f(CO) | Fall time, CLKOUTt |  | 2 |  |  | 2 |  |  | 2 |  | ns |
| tr(CO) | Rise time, CLKOUTt |  | 2 |  |  | 2 |  |  | 2 |  | ns |
| (w(COL) | Pulse duration, CLKOUT lowt | H-4 | H-2 | H | H-4 | H-2 | H | H-4 | H-2 | H | ns |
| (w(COH) | Pulse duration, CLKOUT hight | H-4 | H-2 | H | H-4 | H-2 | H | H-4 | H-2 | H | ns |

t This device utilizes a fully static design and therefore can operate with tC(ci) approaching ∞. The device is characterized at frequencies

approaching 0 Hz. t It is recommended that the PLL clocking option be used for maximum frequency operation.

64

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

divide-by-two/divide-by-four clock option - PLL disabled (continued)

timing requirements for divide-by-two/divide-by-four clock option - PLL disabled (see Figure 14)

|  |  | 'C54x-40 'LC54x-40 |  | 'LC54x-50 | '54x-66 | UNIT |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | MIN MAX | MIN | MAX | MIN | MAX |  |
| 'c(CI) | Cycle time, X2/CLKIN | 20* | t | 20* | t | 20* | t | ns |
| 'f(CI) | Fall time, X2/CLKIN |  | 4 |  | 4 |  | 4 | ns |
| tr(CI) | Rise time, X2/CLKIN |  | 4 |  | 4 |  | 4 | ns |
| (w(CIL) | Pulse duration, X2/CLKIN low | 5 | t | 5 | t | 5 | t | ns |
| (w(CIH) | Pulse duration, X2/CLKIN high | 5 | t | 5 | t | 5 | t | ns |

t This device utilizes a fully static design and therefore can operate with tc(ci) approaching ∞. The device is characterized at frequencies

approaching 0 Hz. * It is recommended that the PLL clocking option be used for maximum frequency operation.

CLKOUT

X2/CLKIN

Figure 14. External Divide-by-Two Clock Timing

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

65

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

multiply-by-N clock option - PLL enabled

The frequency of the reference clock provided at the X2/CLKIN pin can be multiplied by a factor of N to generate the internal machine cycle. The selection of the clock mode and the value of N is described in the clockgenerator section.

When an external clock source is used, the frequency injected must conform to specifications listed in the timing requirements table.

switching characteristics over recommended operating conditions for multiply-by-N clock option - PLL enabled [H = 0.5tC(co)] (see Figure 13 and Figure 15, and the recommended operating conditions table)

|  | PARAMETER |  | 'C54x-40 'LC54x-40 |  |  | 'LC54x-50 |  |  | '54x-66 |  | UNIT |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | MIN | TYP | MAX | MIN | TYP | MAX | MIN | TYP | MAX |  |
| tc(CO) | Cycle time, CLKOUT | 25 | *c(CI)/N |  | 20 | *c(CI)/N |  | 15 | *c(CI)/N |  | ns |
| td(CIH-CO) | Delay time, X2/CLKIN high/low to CLKOUT high/low | 6 | 12 | 18 | 6 | 12 | 18 | 4 | 10 | 16 | ns |
| tf(CO) | Fall time, CLKOUT |  | 2 |  |  | 2 |  |  | 2 |  | ns |
| *r(CO) | Rise time, CLKOUT |  | 2 |  |  | 2 |  |  | 2 |  | ns |
| tw(COL) | Pulse duration, CLKOUT low | H-4 | H-2 | H | H-4 | H-2 | H | H-4 | H-2 | H | ns |
| (w(COH) | Pulse duration, CLKOUT high | H-4 | H-2 | H | H-4 | H-2 | H | H-4 | H-2 | H | ns |
|  | Transitory phase, PLL lock-uptime |  |  | 50 |  |  | 50 |  |  | 50 | [IS |

66

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

multiply-by-N clock option - PLL enabled (continued)

timing requirements for multiply-by-N clock option - PLL enabled (see Figure 15)

|  |  |  | 'C54x-40 'LC54x-40 | 'LC54x-50 | '54x-66 | UNIT |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  | MIN | MAX | MIN | MAX | MIN | MAX |  |
|  |  | Integer PLL multiplier N (N = 1-15) | 20t | 400 | 20t | 400 | 20t | 400 | ns |
| 'c(CI) | Cycle time, X2/CLKIN | PLL multiplier N =x.5 | 20t | 200 | 20t | 200 | 20t | 200 |  |
|  |  | PLL multiplier N =x.25, x.75 | 20T | 100 | 20t | 100 | 20t | 100 |  |
| tf(CI) | Fall time, X2/CLKIN |  |  | 4 |  | 4 |  | 4 | ns |
| tr(CI) | Rise time, X2/CLKIN |  |  | 4 |  | 4 |  | 4 | ns |
| (w(CIL) | Pulse duration, X2/CLKIN low |  | 5 |  | 5 |  | 5 |  | ns |
| (w(CIH) | Pulse duration, X2/CLKIN high |  | 5 |  | 5 |  | 5 |  | ns |

t Note that for all values of tc(ci), the minimum tc(co) period must not be exceeded.

w(CIH)

»c(CI)

:w,CIL,

tr(cl)-H

J  I

X2/CLKIN

CLKOUT

■ tp

JVVVVVVVV

(X Unstable

llAAAAAAAA

tc(CO)

I  I

1

tf(CO) -H

I

Mw,COL,|   \

Figure 15. External Multiply-by-One Clock Timing

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

67

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

memory and parallel I/O interface timing

switching characteristics over recommended operating conditions for a memory read (MSTRB = O)tt (see Figure 16)

| PARAMETER | 'LC542-40 'LC543-40 | 'C54x-40 'LC54x-40 | 'LC54x-50 | '54x-66 | UNIT |
| --- | --- | --- | --- | --- | --- |
|  | MIN MAX | MIN MAX | MIN MAX | MIN MAX |  |
| Delay time, address valid from td(CLKL-A) CLKOUTIow§ | 0 5 | 0 5 | 0 5 | 0 5 | ns |
| Delay time, address valid from ld(CLKH-A) CLKOUT high (transition)!! | 0 5 | 0 5 | 0 5 | -2 3 | ns |
| Delay time, MSTRB low from CLKOUT td(CLKL-MSL) ,ow | 0 5 | 0 5 | 0 5 | 0 5 | ns |
| Delay time, MSTRB high from td(CLKL-MSH) CLKOUT low | -2 3 | -2 3 | -2 3 | -2 3 | ns |
| Hold time, address valid after CLKOUT *h(CLKL-A)R ,ow§ | 0 5 | 0 5 | 0 5 | 0 5 | ns |
| Hold time, address valid after CLKOUT *h(CLKH-A)R highU | 0 5 | 0 5 | 0 5 | -2 3 | ns |

t Address, PS, and DS timings are all included in timings referenced as address.

t See Table 15, Table 16, and Table 17 for address bus timing variation with load capacitance.

§ In the case of a memory read preceded by a memory read

11 In the case of a memory read preceded by a memory write

68

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

memory and parallel I/O interface timing (continued)

timing requirements for a memory read (MSTRB = 0) [H = 0.5 tC(co)]^ (see Figure 16)

|  | 'LC542-40 'LC543-40 | 'C54x-40 'LC54x-40 | 'LC54x-50 | '54x-66 | UNIT |
| --- | --- | --- | --- | --- | --- |
|  | MIN MAX | MIN MAX | MIN MAX | MIN MAX |  |
| Access time, read data access from ta(A)M address valid | 2H-12 | 2H-10 | 2H-10 | 2H-10 | ns |
| Access time, read data access from ta(MSTRBL) MSTRB ,ow | 2H-12 | 2H-10 | 2H-10 | 2H-10 | ns |
| Setup time, read data before CLKOUT (su(D)R ,ow | 7 | 5 | 5 | 5 | ns |
| Hold time, read data after CLKOUT (h(D)R low | 0 | 0 | 0 | 2 | ns |
| Hold time, read data after address th(A-D)R invaNd | 0 | 0 | 0 | 1 | ns |
| 'h(D)MSTRBH Hold time, read data after MSTRB high | 0 | 0 | 0 | 0 | ns |

t Address, PS, and DS timings are all included in timings referenced as address.

t See Table 15, Table 16, and Table 17 for address bus timing variation with load capacitance.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

69

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

| memory and parallel | I/O interface timing (continued) |  |
| --- | --- | --- |
| CLKOUT | V | J | \ | _y v |
|  | K- I I | P^ td(CLKL-A) | I I |  |  |
|  |  |  | I |  | lh(CLKL-A)R |
| A[15:0] |  |  |  | X |
|  |  |  | i i ¦ *su(D)R -k— *a(A)M —P | I I | f4>l lh(A-D)R |
|  |  |  |  | v_ |  |
|  |  |  |  |  | ►¦ »h(D)R |
| D[15:0] |  |  |  |  | )i < |
|  |  |  |  | I I I | /1 \ I ^ P^— *h(D)MSTRBH - td(CLKL-MSH) |
| Ld(CL | KL-MSL) -^ la(MSTRBL) | I |  |  |
| MSTRB |  | \ | 7 | / |
| R/W |  |  |  |  |
| PS, DS |  |  | \ | / | / |

Figure 16. Memory Read (MSTRB = 0)

70

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

memory and parallel I/O interface timing (continued)

switching characteristics over recommended operating conditions for a memory write (MSTRB = 0) [H = 0.5 tc(CO)]tt (see Figure 17)

|  | PARAMETER | 'C54x-40 'LC54x-40 'LC54x-50 | '54x-66 | UNIT |
| --- | --- | --- | --- | --- |
|  |  | MIN | MAX | MIN | MAX |  |
| td(CLKH-A) | Delay time, address valid from CLKOUT high§ | 0 | 5 | -2 | 3 | ns |
| (d(CLKL-A) | Delay time, address valid from CLKOUT lowil | 0 | 5 | 0 | 5 | ns |
| td(CLKL-MSL) | Delay time, MSTRB low from CLKOUT low | 0 | 5 | 0 | 5 | ns |
| (d(CLKL-D)W | Delay time, data valid from CLKOUT low | 0 | 10 | 0 | 6 | ns |
| td(CLKL-MSH) | Delay time, MSTRB high from CLKOUT low | -2 | 3 | -2 | 3 | ns |
| (d(CLKH-RWL) | Delay time, R/W low from CLKOUT high | 0 | 5 | -2 | 3 | ns |
| td(CLKH-RWH) | Delay time, R/W high from CLKOUT high | -2 | 3 | -2 | 3 | ns |
| (d(RWL-MSTRBL) | Delay time, MSTRB low after R/W low | H-2 | H + 3 | H-2 | H + 3 | ns |
| *h(A)W | Hold time, address valid after CLKOUT high§ | 0 | 5 | 0 | 5 | ns |
| (h(D)MSH | Hold time, write data valid after MSTRB high | H-5 | H + 5H | H-5 | H + 5H | ns |
| *w(SL)MS | Pulse duration, MSTRB low | 2H-5 |  | 2H-5 |  | ns |
| *su(A)W | Setup time, address valid before MSTRB low | 2H-5 |  | 2H-5 |  | ns |
| tsu(D)MSH | Setup time, write data valid before MSTRB high | 2H-10 | 2H+10H | 2H-10 | 2H+8§ | ns |

t Address, PS, and DS timings are all included in timings referenced as address.

t See Table 15, Table 16, and Table 17 for address bus timing variation with load capacitance.

§ In the case of a memory write preceded by a memory write.

11 In the case of a memory write preceded by an I/O cycle.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

71

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

| memory and parallel | I/O interface timing (continued) |  |  |
| --- | --- | --- | --- |
| CLKOUT *b | _f ^v J~ "^ |  |  |
|  | —^ td(CL | KL-A) | I | r*—^ *h(A)W^ ^ | ld(CLKH-A) |
| A[15:0] |  | X |  |
|  | I I I —0 |  | f< ^ | *d(CLKL-D)W |  |  | *h(D)MSH |
|  |  |  |  |  | ' i '! |  |
|  |  |  |  | lSU(D)MSH |  |  |  |
| D[15:0] | ) |  | ^_ |  |  |
|  | I |  |  | - td(CLKL-MSL) |  | [CLKL-M |  |
|  | I I |  |  |  | -td |  |  |
|  |  |  |  |  |  |  | SH) |
|  | I* ¦ Isu(A)W •■ |  |  |  |  |
| MSTRB | i | JT |  |  |
|  | \4 M td(CLKH-RWL) |  |  |  | <"\~ I I | td(CLKH-RWH) |
|  |  | " lw(SL)MS - td(RWL-MSTRBL) |  |  |  |  |
| R/W |  |  |  |  |  |  |
| PS,DS | \ |  |  | / |  |

Figure 17. Memory Write (MSTRB = 0)

72

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

memory and parallel I/O interface timing (continued)

switching characteristics over recommended operating conditions for a parallel I/O port read (IOSTRB = O)tt (see Figure 18)

| PARAMETER | 'LC542-40 'LC543-40 | 'C54x-40 'LC54x-40 'LC54x-50 | '54x-66 | UNIT |
| --- | --- | --- | --- | --- |
|  | MIN MAX | MIN MAX | MIN MAX |  |
| 'd(CLKL-A) Delay time, address valid from CLKOUT low | 0 5 | 0 5 | 0 5 | ns |
| td(CLKH-ISTRBL) Delav time, IOSTRB low from CLKOUT high | 0 5 | 0 5 | -2 3 | ns |
| 'd(CLKH-ISTRBH) Delav time. IOSTRB high from CLKOUT high | -2 3 | -2 3 | -2 3 | ns |
| 'h(A)IOR Ho\6 time, address after CLKOUT low | 0 5 | 0 5 | 0 5 | ns |

t Address and IS timings are included in timings referenced as address.

t See Table 15, Table 16, and Table 17 for address bus timing variation with load capacitance.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

73

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

memory and parallel I/O interface timing (continued)

timing requirements for a parallel I/O port read (IOSTRB = 0) [H = 0.5 tC(co)]^ (see Figure 18)

|  | 'LC542-40 'LC543-40 | 'C54x-40 'LC54x-40 'LC54x-50 | '54x-66 | UNIT |
| --- | --- | --- | --- | --- |
|  | MIN MAX | MIN MAX | MIN MAX |  |
| 'a(A)IO Access time, read data access from address valid | 3H-12 | 3H-10 | 3H-10 | ns |
| 'a(ISTRBL)IO Access time, read data access from IOSTRB low | 2H-12 | 2H-10 | 2H-10 | ns |
| 'su(D)IOR Setup time, read data before CLKOUT high | 7 | 5 | 5 | ns |
| 'h(D)IOR Hold time, read data after CLKOUT high | 0 | 0 | 0 | ns |
| 'h(ISTRBH-D)R Hold time> read data after IOSTRB high | 0 | 0 | 0 | ns |

t Address and IS timings are included in timings referenced as address.

t See Table 15, Table 16, and Table 17 for address bus timing variation with load capacitance.

CLKOUT

\

V

A[15:0]

ld(CLKL-A)

i

th(A)IOR

D[15:0]

ta(A)IO

la(ISTRBL)IO

td(CLKH-ISTRBL)

*h(D)IOR

*su(D)IOR

>

*h(ISTRBH-D)R td(CLKH-ISTRBH)

IOSTRB

\

R/W

y

IS

\

Figure 18. Parallel I/O Port Read (IOSTRB = 0)

74

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

memory and parallel I/O interface timing (continued)

switching characteristics over recommended operating conditions for a parallel I/O port write (IOSTRB = 0) [H = 0.5 tc(Co)] (see Figure 19)t

|  | PARAMETER | 'C54x-40 'LC54x-40 'LC54x-50 | '54x-66 | UNIT |
| --- | --- | --- | --- | --- |
|  |  | MIN | MAX | MIN | MAX |  |
| td(CLKL-A) | Delay time, address valid from CLKOUT lowt | 0 | 5 | 0 | 5 | ns |
| td(CLKH-ISTRBL) | Delay time, IOSTRB low from CLKOUT high | 0 | 5 | -2 | 3 | ns |
| tdfCLKH-D^OW | Delay time, write data valid from CLKOUT high | H-5 | H + 10 | H-5 | H+8 | ns |
| td(CLKH-ISTRBH) | Delay time, IOSTRB high from CLKOUT high | -2 | 3 | -2 | 3 | ns |
| td(CLKL-RWL) | Delay time, R/W low from CLKOUT low | 0 | 5 | 0 | 5 | ns |
| td(CLKL-RWH) | Delay time, R/W high from CLKOUT low | -2 | 3 | -2 | 3 | ns |
| (h(A)IOW | Hold time, address valid from CLKOUT lowt | 0 | 5 | 0 | 5 | ns |
| th(D)IOW | Hold time, write data after IOSTRB high | H-5 | H+5 | H-5 | H+5 | ns |
| tsu(D)IOSTRBH | Setup time, write data before IOSTRB high | H-7 | H | H-5 | H | ns |
| *su(A)IOSTRBL | Setup time, address valid before IOSTRB low | H-5 | H+5 | H-5 | H+5 | ns |

t See Table 1 Stable 16, and Table 17 for address bus timing variation with load capacitance. t Address and IS timings are included in timings referenced as address.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

75

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

| memory and | parallel I | /O interface timing (continued) |  |
| --- | --- | --- | --- |
| CLKOUT |  | I | \ / | \ / \ |
| td(CLKL-A) " | «- | rt 1— -i ! | —*J— *su(A)IOSTRBL 1 |  |  | * >j— lh(A)IOW |
| A[15:0] |  | X |  | X |
|  | ld(CL |  |  |  |  | ~ lh(D)IOW |
|  |  | <H-D)IOW 1* 1 1 |  |  |  |  |
|  |  |  |  |  | J vl |  |
| D[15:0] | *d(CL | KH | 1 |  | _r |  |
|  |  |  | -ISTRBL) —14 1 | ld(CLKH-!¦STRBH) —\+- h* | I ► ♦j lsu(D)l | OSTRBH |
| IOSTRB |  |  |  |  |  |  |
|  | r«- | -*— td(CLKL-RWL) \ | —► | j*— td(CLKL-RWH) |
| R/W |  |  |  |  |
|  |  | \ |  |  |  |
| IS |  |  |  |  |  |

Figure 19. Parallel I/O Port Write (IOSTRB = 0)

I/O timing variation with load capacitance: SPICE simulation results

Condition: Temperature Capacitance Voltage Model

125° C 0-100pF 2.7/3.0/3.3 V Weak/Nominal/Strong

90%

10%

Figure 20. Rise and Fall Time Diagram

76

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

I/O timing variation with load capacitance: SPICE simulation results (continued) Table 15. Timing Variation With Load Capacitance: [2.7 V] 10% - 90%

|  | WEAK | NOMINAL | STRONG |
| --- | --- | --- | --- |
|  | RISE | FALL | RISE | FALL | RISE | FALL |
| OpF | 0.476 ns | 0.457 ns | 0.429 ns | 0.391 ns | 0.382 ns | 0.323 ns |
| 10 pF | 1.511 ns | 1.278 ns | 1.386 ns | 1.148 ns | 1.215 ns | 1.049 ns |
| 20 pF | 2.551 ns | 2.133 ns | 2.350 ns | 1.956 ns | 2.074 ns | 1.779 ns |
| 30 pF | 3.614 ns | 3.011 ns | 3.327 ns | 2.762 ns | 2.929 ns | 2.512 ns |
| 40 pF | 4.664 ns | 3.899 ns | 4.394 ns | 3.566 ns | 3.798 ns | 3.264 ns |
| 50 pF | 5.752 ns | 4.786 ns | 5.273 ns | 4.395 ns | 4.655 ns | 4.010 ns |
| 60 pF | 6.789 ns | 5.656 ns | 6.273 ns | 5.206 ns | 5.515 ns | 4.750 ns |
| 70 pF | 7.817 ns | 6.598 ns | 7.241 ns | 6.000 ns | 6.442 ns | 5.487 ns |
| 80 pF | 8.897 ns | 7.531 ns | 8.278 ns | 6.928 ns | 7.262 ns | 6.317 ns |
| 90 pF | 10.021 ns | 8.332 ns | 9.152 ns | 7.735 ns | 8.130 ns | 7.066 ns |
| 100pF | 11.072 ns | 9.299 ns | 10.208 ns | 8.537 ns | 8.997 ns | 7.754 ns |
| Table 16. Timing Variation With Load Capacitance: [3 V] 10% - 90% |
|  | WEAK | NOMINAL | STRONG |
|  | RISE | FALL | RISE | FALL | RISE | FALL |
| OpF | 0.436 ns | 0.387 ns | 0.398 ns | 0.350 ns | 0.345 ns | 0.290 ns |
| 10 pF | 1.349 ns | 1.185 ns | 1.240 ns | 1.064 ns | 1.092 ns | 0.964 ns |
| 20 pF | 2.273 ns | 1.966 ns | 2.098 ns | 1.794 ns | 1.861 ns | 1.634 ns |
| 30 pF | 3.226 ns | 2.765 ns | 2.974 ns | 2.539 ns | 2.637 ns | 2.324 ns |
| 40 pF | 4.168 ns | 3.573 ns | 3.849 ns | 3.292 ns | 3.406 ns | 3.013 ns |
| 50 pF | 5.110 ns | 4.377 ns | 4.732 ns | 4.052 ns | 4.194 ns | 3.710 ns |
| 60 pF | 6.033 ns | 5.230 ns | 5.660 ns | 4.811 ns | 5.005 ns | 4.401 ns |
| 70 pF | 7.077 ns | 5.997 ns | 6.524 ns | 5.601 ns | 5.746 ns | 5.117 ns |
| 80 pF | 8.020 ns | 6.899 ns | 7.416 ns | 6.336 ns | 6.559 ns | 5.861 ns |
| 90 pF | 8.917 ns | 7.709 ns | 8.218 ns | 7.124 ns | 7.323 ns | 6.498 ns |
| 100pF | 9.885 ns | 8.541 ns | 9.141 ns | 7.830 ns | 8.101 ns | 7.238 ns |

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

77

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

I/O timing variation with load capacitance: SPICE simulation results (continued)

Table 17. Timing Variation With Load Capacitance: [3.3 V] 10% - 90% [3 V] 10% - 90%

|  | WEAK | NOMINAL | STRONG |
| --- | --- | --- | --- |
|  | RISE | FALL | RISE | FALL | RISE | FALL |
| OpF | 0.404 ns | 0.361 ns | 0.371 ns | 0.310 ns | 0.321 ns | 0.284 ns |
| 10pF | 1.227 ns | 1.081 ns | 1.133 ns | 1.001 ns | 1.000 ns | 0.892 ns |
| 20 pF | 2.070 ns | 1.822 ns | 1.915 ns | 1.675 ns | 1.704 ns | 1.530 ns |
| 30 pF | 2.931 ns | 2.567 ns | 2.719 ns | 2.367 ns | 2.414 ns | 2.169 ns |
| 40 pF | 3.777 ns | 3.322 ns | 3.515 ns | 3.072 ns | 3.120 ns | 2.823 ns |
| 50 pF | 4.646 ns | 4.091 ns | 4.319 ns | 3.779 ns | 3.842 ns | 3.466 ns |
| 60 pF | 5.487 ns | 4.859 ns | 5.145 ns | 4.503 ns | 4.571 ns | 4.142 ns |
| 70 pF | 6.405 ns | 5.608 ns | 5.980 ns | 5.234 ns | 5.301 ns | 4.767 ns |
| 80 pF | 7.284 ns | 6.463 ns | 6.723 ns | 5.873 ns | 5.941 ns | 5.446 ns |
| 90 pF | 8.159 ns | 7.097 ns | 7.560 ns | 6.692 ns | 6.740 ns | 6.146 ns |
| 100 pF | 8.994 ns | 7.935 ns | 8.300 ns | 7.307 ns | 7.431 ns | 6.822 ns |

78

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

ready timing for externally generated wait states

timing requirements for externally generated wait states [H = 0.5 tC(co)]* (see Figure 21, Figure 22, Figure 23, and Figure 24)

|  | 'C54x-40 'LC54x-40 | 'LC54x-50 | '54x-66 | UNIT |
| --- | --- | --- | --- | --- |
|  | MIN MAX | MIN MAX | MIN MAX |  |
| 'su(RDY) Setup time, READY before CLKOUT low | 10 | 8 | 7 | ns |
| (h(RDY) Hold time, READY after CLKOUT low | 0 | 0 | 0 | ns |
| (v(RDY)MSTRB Valid time, READY after MSTRB lowt | 4H-15 | 4H-12 | 4H-10 | ns |
| (h(RDY)MSTRB Hold time, READY after MSTRB low! | 4H | 4H | 4H | ns |
| (v(RDY)IOSTRB Valid time, READY after IOSTRB low! | 5H-15 | 5H-12 | 5H-10 | ns |
| 'h(RDY)IOSTRB Hold time. READY after IOSTRB low! | 5H | 5H | 5H | ns |
| 'v(MSCL) Valid time. MSC low after CLKOUT low | 0 5 | 0 5 | 0 5 | ns |
| 'v(MSCH) Valid time. MSC ni9n after CLKOUT low | -2 3 | -2 3 | -2 3 | ns |

t The hardware wait states can be used only in conjunction with the software wait states to extend the bus cycles. To generate wait states by READY, at least two software wait states must be programmed. READY is not sampled until the completion of the internal software wait states. t These timings are included for reference only. The critical timings for READY are those referenced to CLKOUT.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

79

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

ready timing for externally generated wait states (continued)

CLKOUT

A[15:0]

X

)C

su(RDY)

I

lh(RDY)

READY

lv(RDY)MSTRB

►!— lh(RDY)MSTRB

MSTRB

\

I

\+~ tv(MSCH)

tv(MSCL)

MSC

\	/

Wait State 4— Generated

Wait States Generated Internally

by READY

Figure 21. Memory Read With Externally Generated Wait States

80

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

ready timing for externally generated wait states (continued)

CLKOUT

A[15:0]

D[15:0]

Wait States Generated Internally

READY

MSTRB

MSC

Wait State Generated by READY

Figure 22. Memory Write With Externally Generated Wait States

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

81

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

ready timing for externally generated wait states (continued)

Wait State Generated by READY

CLKOUT

A[15:0]

READY

IOSTRB

MSC

Wait

States

Generated

Internally

Figure 23. I/O Read With Externally Generated Wait States

82

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

ready timing for externally generated wait states (continued)

CLKOUT

A[15:0]

D[15:0]

lh(RDY)-*j

'su(RDY)

READY

\ I /

v(RDY)IOSTRB

IOSTRB

\

lh(RDY)IOSTRB

v(MSCH)

tv(MSCL)

MSC

/

Wait States Generated Internally

Wait State Generated by READY

Figure 24. I/O Write With Externally Generated Wait States

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

83

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

HOLD and HOLDA timing

switching characteristics over recommended operating conditions for memory control signals and HOLDA [H = 0.5 tc(CO)] (see Figure 25)

| PARAMETER | 'C54x-40 'LC54x-40 'LC54x-50 | '54x-66 | UNIT |
| --- | --- | --- | --- |
|  | MIN MAX | MIN MAX |  |
| 'dis(CLKL-A) Disable time, CLKOUT low to address, PS, DS, IS high impedance | 5 | 5 | ns |
| 'dis(CLKL-RW) Disable time, CLKOUT low to R/W high impedance | 5 | 5 | ns |
| Disable time, CLKOUT low to MSTRB, IOSTRB high tdis(CLKL-S) impedance | 5 | 5 | ns |
| (en(CLKL-A) Enable time, CLKOUT low to address, PS, DS, IS | 2H + 5 | 2H+5 | ns |
| 'en(CLKL-RW) Enable time, CLKOUT low to R/W enabled | 2H + 5 | 2H+5 | ns |
| 'en(CLKL-S) Enable time, CLKOUT low to MSTRB, IOSTRB enabled | 2H + 5 | 2H+5 | ns |
| tv(HOLDA) | Valid time, HOLDA low after CLKOUT low | -2 5 | 0 5 | ns |
|  | Valid time, HOLDA high after CLKOUT low | -2 5 | -2 3 | ns |
| 'w(HOLDA) Pulse duration, HOLDA low duration | 2H-3 | 2H-3 | ns |

timing requirements for HOLD [H = 0.5 tC(co)] (see Figure 25)

|  | 'C54x-40 'LC54x-40 'LC54x-50 | '54x-66 | UNIT |
| --- | --- | --- | --- |
|  | MIN MAX | MIN MAX |  |
| 'w(HOLD) Pulse duration, HOLD low duration | 4H + 10 | 4H + 10 | ns |
| 'su(HOLD) Setup time, HOLD before CLKOUT low | 10 | 10 | ns |

84

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

HOLD and HOLDA timing (continued)

CLKOUT HOLD"

HOLDA

\_

tw(HOLDA)

r

A[15:0] PS, DS, IS

I*- tdis(CLKL-A)

ten(CLKL-A)

D[15:0]

k tdis(CLKL-RW)

*en(CLKL-RW)

R/W

tdis(CLKL-S)

-►)— ten(CLKL-S)

MSTRB

-*\   \*~ ldis(CLKL-S)

en(CLKL-S)

IOSTRB

Figure 25. HOLD and HOLDA Timing (HM = 1)

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

85

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

reset, BIO, interrupt, and MP/MC timings

timing requirements for reset, interrupt, BIO, and MP/MC [H = 0.5 tC(co)] (see Figure 26, Figure 27, and Figure 28)

|  | 'C54x-40 'LC54x-40 | 'LC54x-50 | '54x-66 | UNIT |
| --- | --- | --- | --- | --- |
|  | MIN MAX | MIN MAX | MIN MAX |  |
| *h(RS) Hold time, RS after CLKOUT low | 0 | 0 | 0 | ns |
| (h(BIO) Hold time, Bl° after CLKOUT low | 0 | 0 | 0 | ns |
| *h(INT) Hold time, INTn, NM¦, after CLKOUT lowT | 0 | 0 | 0 | ns |
| th(MPMC) Hold time, MP/MC after CLKOUT low | 0 | 0 | 0 | ns |
| 'w(RSL) Pulse duration, RS lowT-SH | 4H + 10 | 4H + 10 | 4H+10 | ns |
| 'w(BIO)S Pulse duration, BIO low, synchronous | 2H+15 | 2H+12 | 2H+10 | ns |
| 'w(BIO)A Pulse duration, BIO low, asynchronous | 4H | 4H | 4H | ns |
| 'w(INTH)S Pulse duration, INTn, NMI high (synchronous) | 2H+15 | 2H+12 | 2H+10 | ns |
| 'w(INTH)A Pulse duration, INTn, NMI high (asynchronous) | 4H | 4H | 4H | ns |
| 'w(INTL)S Pulse duration, INTn, NMI low (synchronous) | 2H+15 | 2H+12 | 2H+10 | ns |
| 'w(INTL)A Pulse duration, INTn, NMI low (asynchronous) | 4H | 4H | 4H | ns |
| 'w(INTL)WKP Pulse duration, INTn, NMI low for IDLE2/IDLE3 wakeup | 10 | 10 | 10 | ns |
| 'su(RS) Setup time, RS before X2/CLKIN low§ | 5 | 5 | 5 | ns |
| (su(BIO) SetuP time, Bl° before CLKOUT low | 15 | 12 | 10 | ns |
| 'su(INT) SetuP time. INTn. NM¦. RS before CLKOUT low | 15 | 12 | 10 | ns |
| 'su(MPMC) SetuP time. MP/MC before CLKOUT low | 10 | 10 | 10 | ns |

"TThe external interrupts (INTO-INT3, NMI) are synchronized to the core CPU by way of a two flip-flop synchronizer which samples these inputs with consecutive falling edges of CLKOUT. The input to the interrupt pins is required to represent a 1-0-0 sequence at the timing that is corresponding to three CLKOUTs sampling sequence.

t If the PLL mode is selected, then at power-on sequence, or at wakeup from I DLE3.RS must be held low for at least 50 |is to assure synchronization and lock-in of the PLL.

§ Divide-by-two mode

11 Note that RS may cause a change in clock frequency, therefore changing the value of H (see the PLL section).

86

^? Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

reset, BIO, interrupt, and MP/MC timings (continued)

X2/CLKIN

"►I    \<~ lsu(RS)

w(RSL)

RS, INTn, NMI

lsu(INT)

-^

CLKOUT

>	/

lsu(BIO)

lh(BIO)

\

BIO

r

w

lw(BIO)S

Figure 26. Reset and BIO Timings

CLKOUT

INTn, NMI

lw(INTL)A

Figure 27. Interrupt Timing

CLKOUT

RS

MP/MC

Figure 28. MP/MC Timing

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

87

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

instruction acquisition (IAQ), interrupt acknowledge (lACK), external flag (XF), and TOUT timing

switching characteristics over recommended operating conditions for IAQ and IACK [H = 0.5 tc(CO)] (see Figure 29)

| PARAMETER | 'C54x-40 'LC54x-40 'LC54x-50 '54x-66 MIN MAX | UNIT |
| --- | --- | --- |
| 'd(CLKL-IAQL) Delay time, IAQ low from CLKOUT low | 0 5 | ns |
| 'd(CLKL-IAQH) Delay time, IAQ high from CLKOUT low | -2 3 | ns |
| 'd(A)IAQ Delay time, address valid before IAQ low | 4 | ns |
| 'd(CLKL-IACKL) Delay time, IACK low from CLKOUT low | -2 3 | ns |
| 'd(CLKL-IACKH) Delay time , IACK high from CLKOUT low | -2 3 | ns |
| 'd(A)IACK Delay time, address valid before IACK low | 3 | ns |
| 'h(A)IAQ Hold time> address valid after IAQ high | 0 | ns |
| 'h(A)IACK Hold time. address valid after IACK high | 0 | ns |
| 'w(IAQL) Pulse duration, IAQ low | 2H-10 | ns |
| 'w(IACKL) Pulse duration, IACK low | 2H-10 | ns |

CLKOUT

\

Y

A[15:0]

X

X

td(CLKL-IAQL) —\4

-►I

td(A)IAQ

►I- td(CLKL-IAQH)

I

lh(A)IAQ

IAQ

w(IAQL)

I

-►I

7

td(CLKL-IACKL)

ld(A)IACK

I

-►r- td(CLKL-IACKH)

T

lh(A)IACK

IACK

tw(IACKL)

7

MSTRB

\

Figure 29. Instruction Acquisition (IAQ) and Interrupt Acknowledge (lACK) Timing

88

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

instruction acquisition (IAQ), interrupt acknowledge (IACK), external flag (XF), and TOUT timing (continued)

switching characteristics over recommended operating conditions for external flag (XF) and TOUT [H = 0.5 tC(co)] (see Figure 30 and Figure 31)

| PARAMETER | 'C54x-40 'LC54x-40 'LC54x-50 '54x-66 | UNIT |
| --- | --- | --- |
|  | MIN MAX |  |
| *d(XF) | Delay time, XF high after CLKOUT low | -2 3 | ns |
|  | Delay time, XF low after CLKOUT low | 0 5 |  |
| 'd(TOUTH) Delay time, TOUT high after CLKOUT low | -2 3 | ns |
| 'd(TOUTL) Delay time, TOUT low after CLKOUT low | -2 3 | ns |
| 'w(TOUT) Pulse duration, TOUT | 2H-10 | ns |

CLKOUT

\

\

\

td(XF)

XF

X

Figure 30. External Flag (XF) Timing

ld(TOUTH) —f*	H	\4	N— td(TOUTL)

CLKOUT

TOUT

\

2

— tw(TOUT) "

Figure 31. TOUT Timing

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

89

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

serial port receive timing

timing requirements for serial port receive [H = 0.5 tC(co)] (see Figure 32)

|  | 'C54x-40 'LC54x-40 | 'LC54x-50 | '54x-66 | UNIT |
| --- | --- | --- | --- | --- |
|  | MIN MAX | MIN MAX | MIN MAX |  |
| 'c(SCK) Cycle time, serial port clock | 6H t | 6H t | 6H t | ns |
| (f(SCK) Fall time> serial port clock | 6 | 6 | 6 | ns |
| 'r(SCK) Rise time, serial port clock | 6 | 6 | 6 | ns |
| 'w(SCK) Pulse duration, serial port clock low/high | 3H | 3H | 3H | ns |
| 'su(FSR) Setup time, FSR before CLKR falling edge | 7 | 6 | 6 | ns |
| (h(FSR) Hold time, FSR after CLKR falling edge | 7 | 6 | 6 | ns |
| 'h(DR) Hold time. DR after CLKR falling edge | 7 | 6 | 6 | ns |
| 'su(DR) Setup time, DR before CLKR falling edge | 7 | 6 | 6 | ns |

t The serial port design is fully static and, therefore, can operate with WscK) approaching ∞. It is characterized approaching an input frequency ofO Hz but tested at a much higher frequency to minimize test time.

tf(SCK)

CLKR

FSR

DR BIT

1	2

Figure 32. Serial Port Receive Timing

X

7/15

X

8/16

90

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

serial port transmit timing

switching characteristics over recommended operating conditions for serial port transmit with external clocks and frames (see Figure 33)

| PARAMETER | 'C54x-40 'LC54x-40 | 'LC54x-50 | '54x-66 | UNIT |
| --- | --- | --- | --- | --- |
|  | MIN MAX | MIN MAX | MIN MAX |  |
| 'd(DX) Delay time, DX valid after CLKX rising | 25 | 25 | 25 | ns |
| 'h(DX) Hold time, DX valid after CLKX rising | -5 | -5 | -5 | ns |
| 'dis(DX) Disable time, DX after CLKX rising | 40 | 40 | 40 | ns |
| timing requirements for serial port transmit with external clocks and frames [H = 0.5tc/co)] (see Figure 33) |
|  | 'C54x-40 'LC54x-40 | 'LC54x-50 | '54x-66 | UNIT |
|  | MIN MAX | MIN MAX | MIN MAX |  |
| 'c(SCK) Cycle time, serial port clock | 6H t | 6H t | 6H t | ns |
| 'd(FSX) Delay time, FSX after CLKX rising edge | 2H-8 | 2H-5 | 2H-5 | ns |
| (h(FSX) Hold time, FSX after CLKX falling edge (see Note 1) | 7 | 6 | 6 | ns |
| 'h(FSX)H Hold time> FSX after CLKX rising edge (see Note 1) | 2H-8* | 2H-5* | 2H-5* | ns |
| 'f(SCK) Fall time, serial port clock | 6 | 6 | 6 | ns |
| 'r(SCK) Rise time> serial port clock | 6 | 6 | 6 | ns |
| 'w(SCK) Pulse duration, serial port clock low/high | 3H | 3H | 3H | ns |

t The serial port design is fully static and, therefore, can operate with tc(sCK) approaching ~. It is characterized approaching an input frequency

of 0 Hz but tested at a much higher frequency to minimize test time. t If the FSX pulse does not meet this specification, the first bit of serial data is driven on DX until the falling edge of FSX. After the falling edge of

FSX, data is shifted out on DX pin. The transmit buffer-empty interrupt is generated when the th(FSX) and 'h(FSX)H specification is met. NOTE 1:  Internal clock with external FSX and vice versa are also allowable. However, FSX timings to CLKX always are defined depending on the source of FSX, and CLKX timings always are dependent upon the source of CLKX. Specifically, the relationship of FSX to CLKX is independent of the source of CLKX.

-H I-*- tf(SCK)

CLKX

FSX

DXBIT

1	2	7/15	8/16

Figure 33. Serial Port Transmit Timing With External Clocks and Frames

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

91

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

serial port transmit timing (continued)

switching characteristics over recommended operating conditions for serial port transmit with internal clocks and frames [H = 0.5tC(co)] (see Figure 34)

| PARAMETER | 'C54x-40 'LC54x-40 'LC54x-50 | '54x-66 | UNIT |
| --- | --- | --- | --- |
|  | MIN TYP MAX | MIN TYP MAX |  |
| 'c(SCK) Cycle time, serial port clock | 8H | 8H | ns |
| 'd(FSX) Delay time, CLKX rising to FSX | 15 | 15 | ns |
| 'd(DX) Delay time, CLKX rising to DX | 15 | 15 | ns |
| 'dis(DX) Disable time, CLKX rising to DX | 20 | 20 | ns |
| 'h(DX) Hold time, DX valid after CLKX rising edge | -5 | -5 | ns |
| tf(scK) Fall time, serial port clock | 4 | 4 | ns |
| 'r(SCK) Rise time, serial port clock | 4 | 4 | ns |
| 'w(SCK) Pulse duration, serial port clock low/high | 4H-8 | 4H-8 | ns |

H	lc(SCK)

I

-H I-*- tf(SCK)

CLKX

FSX

DX

1	2	7/15	8/16

Figure 34. Serial Port Transmit Timing With Internal Clocks and Frames

92

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

buffered serial port receive timing

timing requirements for buffered serial port receive (see Figure 35)

|  | 'C54x-40 'LC54x-40 | '54x-50 '54x-66 | UNIT |
| --- | --- | --- | --- |
|  | MIN MAX | MIN MAX |  |
| 'c(SCK) Cycle time, serial port clock | 25 t | 20 t | ns |
| 'f(SCK) Fall time> serial port clock | 4 | 4 | ns |
| 'r(SCK) Rise time> serial port clock | 4 | 4 | ns |
| 'w(SCK) Pulse duration, serial port clock low/high | 8.5 | 6 | ns |
| 'su(BFSR) Setup time, BFSR before BCLKR falling edge (see Note 2) | 2 | 2 | ns |
| (h(BFSR) Hold time, BFSR after BCLKR falling edge (see Note 2) | 10 tc(scK)-2* | 10 tc(scK)-2* | ns |
| (su(BDR) Setup time, BDR before BCLKR falling edge | 0 | 0 | ns |
| 'h(BDR) Hold time. BDR after BCLKR falling edge | 10 | 10 | ns |

t The serial port design is fully static and therefore can operate with tc(scK) approaching infinity. It is characterized approaching an input frequency

of 0 Hz but tested at a much higher frequency to minimize test time. t First bit is read when BFSR is sampled low by BCLKR clock. NOTE 2: Timings for BCLKR and BFSR are given with polarity bits (BCLKP and BFSP) set to 0.

tc(SCK)

8/10/12/16

BCLKR

BFSR

BDR

Figure 35. Buffered Serial Port Receive Timing

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

93

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

buffered serial port transmit timing of external frames

switching characteristics over recommended operating conditions for buffered serial port transmit of external frames (see Figure 36)

| PARAMETER | 'C54x-40 'LC54x-40 'LC54x-50 | '54x-66 | UNIT |
| --- | --- | --- | --- |
|  | MIN MAX | MIN MAX |  |
| 'd(BDX) Delay time, BDX valid after BCLKX rising | 18 | 18 | ns |
| 'dis(BDX) Disable time, BDX after BCLKX rising | 4 6 | 4 6 | ns |
| 'dis(BDX)pcm Disable time, PCM mode, BDX after BCLKX rising | 6 | 6 | ns |
| 'en(BDX)pcm Enable time, PCM mode, BDX after BCLKX rising | 8 | 8 | ns |
| 'h(BDX) Hold time> BDX valid after BCLKX rising | 4 | 2 | ns |

timing requirements for buffered serial port transmit of external frames (see Figure 36)

|  | 'C54x-40 'LC54x-40 | '54x-50 '54x-66 | UNIT |
| --- | --- | --- | --- |
|  | MIN MAX | MIN MAX |  |
| 'c(SCK) Cycle time, serial port clock | 25 t | 20 t | ns |
| 'f(SCK) Fall time, serial port clock | 4 | 4 | ns |
| 'r(SCK) Rise time> serial port clock | 4 | 4 | ns |
| 'w(SCK) Pulse duration, serial port clock low/high | 8.5 | 6 | ns |
| 'h(BFSX) Hold time> BFSX after CLKX falling edge (see Notes 3 and 4) | 6 *c(SCK)-6* | 6 *c(SCK)-6* | ns |
| 'su(BFSX) Setup time, FSX before CLKX falling edge (see Notes 3 and 4) | 6 | 6 | ns |

t The serial port design is fully static and therefore can operate with tc(sCK) approaching infinity. It is characterized approaching an input frequency

ofO Hz but tested at a much higher frequency to minimize test time. t If BFSX does not meet this specification, the first bit of the serial data is driven on BDX until BFSX goes low (sampled on falling edge of BCLKX).

After falling edge of the BFSX, data will be shifted out on the BDX pin. NOTES:  3. Internal clock with external BFSX and vice versa are also allowable. However, BFSX timings to BCLKX always are defined

depending on the source of BFSX, and BCLKX timings always are dependent upon the source of BCLKX. 4. Timings for BCLKX and BFSX are given with polarity bits (BCLKP and BFSP) set to 0.

94

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

buffered serial port transmit timing of external frames (continued)

tc(SCK) -H

-H I-*- tf(SCK)

BCLKX

BFSX

BDX

1	2	8/10/12/16

Figure 36. Buffered Serial Port Transmit Timing of External Clocks and External Frames

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

95

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

buffered serial port transmit timing of internal frame and internal clock

switching characteristics over recommended operating conditions for buffered serial port transmit of internal frame and internal clock [H = 0.5tc(CO)] (see Figure 37)

| PARAMETER | 'C54x-40 'LC54x-40 'LC54x-50 | '54x-66 | UNIT |
| --- | --- | --- | --- |
|  | MIN MAX | MIN MAX |  |
| 'c(SCK) Cycle time, serial port clock, internal clock | 2H 62H | 20 62H | ns |
| Delay time, BFSX after BCLKX rising edge ld(BFSX) (see Notes 3 and 4) | 10 | 10 | ns |
| 'd(BDX) Delay time, BDX valid after BCLKX rising edge | 8 | 8 | ns |
| 'dis(BDX) Disable time, BDX after BCLKX rising edge | 0 5 | 0 5 | ns |
| 'dis(BDX)pcm Disable time, PCM mode, BDX after BCLKX rising edge | 5 | 5 | ns |
| 'en(BDX)pcm Enable time, PCM mode, BDX after BCLKX rising edge | 7 | 7 | ns |
| (h(BDX) Hold time, BDX valid after BCLKX rising edge | 0 | 0 | ns |
| (f(SCK) Fa"time. serial port clock | 4 | 4 | ns |
| 'r(SCK) R'se time, serial port clock | 4 | 4 | ns |
| 'w(SCK) Pulse duration, serial port clock low/high | H-4 | 6 | ns |

NOTES:  3. Internal clock with external BFSX and vice versa are also allowable. However, BFSX timings to BCLKX always are defined

depending on the source of BFSX, and BCLKX timings always are dependent upon the source of BCLKX. 4. Timings for BCLKX and BFSX are given with polarity bits (BCLKP and BFSP) set to 0.

lc(SCK)

-H  I*- tf(SCK)

y-

BCLKX

BFSX

BDX

1	2	8/10/12/16

Figure 37. Buffered Serial Port Transmit Timing of Internal Clocks and Internal Frames

96

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

serial-port receive timing in TDM mode

timing requirements for serial-port receive in TDM mode [H = 0.5tC(co)] ('542/'543 only) (see Figure 38)

|  | '542 '543 MIN MAX | UNIT |
| --- | --- | --- |
| 'c(SCK) Cycle time, serial-port clock | 8H t | ns |
| 'f(SCK) Fall time, serial-port clock | 6 | ns |
| 'r(SCK) Rise time, serial-port clock | 6 | ns |
| 'w(SCK) Pulse duration, serial-port clock low/high | 4H | ns |
| 'su(TD-TCL) Setup time, TDAT/TADD before TCLK falling edge | -(3H-9) | ns |
| 'h(TCH-TD) Hold time, TDAT/TADD after TCLK rising edge, tw(sCKL) < 5H | 0 | ns |
| th(TCL-TD) Hold time, TDAT/TADD after TCLK falling edge, tw(scKL) > 5H | 5H+5 | ns |
| 'su(TF-TCH) Setup time, TFRM before TCLK rising edgef | 10 | ns |
| 'h(TCH-TF) Hold time, TFRM after TCLK rising edgef | 10 | ns |

t The serial-port design isfullystaticand, therefore, can operate with tc(sCK) approaching infinity. It is characterized approaching an input frequency

of 0 Hz but tested at a much higher frequency to minimize test time. t TFRM timing and waveforms shown in Figure 38 are for external TFRM. TFRM can also be configured as internal. The TFRM internal case is

illustrated in the transmit timing diagram in Figure 39.

timing requirements for serial-port receive in TDM mode [H = 0.5tc/co)] ('54x devices other than '542/'543) (see Figure 38)

|  | 'C54x-40 'LC54x-40 'LC54x-50 | '54X-66 | UNIT |
| --- | --- | --- | --- |
|  | MIN MAX | MIN MAX |  |
| 'c(SCK) Cycle time, serial-port clock | 8H t | 16H t | ns |
| 'f(SCK) Fall time, serial-port clock | 6 | 6 | ns |
| 'r(SCK) Rise time, serial-port clock | 6 | 6 | ns |
| 'w(SCK) Pulse duration, serial-port clock low/high | 4H | 8H | ns |
| 'su(TD-TCH) Setup time, TDAT/TADD before TCLK rising edge | 25 | 10 | ns |
| 'h(TCH-TD) Hold time> TDAT/TADD after TCLK rising edge | -6 | 1 | ns |
| 'su(TF-TCH) Setup time, TFRM before TCLK rising edgef | 10 | 10 | ns |
| 'h(TCH-TF) Hold time> TFRM after TCLK rising edgef | 10 | 10 | ns |

t The serial-port design isfullystaticand, therefore, can operate with WsCK) approaching infinity. It is characterized approaching an input frequency

of 0 Hz but tested at a much higher frequency to minimize test time. t TFRM timing and waveforms shown in Figure 38 are for external TFRM. TFRM can also be configured as internal. The TFRM internal case is

illustrated in the transmit timing diagram in Figure 39.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

97

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

"H I*- tf(SCK)

su(TD-TCL)

- tsu(TD-TCH)+| f- th(TCH-TD) J

serial-port receive timing in TDM mode (continued)

tw(SCK) -^	►

tsu(TD-TCL)*

<

TCLK

|<— lc(SCK) -*|

TDAT

B14

th(TCL-TD)*	f<	>

B15

A1

TADD

TFRM

A0

B12

A3

"H I"*" tr(scK) th(TCL-TD)*

B1

A4      A7

t All devices except '542/'543 t '542/'543 only

Figure 38. Serial-Port Receive Timing in TDM Mode

98

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

serial-port transmit timing in TDM mode

switching characteristics over recommended operating conditions for serial-port transmit in TDM mode [H = 0.5tC(co)] (see Figure 39)

| PARAMETER | '542 '543 | 'C54x-40 'LC54x-40 'LC54x-50 | UNIT |
| --- | --- | --- | --- |
|  | MIN MAX | MIN MAX |  |
| 'h(TCH-TDV) Hold time> TDAT/TADD valid after TCLK rising edge, TCLK external | 3 | 0 | ns |
| 'h(TCH-TDV) Hold time. TDAT/TADD valid after TCLK rising edge, TCLK internal | 1 | -5 | ns |
| (d(TCH-TFV) | Delay time, TFRM valid after TCLK rising edge TCLK extt | H-3 3H + 22 | H-3 3H + 22 | ns |
|  | Delay time, TFRM valid after TCLK rising edge, TCLK intt | H-3 3H + 12 | H-3 3H + 12 |  |
| td(TC-TDV) | Delay time, TCLK to valid TDAT/TADD, TCLKext | 18 | 25 | ns |
|  | Delay time, TCLK to valid TDAT/TADD, TCLKint | 18 | 18 |  |

t TFRM timing and waveforms shown in Figure 39 are for internal TFRM. TFRM can also be configured as external. The TFRM external case is illustrated in the receive timing diagram in Figure 38.

switching characteristics over recommended operating conditions for serial-port transmit in TDM mode [H = 0.5tC(co)] (see Figure 39)

| PARAMETER | '54x-66 | UNIT |
| --- | --- | --- |
|  | MIN MAX |  |
| 'h(TCH-TDV) Hold time> TDAT/TADD valid after TCLK rising edge, TCLK external | 1 | ns |
| 'h(TCH-TDV) Hold time. TDAT/TADD valid after TCLK rising edge, TCLK internal | 1 | ns |
| (d(TCH-TFV) | Delay time, TFRM valid after TCLK rising edge, TCLK extt | H-3 3H+22 | ns |
|  | Delay time, TFRM valid after TCLK rising edge, TCLK intt | H-3 3H+12 |  |
| (d(TC-TDV) | Delay time, TCLK to valid TDAT/TADD, TCLKext | 25 | ns |
|  | Delay time, TCLK to valid TDAT/TADD, TCLKint | 18 |  |

t TFRM timing and waveforms shown in Figure 39 are for internal TFRM. TFRM can also be configured as external. The TFRM external case is illustrated in the receive timing diagram in Figure 38.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

99

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

serial-port transmit timing in TDM mode (continued)

timing requirements for serial-port transmit in TDM mode [H = 0.5tC(co)] (see Figure 39)

|  |  | 'C54x-40 'LC54x-40 'LC54x-50 | '54X-66 |  | UNIT |
| --- | --- | --- | --- | --- | --- |
|  |  | MIN MAX | MIN | MAX |  |
| (c(SCK) | Cycle time, serial-port clock | 8Ht t | 16Ht | t | ns |
| tf(SCK) | Fall time, serial-port clock | 6 |  | 6 | ns |
| (r(SCK) | Rise time, serial-port clock | 6 |  | 6 | ns |
| (w(SCK) | Pulse duration, serial-port clock low/high | 4Ht | 8Ht |  | ns |

t When SCK is generated internally, this value is typical. t The serial-port design is fully static and, therefore, can operate with tc(scK) approaching oo. It is characterized approaching an input frequency of 0 Hz but tested as a much higher frequency to minimize test time.

B14     )(     B13     )(B12    " B8XB7     " B2X      B1

TCLK

TDAT

TADD

TFRM

lw(SCK)

Figure 39. Serial-Port Transmit Timing in TDM Mode

100

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

host-port interface timing

switching characteristics over recommended operating conditions for host-port interface [H = 0.5tC(co)] (see Note 5, Note 6, and Figure 40 through Figure 43)

| PARAMETER | 'C54x-40 'C54x-50 'C54x-66 | UNIT |
| --- | --- | --- |
|  | MIN MAX |  |
| 'd(DSL-HDV) Delay time, DS low to HD driven | 5 12 | ns |
| Delaytime, HDS falling to HDvalidforfirstbyte (d(HEL-HDV1) Of a non-subsequent read: -> max 20 nstt | Case 1: Shared-access mode if (w(DSH) < 7H | 7H+20-tw(DSH) | ns |
|  | Case 2: Shared-access mode if (w(DSH) > 7H | 20 |  |
|  | Case 3: Host-only mode if *w(DSH) < 20 ns | 4°-tw(DSH) |  |
|  | Case 4: Host-only mode if *w(DSH) > 20 ns | 20 |  |
| (d(DSL-HDV2) Delay time, DS low to HD valid, second byte | 5* 20 | ns |
| 'd(DSH-HYH) Delay time, DS high to HRDY high | 10H+10 | ns |
| 'su(HDV-HYH) Setuptime, HD valid before HRDY rising edge | 3H-10 | ns |
| 'h(DSH-HDV)R Hold time, HD valid after DS rising edge, read | 0 12 | ns |
| 'd(COH-HYH) Delay time, CLKOUT rising edge to HRDY high | 10 | ns |
| td(DSH-HYL) DelaYtime, HDS or HCS ni9n to HRDY low | 12 | ns |
| 'd(COH-HTX) Delay time, CLKOUT rising edge to HINT change | 15 | ns |

t Host-only mode timings apply for read accesses to HPIC or HPIA, write accesses to BOB, and resetting DSPINT or HINT to 0 in shared-access

mode. HRDY does not go low for these accesses. t Shared-access mode timings will be met automatically if HRDY is used. NOTES:  5. SAM = shared-access mode, HOM = host-only mode HAD stands for HCNTRL0, HCNTRU.and HR/W. HDS refers to either HDS1 or HDS2. DS refers to the logical OR of HCS and HDS.

6. On host read accesses to the HPI, the setup time of HD before DS rising edge depends on the host waveforms and cannot be specified here.

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

101

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

host-port interface timing (continued)

timing requirements for host-port interface [H = 0.5tc/co)] (see Note 5 and Figure 40 through Figure 43)

|  | 'C54x-40 'C54x-50 'C54x-66 | UNIT |
| --- | --- | --- |
|  | MIN MAX |  |
| 'su(HBV-DSL) Setup time, HAD/HBIL valid before DS or HAS falling edge | 10 | ns |
| 'h(DSL-HBV) Hold time. HAD/HBIL valid after DS or HAS falling edge | 5 | ns |
| 'su(HSL-DSL) Setup time, HAS low before DS falling edge | 12 | ns |
| 'w(DSL) Pulse duration, DS low | 30t | ns |
| 'w(DSH) Pulse duration, DS high | 10 | ns |
| + Cycle time, DS rising edge to next DS *c(DSH-DSH)T rising edge | Case 1: HOM access timings (see Access Timing Without HRDY) | 50 | ns |
|  | Case 2a: SAM accesses and HOM active writes to DSPINTorHINT. (see Access Timings With HRDY) | 10H |  |
| 'su(HDV-DSH) Setup time, HD valid before DS rising edge | 12 | ns |
| 'd(DSH-HSL)^ Delay time, DS high to next HAS low | 10H | ns |
| 'h(DSH - HDV)W Hold time. HD valid after DS risin9 ed9e, write | 3 | ns |

t A host not using HRDY should meet the 10H requirement all the time unless a software handshake is used to change the access rate according

to the HPI mode.

t Must only be met if HAS is going low when not accessing the HPI (as would be the case where multiple devices are being driven by one host). NOTE 5: SAM = shared-access mode, HOM = host-only mode

HAD stands for HCNTRL0, HCNTRL1, and HR/W.

HDS refers to either HDS1 or HDS2.

DS refers to the logical OR of HCS and HDS.

102

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

host-port interface timing (continued)

FIRST BYTE

SECOND BYTE

vand

w(DSH)

hcs y~ ~\

HDS     A	A

ld(HEL-HDV1)

th(DSH-HDV)R

lh(DSH-HDV)W

HAD

HBIL

HD READ

HD WRITE

th(DSL-HBV) tsu(HBV-DSL)

th(DSL-HBV)

>]— tsu(HBV-DSL)

Figure 40. Read/Write Access Timings Without HRDY or HAS

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

103

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

tsu(HBV-DSL)

lh(DSL-HBV)

{*— th(DSL-HBV)T

host-port interface timing (continued)

Valid

FIRST BYTE

HD WRITE

ld(HEL-HDV1) td(DSL-HDV) "

SECOND BYTE

tc(DSH-DSH)

\

lh(DSH-HDV)R

I

td(DSL-HDV2)

l -/     Valid      \

tsu(HDV-DSH) -\4 *h(DSH-HDV)W |

-f

Valid

I

-►I	 td(DSH-HSL)

*h(DSH-HDV)R

lh(DSH-HDV)W

twhen HAS is tied to

Figure 41. Read/Write Access Timings Using HAS Without HRDY

104

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

host-port interface timing (continued)

SECOND BYTE

HAS

tsu(HBV-DSL) HAD

lsu(HBV-DSL) HBIL

w(DSH)

HCS HDS

►(— ts

ld(DSH-HYH)

su(HDV-HYH)

HRDY

*d(HEL7HDV1)

td(DSH-HYL)

H	»j	ld(DSL-HDV2)

*h(DSH-HDV)R

lh(DSH-HDV)R

HD READ

Valid

su(HDV-DSH)

4	>

su(HDV-DSH)

*h(DSH-HDV)W

HD WRITE

Valid

Valid

H	td(COH-HYH)

CLKOUT

HINT

td(COH-HTX)

tWhen HAS is tied to VDD

Figure 42. Read/Write Access Timing With HRDY

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

105

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

host-port interface timing (continued)

HCS

td(DSH-HYL)

HRDY	\	jf

\*	 ld(DSH-HYH)

HDS

\

Figure 43. HRDY Signal When HCS is Always Low

^ Texas Instruments

1 06	POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

MECHANICAL DATA

TMS320LC542/'LC545 128-Pin Thin Plastic Quad Flatpack (TQFP)

PBK (S-PQFP-G128)	PLASTIC QUAD FLATPACK

0,40 96

0,23 0,13

65

0,07 (M)

97

64

0,13 NOM

0,05 MIN

0°-7c

128.

o

12,40 TYP 14,20

SQ

SQ

13,80 16,20 15,80

32

33

|  | 1,45 ~~ 1^35 | /^ | ^\ |
| --- | --- | --- | --- |
| ik i |  |  | i=, \ I |
|  | r ,JT |  | ^L-1 ▼ Seating Plane |
|  | 1,60 MAX ^~ | / t |
| 1— |  | —^ ! ^ 0,08 |

0,75 0^45

4040279-3/B 03/95

NOTES: A. All linear dimensions are in millimeters.

B. This drawing is subject to change without notice.

Thermal Resistance Characteristics

| PARAMETER | °c/w |
| --- | --- |
| RGJA | 58 |
| Rgjc | 10 |

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

107

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

MECHANICAL DATA

TMS320C542/'LC542/'LC548, 'LC549, 'VC549 144-Pin Thin Plastic Quad Flatpack (TQFP)

PGE (S-PQFP-G144)	PLASTIC QUAD FLATPACK

108

73

109 '

72

0,27

0,08 (M)

0,13 NOM

0,05 MIN

0°-7c

144 i

o

17,50 TYP

SQ

SQ

20,20 19,80 22,20 21,80

36

-►

37

1,45 1,35

— 1,60 MAX

0,75 0,45

Seating Plane

0,08

4040147/B 10/94

NOTES: A. All linear dimensions are in millimeters.

B.	This drawing is subject to change without notice.

C.	Falls within JEDEC MO-136

Thermal Resistance Characteristics

| PARAMETER | °c/w |
| --- | --- |
| RGJA | 56 |
| Rgjc | 5 |

108

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C- FEBRUARY 1996- REVISED DECEMBER 1999

MECHANICAL DATA

TMS320C541/'LC541/'LC543/'LC546 100-Pin Thin Plastic Quad Flatpack (TQFP)

PZ (S-PQFP-G100)	PLASTIC QUAD FLATPACK

0,50 75

51

0,27

76

50

0,13 NOM

0,05 MIN

0°-7c

100i

o

12,00 TYP 14,20

SQ

SQ

13,80 16,20 15,80

25

-►

26

1,45

L- 1,60 MAX

,,   Seating Plane

0,08

0,75 0,45

4040149 /B 10/94

NOTES: A. All linear dimensions are in millimeters.

B.	This drawing is subject to change without notice.

C.	Falls within JEDEC MO-136

Thermal Resistance Characteristics

| PARAMETER | °C/W |
| --- | --- |
| RGJA | 58 |
| RGJC | 10 |

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

109

TMS320C54x, TMS320LC54x, TMS320VC54x FIXED-POINT DIGITAL SIGNAL PROCESSORS

SPRS039C - FEBRUARY 1996 - REVISED DECEMBER 1999

MECHANICAL DATA

TMS320LC548, TMS320LC549, and TMS320VC549 144-Pin Plastic Ball Grid Array Package (BGA)
GGU (S-PBGA-N144)	PLASTIC BALL GRID ARRAY PACKAGE

12,10

11,90

SQ

13 12 11 10 9  8 7 6 5 4 3 2  1

o o o o o o o o o o o o o o o o o o

Q O Q

-o o o o o o o o o o o o o o o o o o

O O O C)	O

O O O C)	O

O O O C)	O

O O O Q	O

o
o
e

o o

000(1)0 O O O C) O O O O () O O O O () O

o o o o o o o o o o o o

o o o

o o o

o o o

o o o

o o

o o

Q Q O O

o o o o o o o o o o o o

o o o o o o o o o o o o o o o o

A B

C

D

E F G H

J

K

L M N

1,40 MAX

4073221/A 11/96

NOTES: A. All linear dimensions are in millimeters.

B. This drawing is subject to change without notice.

Thermal Resistance Characteristics

| PARAMETER | °c/w |
| --- | --- |
| Rgja | 38 |
| Rgjc | 5 |

110

^ Texas Instruments

POST OFFICE BOX 1443 • HOUSTON, TEXAS 77251-1443

IMPORTANT NOTICE

Texas Instruments and its subsidiaries (TI) reserve the right to make changes to their products or to discontinue any product or service without notice, and advise customers to obtain the latest version of relevant information to verify, before placing orders, that information being relied on is current and complete. All products are sold subject to the terms and conditions of sale supplied at the time of order acknowledgement, including those pertaining to warranty, patent infringement, and limitation of liability.

TI warrants performance of its semiconductor products to the specifications applicable at the time of sale in accordance with TI's standard warranty. Testing and other quality control techniques are utilized to the extent TI deems necessary to support this warranty. Specific testing of all parameters of each device is not necessarily performed, except those mandated by government requirements.

CERTAIN APPLICATIONS USING SEMICONDUCTOR PRODUCTS MAY INVOLVE POTENTIAL RISKS OF DEATH, PERSONAL INJURY, OR SEVERE PROPERTY OR ENVIRONMENTAL DAMAGE ("CRITICAL APPLICATIONS"). TI SEMICONDUCTOR PRODUCTS ARE NOT DESIGNED, AUTHORIZED, OR WARRANTED TO BE SUITABLE FOR USE IN LIFE-SUPPORT DEVICES OR SYSTEMS OR OTHER CRITICAL APPLICATIONS. INCLUSION OF TI PRODUCTS IN SUCH APPLICATIONS IS UNDERSTOOD TO BE FULLY AT THE CUSTOMER'S RISK.

In order to minimize risks associated with the customer's applications, adequate design and operating safeguards must be provided by the customer to minimize inherent or procedural hazards.

TI assumes no liability for applications assistance or customer product design. TI does not warrant or represent that any license, eitherexpress or implied, isgranted underany patent right, copyright, mask work right, orother intellectual property right of TI covering or relating to any combination, machine, or process in which such semiconductor products or services might be or are used. TI's publication of information regarding any third party's products or services does not constitute TI's approval, warranty or endorsement thereof.

Copyright© 1999, Texas Instruments Incorporated