Робоча частота 20МHz

Діапазон температури  –55°C до 125°C.

Пам’ять даних RAM 1Kx16

Пам’ять програм RAM 2k x 24

2 Serial Port

Host Interface Port

| Pin Name(s) | # of Pins | Input /Output | Function |
| --- | --- | --- | --- |
| ADDR | 14 | О | Шина адреси |
| DATA | 24 | I/O | Шина даних |
| ______ RESET | 1 | І | Загальний скид процесора |
| ____ IRQ2 | 1 | І | Запит на зовнішнє переривання |
| ___ BR2 | 1 | І | Запит використання зовнішньої шини |
| __ BG | 1 | О | Дозвіл викоритстання зовнішньої шини |
| ____ PMS | 1 | О | Вибір зовнішньої пам’яті програм |
| ____ DMS | 1 | О | Вибір зовнішньої пам’яті даних |
| ____ BMS | 1 | О | Вибір boot пам’яті |
| __ RD | 1 | О | Дозвіл читання з зовнішньої пам’яті |
| ___ WR | 1 | О | Дозвіл запису у зовннішню пам’ятть WR |
| MMAP | 1 | І | Вибір карти пам’яті |
| CLKIN, XTAL | 2 | І | Зовнішній Clock або кварцовий генератор |
| CLKOUT | 1 | О | Вихід таймера процесора |
| VDD |  |  | Живлення |
| GND |  |  | Земля |
| SPORT0 | 5 | І/О | Serial Port 0 Pins (TFS0, RFS0, DT0, DR0, SCLK0) |
| SPORT1 | 5 | І/О | Serial Port 1 Pins (TFS1, RFS1, DT1, DR1, SCLK1) |
| ____ IRQ0 (RFS1) | 1 | І | Запит на зовнішнє переривання #0 |
| ____ IRQ1 (TFS1) | 1 | І | Запит на зовнішнє переривання #1 |
| FI (DR1) | 1 | І | Вхід флага |
| FO (DT1) | 1 | О | Вихід флага |
| FL2–0 | 3 | О | Загальні виходи флага |
| ____ HSEL | 1 | І | Вибір НІР |
| _____ HACK | 1 | О | Визначення НІР |
| HSIZE | 1 | І | Вибір розрядності (0 = 16-Bit, 1 = 8-Bit) |
| BMODE | 1 | І | Boot Mode Select (0 = Standard EPROM Booting, 1 = HIP Booting) |
| HMD0 | 1 | І | Bus Strobe Select (0 = RD/WR, 1 = RW/DS) |
| HMD1 | 1 | І | Вибір режиму НІР адреса/дані (0=розділені,1=мультиплексовані) |
| ____ HRD/HRW | 1 | І | Строб читання з НІР або вибір читання/запис |
| ____ ____ HWR/HDS | 1 | І | HIP Write Strobe or Host Data Strobe Select |
| HD15–0 /HAD15-0 | 16 | І/О | НІР дані або НІР дані і адреса |
| HA2/ALE | 1 | І | Host Address 2 Input or Address Latch Enable Input |
| HA1–0/Unused | 2 | І | Адреса хоста 1 або не використовується |

Boot Memory Interface

On the ADSP-2101, ADSP-2103, and ADSP-2111, boot

memory is an external 64K by 8 space, divided into eight

separate 8K by 8 pages. On the ADSP-2105 and ADSP-2115,

boot memory is a 32K by 8 space, divided into eight separate

4K by 8 pages. The 8-bit bytes are automatically packed into

24-bit instruction words by each processor, for loading into onchip

program memory.

Three bits in the processors’ System Control Register select

which page is loaded by the boot memory interface. Another bit

in the System Control Register allows the forcing of a boot

loading sequence under software control. Boot loading from

Page 0 after RESET is initiated automatically if MMAP = 0.

The boot memory interface can generate zero to seven wait

states; it defaults to three wait states after RESET. This allows

the ADSP-21xx to boot from a single low cost EPROM such as

a 27C256. Program memory is booted one byte at a time and

converted to 24-bit program memory words.

The BMS and RD signals are used to select and to strobe the

boot memory interface. Only 8-bit data is read over the data

bus, on pins D8-D15. To accommodate up to eight pages of

boot memory, the two MSBs of the data bus are used in the

boot memory interface as the two MSBs of the boot memory

address: D23, D22, and A13 supply the boot page number.

The ADSP-2100 Family Assembler and Linker allow the

creation of programs and data structures requiring multiple boot

pages during execution.

The BR signal is recognized during the booting sequence. The

bus is granted after loading the current byte is completed. BR

during booting may be used to implement booting under control

of a host processor