CONTENT

1. INTRODUCTION……………………………………………………………. 3

2.INTRODUCTION  TO  PRIMARY FLIGHT CONTROLS OF BOEING

B737CL…………………………………………………………………………. 6

3. ROLL CONTROL…………………………………………………………… 7

4. PITCH CONTROL……………………………………………………………10

5. YAW  CONTROL…………………………………………………………….12

6. FLIGHT CONTROL PANEL………………………………………………...16

7. CONCLUSION………………………………………………………………..23

8. THE LIST OF LITERATURE……………………………………………….. 24

ABBREAVIATION:

FLT-Flight

PCU – power control unit

RSEP – rudder system Entancement Program

- INTRODUCTION

Whenever an airplane changes its flight attitude or position in flight, it rotates about one or more of three axes, which are imaginary lines that pass through the airplane’s center of gravity. The axes of an airplane can be considered as imaginary axles around which the airplane turns, much like the axle around which a wheel rotates. At the point where all three axes intersect, each is at a 90° angle to the other two. The axis, which extends lengthwise through the fuselage from the nose to the tail, is the longitudinal axis. The axis, which extends crosswise from wingtip to wingtip, is the lateral axis. The axis, which passes vertically through the center of gravity, is the vertical axis. (see fig. 1.1)The airplane’s motion about its longitudinal axis resembles the roll of a ship from side to side. In fact, the names used in describing the motion about an airplane’s three axes were originally nautical terms. They have been adapted to aeronautical terminology because of the similarity of motion between an airplane and the seagoing ship. In light of the adoption of nautical terms, the motion about the airplane’s longitudinal axis is called “roll”; motion about its lateral axis is referred to as “pitch.” Finally, an airplane moves about its vertical axis in a motion, which is termed “yaw”—that is, a horizontal (left and right) movement of the airplane’s nose.

The three motions of the airplane (roll, pitch, and yaw) are controlled by three control surfaces. Roll is controlled by the ailerons; pitch is controlled by the elevators; yaw is controlled by the rudder.(see Fig 1.2)

Fig 1.1

Fig  1.2

Ailerons: The two ailerons, one at the outer trailing edge of each wing, are movable surfaces that control movement about the longitudinal axis. The movement is roll. Lowering the aileron on one wing raises the aileron on the other. The wing with the lowered aileron goes up because of its increased lift, and the wing with the raised aileron goes down because of its decreased lift. Thus, the effect of moving either aileron is aided by the simultaneous and opposite movement of the aileron on the other wing.  Rods or cables connect the ailerons to each other and to the control wheel (or stick) (see Fig 1.3)  in the cockpit. When pressure is applied to the right on the control wheel, the left aileron goes down and the right aileron goes up, rolling the airplane to the right. This happens because the down movement of the left aileron increases the wing camber (curvature) and thus increases the angle of attack. The right aileron moves upward and decreases the camber, resulting in a decreased angle of attack. Thus, decreased lift on the right wing and increased lift on the left wing cause a roll and bank to the right.

Elevators: The elevators control the movement of the airplane about its lateral axis. This motion is pitch. The elevators form the rear part of the horizontal tail assembly and are free to swing up and down. They are hinged to a fixed surface--the horizontal stabilizer. Together, the horizontal stabilizer and the elevators form a single airfoil. A change in position of the elevators modifies the camber of the airfoil, which increases or decreases lift. Like the ailerons, the elevators are connected to the control wheel (or stick) by control cables. When forward pressure is applied on the wheel, the elevators move downward. This increases the lift produced by the horizontal tail surfaces. The increased lift forces the tail upward, causing the nose to drop. Conversely, when back pressure is applied on the wheel, the elevators move upward, decreasing the lift produced by the horizontal tail surfaces, or maybe even producing a downward force. The tail is forced downward and the nose up. The elevators control the angle of attack of the wings. When back pressure is applied on the control wheel, the tail lowers and the nose raises, increasing the angle of attack. Conversely, when forward pressure is applied, the tail raises and the nose lowers, decreasing the angle of attack.

Rudder: The rudder controls movement of the airplane about its vertical axis. This motion is yaw. Like the other primary control surfaces, the rudder is a movable surface hinged to a fixed surface which, in this case, is the vertical stabilizer, or fin. Its action is very much like that of the elevators, except that it swings in a different plane--from side to side instead of up and down. Control cables connect the rudder to the rudder pedals(see Fig 1.3).

Fig 1.3

Generally, the primary cockpit  flight controls are arranged as follows:

1.A control yoke (also known as a control column), centre stick or side-stick (the latter two also colloquially known as a control or joystick), governs the aircraft's roll and pitch by moving the ailerons (or activating wing warping on some very early aircraft designs) when turned or deflected left and right, and moves the elevators when moved backwards or forwards

2. Rudder pedals, or the earlier, pre-1919 "rudder bar", to control yaw, which move the rudder; left foot forward will move the rudder left for instance.

3.Throttle controls to control engine speed or thrust for powered aircraft.

2.INTRODUCTION  TO  PRIMARY FLIGHT CONTROLS OF BOEING B737CL

The primary flight control system uses conventional control wheel, column, and pedals linked mechanically to hydraulic power control units which command the primary flight control surfaces : ailerons, elevators and rudder. The flight controls are powered by redundant hydraulic sources: system A and system B. Either hydraulic system can operate all primary flight controls. The ailerons and elevators may be operated manually if required. The rudder may be operated by the standby hydraulic system if system A and system B pressure is not available.

PILOT PRIMARY CONTROLS:

- two control columns

- two control wheels

- two pairs of rudder pedals

- AILERON trim switches

- RUDDER trim control

- Yaw damper switch

3. ROLL CONTROL

Fig 3.1

:

Fig 3.2

4. PITCH CONTROL

Fig  4.1

5. YAW  CONTROL

Fig  5.1

Fig 5.2

6. FLIGHT CONTROL PANEL

Fig 6.1

Fig 6.2

Fig 6.3

Fig 6.4

7. CONCLUSION

The aircraft  is controlled  by primary controls  for  movement in three motions of the airplane (roll, pitch, and yaw). Primary , because of primary need. In case  of  failure of any of elements of this controls leads to loss of controllability, and  high probably  to the aircraft crash.  So it is very important to provide safe and reliable work of controls.

8.THE LIST OF LITERATURE

1.  http://www.smartcockpit.com/pdf/plane/boeing/B737/systems/0018/   :

2. http://en.wikipedia.org/wiki/Aircraft_flight_control_system

3. http://www.free-online-private-pilot-ground-school.com/Flight_controls.html

4. http://www.aviation-history.com/theory/flt_ctl.htm

5.http://www.flightsimbooks.com/flightsimhandbook/CHAPTER_02_07_Primary_Flight_Controls.php